## Slide 1: ACSF-C2 2-actions system
Industry input to ACSF IG
16th meeting
January 2018, Tokyo
Informal Document: ACSF-16-04

## Slide 2: Content
Industry interest
Description of ACSF-C2
Comparison of Concepts
Philosophy of ACSF C2 Why only short range sensor is needed ?
Blind zone detection
Mode confusion issue
Technical Proposal

## Slide 3: Industry interest
  At GRRF-85 of December, the text of ACSF-C (former ACSF-C1) was adopted.
  Industry still have a strong interest for ACSF-C2, e.g. regarding:
  C2 is a more natural HMI, closer to manual lane change: the driver has full control on the timing of the 2 steps of a LC. This permits to increase the maximum time between the LCP and the LCM.
  Automatic deactivation of direction indicator causes unnecessary technical problems that can be corrected with ACSF-C2.
  Current ACSF-C requirements are design restrictive regarding HMI
  HCVs have a particular interest for ACSF-C2
  Industry expectations from ACSF IG is to start the drafting phase to cover C2.

## Slide 4: Description of ACSF C2
Lane Change Procedure
Lane Change Maneuver
1st Deliberate action by the driver
on the direction indicator
< [ X ] secondes
1
2
3
1s
4
2nd Deliberate action by the driver
5
(ACSF B1)
1

## Slide 5: Comparison of concepts
 | Manual driving | ACSF C1 | ACSF C2
1st action | Activation of the direction indicator to inform the other users | Activation of the direction indicator to inform the other users and initiate the lane change procedure | Activation of the direction indicator to inform the other users and initiate the lane change procedure
2nd action | Action on the steering control to change lane | Automatic start of the lane change manoeuver, 3 to 5s after the driver action. | Second deliberate action to initiate the lane change manoeuver.
Given the LCM starts automatically up to 5s (i.e. 180m at 130km/h) after the driver deliberate action…
backward looking sensors have been judged necessary
Given the LCM only starts
after a 2nd deliberate action of the driver, no backward looking sensors are necessary…
there are other ways to ensure same level of safety, see next slides

## Slide 6: Philosophy of ACSF-C2 Safety measures
  ACSF C2 is Level-2 system: the driver is hands-on and drives, the system only assists
  The driver is expected to get quickly used to an HMI which is quite similar to that of the manual driving
  The driver masters the exact time when the vehicle starts moving towards the lane, and consequently when the manoeuver starts, depending the surrounding traffic, similarly to the manual driving
  The lane change assistance does not start automatically, thus “no surprise”
  Unintentional activation is prevented thanks to:
    ON/OFF switch
    2-action activation
  The overriding force remains low (< 50 N)
  Blind zone detection sensors ensure safety regarding the area not covered by the mirrors (and minimize over-reliance risks)  see next slides

## Slide 7: Philosophy of ACSF-C2 Why only short range sensors are needed ?
  From previous slide:
    The driver masters the exact time when the vehicle starts moving towards the lane.
    With two actions HMI, the system requires two decisions from the driver, which are assumed to be based on the monitoring of the rear traffic.
The driver is aware of the vehicle environment thanks to direct Field Of Vision (FOV) and indirect FOV (R46 mirrors):
The system must only monitor the zones out of mirror coverage:
  M1/N1: Class I and III FOV
  M2/M3 : Class II FOV
  N2/N3: Class II, IV and V FOV

## Slide 8: Proposed blind zone detection example of N3 vehicles
UN R46 Class II Field of view
Outside edges
Driver‘s ocular points
4m
1m
1.5m
5m
4.5m
30m
15m
25m
10m
UN R46 Class IV Field of view
3m
3m
0.5m
Leading edge
Rear edge
(truck)
ISO 17387 „shall warn area“
2m
UN R46 Class V Field of view
2.75m
3m
R 2000

## Slide 9: Proposed blind zone detection M1/N1
ISO 17387 „shall warn“ area
Improve safety compared to manual driving
UN R46 Class III Field of view
Calculated at ground level
Ocular points 95%ile
Leading edge
Rear edge
3m
3m
0.5m
Outside edge
20m
1m
4m
4m

## Slide 10: Mode confusion issue
What happens if the driver has wrong perception of the system installed in the vehicle?
OK | B
A | OK
The vehicle is equipped with
C1
C2
C1
C2
The driver believes to have

## Slide 11: Mode confusion issue
Scenario A : The driver believes to be in a C1 while being in a C2 equipped vehicle.
The driver uses the command to initiate the procedure and nothing happens (the system waits for a second action).
   No safety issue
Scenario B : The driver believes to be in a C2 while being in a C1 equipped vehicle.
The driver uses the direction indicator to initiate the procedure and
the system starts a manoeuver only if the situation is deemed not critical.
   No safety issue

## Slide 12: Technical Proposal
“3m x 3m” blind spot detection area (ISO17387 – see sketches) for M1/N1
“3m x 3m” blind spot detection area inspired from ISO17387 – see sketches) for M2M3/N2N3 *
If approaching vehicle detected in blind spot, then
  Warn the driver
  Lane change procedure suppressed automatically.
* For vehicles fitted with class IV mirrors, no Blind Spot sensor is needed since mirrors cover the whole zone

## Slide 13
ANNEX

## Slide 14: Radar vs. US sensors
Ultra-sonic sensor capabilities
Range: 0-5 m
Sensor-to-target relative speed: < 10km/h
Angle of detection: ~ 120°
Target movement: stationary and moving
Target nature: any solid, no distinction
HMI: ON/OFF detection
Sensitivity to wheather conditions: low
Radar sensor capabilities
Range: 55m (motorbikes)
Sensor-to-target relative speed: 0-max speed
Angle of detection: 150°
Target movement: stationary and moving
Target nature: any solid, no distinction
HMI: can transmit distance and speed
Sensitivity to weather conditions: low