## Slide 1: 21st EPPR Informal Working Group Meeting IMMA proposal on definition of OBD2 gtr
10/Jan/2018

## Slide 2
Calibration |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘calibration’ of the powertrain / engine or drive train control unit means the application specific set of data maps and parameters used by the control unit's software to tune the vehicle's powertrain / engine or drive train; | Delete this definition | Term is too general to be defined. No comparable definition in R83. IMMA propose to delete definition to align with R83.
Communication protocol |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘communication protocol’ means a system of digital message formats and rules for exchanging those messages in or between computing systems or units; | Delete this definition | Term is too general to be defined. No comparable definition in R83. IMMA propose to delete definition to align with R83.
Driving cycle |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘driving cycle’ means a test type I cycle consisting of engine start-up, driving mode where a malfunction would be detected if present, and engine shut-off; | A "driving cycle" consists of engine key-on, a driving mode where a malfunction would be detected if present, and engine key-off." | Definition should be modified to allow hybrid vehicle and to align with R83.

## Slide 3
NOVC vehicle |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘NOVC vehicle’ means a not off-vehicle chargeable hybrid electric vehicle; | Delete this definition | No comparable definition in R83. As long as hybrid vehicle is out of scope for this gtr, definition can be deleted.
OVC vehicle |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘OVC vehicle’ means an off-vehicle charging hybrid electric vehicle; | Delete this definition | No comparable definition in R83. As long as hybrid vehicle is out of scope for this gtr, definition can be deleted.
Software |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘software’ of the powertrain / engine or drive train control units means a set of algorithms concerned with the operation of powertrain, engine or drive train data processing systems, containing an ordered sequence of instructions that change the state of the powertrain, engine or drive train control unit; | Delete this definition | Term is too general to be defined. No comparable definition in R83. IMMA propose to delete definition to align with R83. Since software is too generic, use of this term in the main test should be replaced by “software of power train /engine or drive train of control units”.

## Slide 4
Repair information |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘repair information’ means all information required for diagnosis, servicing, inspection, periodic monitoring or repair of the vehicle and which the manufacturers provide for their authorized dealers/repair shops. Where necessary, such information shall include service handbooks, technical manuals, diagnosis information (e.g. minimum and maximum theoretical values for measurements), wiring diagrams, the software calibration identification number applicable to a vehicle type, instructions for individual and special cases, information provided concerning tools and equipment, data record information and two-directional monitoring and test data. | Delete this definition | It is already well described in main text. IMMA proposes to delete definition.

## Slide 5
Calibration verification number |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | Leave this term undefined. | There is definition in GTR No.5, but not defined in OBD1 gtr nor R83. Definition is unnecessary to understand OBD regulation. IMMA propose to leave this term undefined to align with WLTP
Component monitoring |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | Leave this term undefined. | There is definition in GTR No.5, but not defined in OBD1 gtr nor R83. Definition is unnecessary to understand OBD regulation. IMMA propose to leave this term undefined to align with WLTP
Engine system |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | Leave this term undefined. | There is definition in GTR No.5, but not defined in OBD1 gtr nor R83. Definition is unnecessary to understand OBD regulation. IMMA propose to leave this term undefined to align with WLTP

## Slide 6
Decision area |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘decision area’ means the area between the emission [certification] / [approval] limits and the OBD emission thresholds in which the malfunction indicator may be activated at the choice of the manufacturer; | Delete this definition | This concept no longer exist in EURO5. If this concept is no longer used in gtr as well, definition is unnecessary.
Long-term fuel trim / short-term fuel trim |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘long-term fuel trim’ refers to much more gradual adjustments to the fuel calibration schedule which compensate for vehicle differences and gradual changes that occur over time; ‘short-term fuel trim’ refers to dynamic or instantaneous adjustments to the base fuel schedule; | A "Fuel trim" refers to feedback adjustments to the base fuel schedule. Short-term fuel trim refers to dynamic or instantaneous adjustments. Long-term fuel trim refers to much more gradual adjustments to the fuel calibration schedule than short-term trim adjustments. These long-term adjustments compensate for vehicle differences and gradual changes that occur over time. | R83 combines these definitions into single definition. IMMA propose to define these terms in same manner as R83 to align with WLTP.

## Slide 7
Power take-off unit |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘power take-off unit’ means an engine-driven output provision for the purposes of powering ancillary, vehicle‑mounted equipment; | "Power take-off unit" means an engine-driven output provision for the purposes of powering auxiliary, vehicle mounted, equipment. | Word “ancillary” is replaced by “auxiliary” to align with R83. If power take-off unit is decided as not applicable for 2 wheelers, and the use of this term is deleted form the main text, this definition is no longer necessary. It should be finalized at the end of OBD2 discussion.
Secondary air |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘secondary air’ means air introduced into the exhaust system by means of a pump or aspirator valve or other means intended to aid in the oxidation of HC and CO contained in the exhaust gas flow; | "Secondary air" refers to air introduced into the exhaust system by means of a pump or aspirator valve or other means that is intended to aid in the oxidation of HC and CO contained in the exhaust gas stream. | Word “gas flow” is replaced by “gas stream” to align with R83.

## Slide 8
Standardized data |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘standardized data’ means that all data stream information, including all fault codes used, is produced only in accordance with industry standards which, by virtue of the fact that their format and their permitted options are clearly defined, provide for a maximum level of harmonization in the light vehicle industry, and the use of which is expressly permitted in this Regulation; | "Standardized" means that all data stream information, including all fault codes used, shall be produced only in accordance with industry standards which, by virtue of the fact that their format and their permitted options are clearly defined, provide for a maximum level of harmonization in the motor vehicle industry, and whose use is expressly permitted in this Regulation. | Term is modified from “standardized data" to “Standardized" to align with R83.
Unrestricted access to the OBD system |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘unrestricted access to the OBD system’ means: (a) access not dependent on an access code obtainable only from the manufacturer, or a similar device; or (b) access allowing evaluation of the data produced without the need for any unique decoding information, unless that information itself is standardized information; | "Unrestricted" means: (a) Access not dependent on an access code obtainable only from the manufacturer, or a similar device; or (b) Access allowing evaluation of the data produced without the need for any unique decoding information, unless that information itself is standardized. | Term is modified from “unrestricted access to the OBD" to “unrestricted" to align with R83.

## Slide 9
Control system |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | “Control system" means the electronic engine management controller and any component referred to in this UN gtr which supplies an input to or receives an output from this controller. | Cannot align with WLTP since they explicitly limit purpose on indicating emission related failure. Current OBD1 gtr definition is carried over. No need to change term to differentiate since R83 uses “Emission control system”.
Significant reduction of torque |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘significant reduction of propulsion unit torque’ means a propulsion unit torque less than or equal to 90 % of torque in normal operation mode; | Delete this definition | Definition is deleted to reflect discussion in OBD1 gtr.
Type I test |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘type I test’ means the applicable test procedure and driving cycle used for emissions [certification] / [approvals]; | Delete this definition | It is prescribed in gtr No.2. OBD gtr specifies to reference gtr No.2 for the definition. IMMA propose to delete definition since it is not already defined in gtr No.5

## Slide 10
Permanent default mode |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘permanent default mode’ refers to a case where the engine management controller permanently switches to a setting that does not require an input from a failed component or system where such a failed component or system would result in increasing emissions from the vehicle exceeding the OBD emission thresholds [set out in xx.xx] or in which the torque is significantly reduced for safety purposes or component protection; | ‘permanent default mode’ refers to a case where the engine management controller permanently switches to a setting that does not require an input from a failed component or system where such a failed component or system would result in increasing emissions from the vehicle exceeding the OBD thresholds set out in xx.xx or in which resulting Limp-home mode for component protection. | Cannot align with WLTP since two wheeler gtr includes torque monitoring and functional safety in its purpose. Expressions of “torque reduction” and “safety” are replaced by “limp-home” to reflect OBD1 discussion. No need to change term to differentiate since R83 uses “Permanent emission default mode”.

## Slide 11
warm-up cycle |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘warm-up cycle’ means vehicle operation whereby the coolant temperature rises by at least 22 K from engine start-up to at least 343.2 K (70°C); | "Warm-up cycle for category 3 vehicle*" means sufficient vehicle operation such that the coolant temperature rises by at least 22 ºC from engine start-up to at least 70°C If this condition is insufficient to determine the warm up cycle, with the permission of the approval authority, alternative criteria and/or alternative signal(s) or information (e.g. spark plug seat temperature, engine oil temperature, vehicle operation time, accumulative engine revolution, travel distance, etc.) may be adopted. In any case, all signal(s) and information used for determination need to be monitored by the ECU and shall be made available by data stream. *ECE/TRANS/WP.29/1045, as amended by Amends. 1 and 2 (Special Resolution No. 1) | Cannot align with WLTP since two wheeler gtr allows alternative means to judge warm-up cycle. Thus, Term is modified from “warm-up cycle" to “warm-up cycle for category 3 vehicle*" to clearly differentiate from WLTP. Current OBD1 gtr definition is carried over.

## Slide 12
Malfunction |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘malfunction’ means the failure of a component or system that would result in emissions exceeding the OBD emission thresholds set out in point 4 of section B.1., or the triggering of any operating mode which significantly reduces engine torque, or the OBD system being unable to fulfill the basic monitoring requirements; | ‘malfunction for category 3 vehicle*’ means the failure of a component or system that would result in emissions exceeding the OBD thresholds set out in point 4 of section B.1., the circuit failure, the triggering of Limp-home, or the OBD system being unable to fulfill the basic monitoring requirements; *ECE/TRANS/WP.29/1045, as amended by Amends. 1 and 2 (Special Resolution No. 1) | Cannot align with WLTP since two wheeler gtr includes torque monitoring in its purpose. Thus, term is modified from “Malfunction" to “Malfunction for category 3 vehicle*" to clearly differentiate from WLTP. Expression of “torque reduction” is replaced by “limp-home” to reflect OBD1 discussion.
On-Board Diagnostic system (OBD) |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
"On-Board Diagnostic system (OBD)" means an electronic system fitted on-board of a vehicle that has the capability of identifying the likely area of malfunction by means of fault codes stored in a computer memory which can be accessed by means of a generic scan tool; | "On-Board Diagnostic system for category 3 vehicle* (OBD for category 3 vehicle*)" means an electronic system fitted on-board of a vehicle that has the capability of identifying the likely area of malfunction by means of fault codes stored in a computer memory which can be accessed by means of a generic scan tool; *ECE/TRANS/WP.29/1045, as amended by Amends. 1 and 2 (Special Resolution No. 1) | Cannot align with WLTP since they explicitly limit purpose on detecting emission related failure. Thus, term is modified from “OBD" to “OBD for category 3 vehicle*" to clearly differentiate from WLTP. Current OBD1 gtr definition is carried over.

## Slide 13
Vehicle type |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | "Vehicle type" means a category of power-driven vehicles which do not differ in such essential engine and OBD system characteristics. | Definition of R83 is adopted to align with WLTP.
Malfunction indicator |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘malfunction indicator’ (‘MI’) means a visible or audible indicator that clearly informs the driver of the vehicle in the event of malfunctions; | "Malfunction Indicator for category 3 vehicle (MI for category 3 vehicle*)" means a visible indicator that clearly informs the driver of the vehicle in the event of malfunctions. *ECE/TRANS/WP.29/1045, as amended by Amends. 1 and 2 (Special Resolution No. 1) | Audible indicator insufficient for two wheelers. Cannot align with WLTP since they explicitly limit purpose on indicating emission related failure. Thus, term is modified from “OBD" to “OBD for category 3 vehicle*" to clearly differentiate from WLTP. Current OBD1 gtr definition is carried over.

## Slide 14
Access to OBD |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘access to OBD’ means the availability of all emission and safety critical related on-board diagnostic information including all fault codes required for the inspection, diagnosis, servicing or repair of environmental or functional‑safety‑related parts of the vehicle, via the serial interface for the standard diagnostic connection, pursuant to point 3.12 of Annex B.1.1. | "Access" means the availability of all emission-related OBD data including all fault codes required for the inspection, diagnosis, servicing or repair of emissions-related parts of the vehicle, via the serial interface for the standard diagnostic connection (pursuant to [paragraph 3.12. of Annex 1]). | Functional safety is removed from definition to reflect OBD1 gtr discussion and to align with R83. Term is modified from "Access to OBD" to "Access" to align with R83. WLTP decided not to change this definition as to reflect wireless connection feature.
Calculated load value |  | 
Original definition | IMMA proposal | Comment / justification
‘calculated load value’ means referring to an indication of the current airflow divided by peak airflow, where peak airflow is corrected for altitude, if available. This definition provides a dimensionless number that is not engine‑specific and provides the service technician with an indication of the proportion of engine capacity being used (with wide open throttle as 100%); | Delete this definition | WLTP decided to delete this definition since this term is only used in description of freeze frame data and is unnecessary to understand OBD regulation. Definition is also deleted from two wheeler gtr definition to align with WLTP.

## Slide 15
Limp-home |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | "Limp-home" means an operation mode triggered by the control system that restricts fuel quantity, intake air quantity, spark delivery or other powertrain control variables resulting in significant reduction of output torque or engine revolution or vehicle speed; | Not defined in R83, but WLTP decided to define this term in their new gtr. However, they decided to fix main text first and then comeback to the definition afterward. IMMA propose to adopt OBD1 gtr definition for now, and consider for alignment when it is fixed by WLTP.
Pending DTC |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | “Pending DTC (Pending fault code)” is a diagnostic trouble code stored upon the initial detection of a malfunction prior to illumination of the malfunction indicator. | Not defined in R83, but WLTP decided to define this term in their new gtr. IMMA propose to adopt definition created by WLTP to align.

## Slide 16
Readiness |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | Readiness" means a status indicating whether a monitor or a group of monitors have run since the last erasing. Readiness is also indicated when status is erased by power loss. | Not defined in R83, but WLTP decided to define this term in their new gtr. IMMA propose to adopt definition created by WLTP to align with WLTP.
Confirmed DTC |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | ”Confirmed DTC (Confirmed fault code)” is a diagnostic trouble code stored when an OBD system has confirmed that a malfunction exists. | Not defined in R83, but WLTP decided to define this term in their new gtr. IMMA propose to adopt definition created by WLTP to align with WLTP.

## Slide 17
Scan-tool |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | “Scan tool" means an external test equipment used for standardized off-board communication with the OBD system in accordance with the requirements of this GTR. | Not defined in R83, but WLTP decided to define this term in their new gtr. WLTP also decided to change term from “scan-tool” to “scan tool”. IMMA propose to change term and to adopt definition created by WLTP to align.
Software calibration identification |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | "Software calibration identification (CAL ID)" means a series of alphanumeric characters that identifies the emission-related calibration and/or software version. | Not defined in R83, but WLTP decided to define this term in their new gtr. IMMA propose to adopt definition created by WLTP to align with WLTP.

## Slide 18
Useful life |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | "Useful life" means the relevant period of distance and/or time over which compliance with the OBD system has to be assured. | Since this term is general term which is also used in outside of OBD, WLTP OBD TF decided to request WLTP IWG to define definition in gtr15. IMMA propose to adopt OBD1 gtr definition for now, and consider for alignment when it is fixed in gtr15.
Deficiency |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘deficiency’ in respect of vehicle OBD systems, means a situation in which up to two separate components or systems that are monitored contain temporary or permanent operating characteristics that impair their otherwise efficient OBD monitoring or do not meet all other detailed requirements for OBD; | “Deficiency" means, in respect of vehicle OBD systems, that components or systems that are monitored contain temporary or permanent operating characteristics that impair the otherwise efficient OBD monitoring of those components or systems or do not meet all of the other detailed requirements for OBD. | WLTP decided to change this definition. Requirement is removed from definition since it should be described in the main text. IMMA propose to adopt definition created by WLTP to align with WLTP.

## Slide 19
Engine misfire |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘engine misfire’ means a lack of combustion in the cylinder of a combustion engine due to the absence of spark, poor fuel metering, poor compression or any other cause; | “Engine misfire" means lack of combustion in the cylinder of a positive ignition engine due to absence of spark, poor fuel metering, poor compression or any other cause. | R83 and OBD1 gtr had different definition. Requirement should be described in main text. WLTP agreed to remove requirement from their definition as IMMA proposed.
OBD emission threshold |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
‘OBD emission thresholds’ means limits of the pollutant emission constituents above which the malfunction indicator shall be activated; | Delete this definition | WLTP decided to call this term OBD threshold and to delete definition since it is self explanatory. IMMA propose to change term from “OBD emission threshold” to “OBD threshold” and to delete this definition to align with WLTP.

## Slide 20
Diagnostic trouble code |  | 
Original definition (EPPR-8-14e) | IMMA proposal | Comment / justification
Not defined in original draft. | “Diagnostic trouble code” or “fault code” is a numeric or alphanumeric identifier for a fault condition identified by the On Board Diagnostic system. | Not defined in R83, but WLTP decided to define this term in their new gtr. IMMA propose to adopt definition created by WLTP to align with WLTP.