|  | United Nations | ECE/TRANS/WP.29/GRRF/2013/?? |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 december 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

Working Party on Brakes and Running Gear (GRRF)

Seventy-fifth session

Geneva,  September 2013

Item ? of the provisional agenda

Coupling devices – Regulation No. 55

Proposal for an Amendment to Regulation No. 55 
(Uniform provisions concerning the approval of mechanical coupling components of combinations of vehicles)

Submitted by the expert from GRRF ECE R55 informal group

The text reproduced below was prepared by the expert from ECE R55 informal group in order to introduce amendments regarding

Requirements on movable ball couplings

Increased range of application of remote controls to couplings similar to C50-X and G50-X

Couplings

Possible increase of characteristic values of standard 	couplings

Addition of further requirements to the mounting of couplings.

The modifications to the current text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

Paragraph 5.1.9., amend to read:

"5.1.9.		In cases where two separate service brake systems are installed, the systems may share a common brake, if a failure in one system occurs does not affect the performance of the other, such a failure does not preclude the other system from meeting the single brake system performance requirements."

Annex 5, insert new item

“1.4. 	Movable ball coupling devices

A movable coupling device shall be designed for positive mechanical engagements in service position.”

Renumber annex 5 old item 1.4. to 1.5 until 1.7. to 1.8

Annex 5 item 12.1, 	amend to read

12.1            Devices for remote indication and remote control are permitted only on automatic drawbar couplings and automatic fifth wheel couplings coupling devices of Classes C50-X and G50-X.

Headline TABLE 3, amend to read

“Minimum characteristic values for standard flange type ball couplings”

Headline TABLE 5, amend to read

“Minimum characteristic values for standard drawbar couplings”

Headline TABLE 7, amend to read

“Minimum characteristic values for standard drawbar eyes”

Headline TABLE 9, amend to read

“Minimum characteristic values for Class L toroidal drawbar eyes”

Headline TABLE 13, amend to read

“Minimum characteristic values for Class K hook type couplings

Regulation chapter 6:  add new items 6.4., 6.5., 6.6., 6.7. “

  - The vehicle manufacturer shall state which types and classes of coupling devices may be fitted to the vehicle type giving the values of D, V (1), S or U (if applicable) which are based on the construction of the vehicle type in combination with the type(s) of the coupling device(s) intended to be used. The characteristics D, V, S or U of the coupling devices approved in accordance with this Directive shall be equal or greater than the characteristics given for the combination concerned.

  - The coupling device shall be attached to the vehicle type according to the installation instructions, given by the vehicle manufacturer in agreement with the coupling manufacturer and the Technical Service. The vehicle manufacturer shall state the appropriate attachment points for the coupling device on the vehicle type and, if necessary, mounting brackets, mounting plates, etc. to be fitted on the specific vehicle type.

  - Only automatic coupling devices which allow an automatic coupling procedure on motor vehicles shall be employed for the coupling of trailers having a maximum mass of more than 3,5 tonnes.

  - When mounting coupling devices of Classes B, D, E, H and L on trailers, a value of 32 tonnes for the maximum mass T of the towing vehicle must be taken into account for D-value calculation. If the D-value of the coupling device is not sufficient for T = 32 tonnes, the resulting restriction on the mass T of the towing vehicle or the mass of the vehicle combination must be stated in the vehicle type-approval certificate of the trailer.

II.	Justification

- Today an increasing number of coupling types (especially ball-couplings, which

are movable, retractable, bendable and else are developed due to esthetic

requirements). The minimum requirement to this kind of ball coupling devices shall be

stated. This is in order to avoid accidents, when a trailer is coupled.

- If every partner of a coupling combination fulfills minimum requirement a

safe combination is given. Any device being tested against higher characteristic

values does still comply with every requirement of the standard device, but with a

higher security for the whole coupled combination.

indication of general value 32t is missing (indeed the whole chapter is missing!)

- Remote indications may help the driver to assure safe coupling procedures.

It is much more safety and innovative to use couplings with remote control and remote indication, in particular if remote indication is integrated in the dashboard.

n the today`s version the safety feature of remote control and remote indication is only permitted to C50-X, so that C50-1until C50-7 and also G50-X, but also class S automatic pin couplings with a 40 mm bolt and the very common automatic 5th

- Annex 7 of the regulation had been copied from 94/20/EC. It was cancelled the 1 paragraph of this annex

“General requirements…” of the 94/20/EC, because there was just a paragraph in the regulation R55.

In this paragraph is refered to detailed requirements in annex 6 and 7, but now this detailed requirements are cancelled. This detailed requirements are needed for the approval of vehicles with regard to the fitting as well as for a basic of D-value calculation. The new items are exactly copied from 94/20/EC annex 7 chapter 1.