## Slide 1: Drawbar a separate technical unit
There are no clear technical definition over a drawbar being a separate technical unit.
The standard ISO7641 show some examples that are classified
  More through a gut feeling than a solid guidance
Alternative approaches have been proposed
  Function based definition
  Mechanical properties definition
  Rigid drawbars of dollies shall be classified as integrated part of the chassis.

## Slide 2: Drawbar a separate technical unit
  Function based definition
  Chassis functions
    Transfer cargo weight to the ground
  Drawbar functions
    Transfer tractive/braking forces between towing and towed vehicle
    Balance pitching movements of center axle trailer or dolly
  When a drawbar delivers the drawbar functions and part of the Chassis functions then it is an integrate part of the chassis.
    When a substantial part (e.g. >5% of the trailer total weight is carried as support load in the coupling then the drawbar is an integrated part of the chassis.

## Slide 3: Drawbar a separate technical unit
Mechanical properties based definition
  If the natural frequency of the rigid drawbar is much different from the natural frequency of the chassis (unloaded and without axles) that drawbar is a separate technical unit.
    E.g. if 1/3 < fdrawbar/fchassis < 3 then the drawbar is an integrated part of the chassis.
  The natural frequency may be calculated with FEM, measured through some impact hammer and accelerometer or estimated from static deflections test.
    The rigid drawbar shall be considered as a cantilever fully fixed at the chassis end.
    The chassis without axles shall be considered as beam simply supported
  If frequencies are not evaluated satisfactorily the drawbar is classified as a separate technical unit.

## Slide 4: Drawbar a separate technical unit
Pros and Cons
  Function based definition
    It is very simple
    It makes sense to look at what task is carried out by the drawbar.
    This will make many rigid drawbar as designed today a separate technical unit.
    It will possibly start a trend to develop center axle trailers with a support load high enough for the drawbar to be classified as integrated part of the chassis.

## Slide 5: Drawbar a separate technical unit
Pros and Cons (cont.)
  Mechanical properties based definition
    It is not as simple but it could be made reasonably simple
    From a mechanics perspective the drawbar and the chassis will dynamically behave as separate units if the natural frequencies as far separated.
    It puts some demand on the competency of the trailer manufacturer in order to satisfactorily evaluate the natural frequency.
    When the drawbar is a continuation of the side members of the chassis the drawbar is considered to start at the forward end of the loading area. Apart from that there are no issue whether the drawbar is riveted, bolted or welded to the chassis.
    This definition will most likely confirm the drawbar classifications used for center axle trailers running today. I.e. it will not generate any unnatural design trends.

## Slide 6: Drawbar a separate technical unit
Recommendation
  Based on the above discussion the recommendation is to elaborate a Mechanical properties based definition.