## Slide 1
Approval Marking Layout Examples
SLR-23-06/Rev.1

## Slide 2
Approval Marking Layout Examples of Single Device
It is assumed that LSD will be UN Reg. No.168, RID will be UN Reg. No.169 and RRD will be UN Reg. No.170
E4
168R00-1111
RL
Daytime Running Lamp
LSD
00 Series
Approval No
E4
169R01-2222
F3
Front Fog Lamp
RID
01 Series
Approval No
E4
170R02
IA
3333
Approval No
Retro-Reflective Device
RRD
02 Series
The approval number may be separated from the other markings.
Example 1
Example 2
Example 3

## Slide 3
Approval Marking Layout Examples of Combined Devices
in Same Regulation
E4
168R00-1111
R1
S1
2a
Rear Position Lamp
Stop Lamp
Rear Direction
Indicator Lamp
LSD
00 Series
Approval No
E4
168R00-1111
R1
S1
2a
E4
168R00
1111
R1
S1
2a
The approval number may be separated from the other markings.
Example 1
Example 2
Example 3

## Slide 4
Approval Marking Layout Examples of Combined Devices
in Different Regulations
E4
168R00
1b
RL
HC
A
169R01
1111
E4
168R00-1111
1b
RL
HC
A
169R01-1111
E4
168R00-1111
1b
RL
HC
A
169R01-1111
Passing-beam Headlamp
Front Position
Lamp
Front
Direction
Indicator
Lamp
Daytime Running Lamp
RID
01 Series
Approval No
LSD
00 Series
As only one approval number applies it is only necessary to show it once in the marking
Example 1
Example 2
Example 3

## Slide 5
Alternative Approval Marking Layout Examples of Combined Devices in Different Regulations
E
4
3333
IA
00
2b
00
R2
00
F2
00
AR
00
S2
00
Marking according to Reg. 3, 6, 7 etc.

## Slide 6
Alternative Approval Marking Layout Examples of Combined Devices in Different Regulations
E
4
3333
IA
00
2b
00
R2
00
F2
00
AR
00
S2
00
E
4
168R00
IA
2b
R2
F2
AR
S2
170R00
3333
Marking according to Reg. 3, 6, 7 etc.
Marking according to Reg. LSD and RRD

## Slide 7
Alternative Approval Marking Layout Examples of Combined Devices in Different Regulations
E
4
3333
IA
00
2b
00
R2
00
F2
00
AR
00
S2
00
E
4
[168]R00
IA
2b
R2
F2
AR
S2
[170]R00
3333
Marking according to Reg. 3, 6, 7 etc.
Marking according to Reg. LSD and RRD