## Slide 1
Collision point
da (dummy)
db (truck)
dc (LPI)
dlateral
New Test Case | Orig. Test Case | rturn | vvehicle [km/h] | vBicycle [km/h] | dlateral [m] | da [m] | db [m] | dc [m] | dbicycle [m] | lcorridor [m] | dcorridor [m] | dcorridor,outer [m] | Include cone to account for initial swerving?
1 | 1 | 5 | 10 | 20 | 1.5 | 44.4 | 15.8 | 4.3 | < 55 | > 70 | vehicle width + 1m | 5 | Yes
2 | 4 | 10 | 10 | 20 |  |  | 22 | 4.4 |  |  |  | 2 | Yes
3 | 7 | 25 | 20 | 20 |  |  | 38.3 | 10.7 |  |  |  | 1 | No
4 | 6 | 25 | 20 | 10 | 4.5 | 22.2 | 43.5 | 10 |  |  |  | 1 | No
5 | 5 | 5 | 10 | 10 |  |  | 19.8 | 2.4 |  |  |  | 6 | Yes
6 | 2 | 10 | 10 | 20 |  | 44.4 | 14.7 | 3.4 |  |  |  | 3 | Yes
7 | 3 |  |  |  |  |  | 17.7 |  |  |  |  | 2 | Yes
8 | 1* | 5 | 10 | 20 | 1.5 | 44.4 | 15.8 | 4.3 |  |  |  | 1 | No
9 | 4* | 10 | 10 | 20 |  |  | 22 | 4.4 |  |  |  |  | No
10 | 5* | 5 | 10 | 10 | 4.5 | 22.2 | 19.8 | 2.4 |  |  |  |  | No
11 | 2* | 10 | 10 | 20 |  | 44.4 | 14.7 | 3.4 |  |  |  |  | No
12 | 3* | 10 | 10 | 20 |  |  | 17.7 |  |  |  |  |  | No
dc possibly to be re-defined based on TTC* for the particular vehicle speed if the vehicle would have made a turn. Use turning radius that fits to the particular vehicle speed (e.g. assume fixed lateral acceleration)
* TTC based on 1,4s reaction time and 5 m/s2 brake performance
= not necessary anymore in this new proposal
= may not be useful because dummy is visible for driver at LPI (~ 5 m) ahead of truck) – as an alternative change cyclist speed to 15 km/h for this test case (In general in case truck speed is high and dummy speed is low)
New proposal for BSIS testing without turning (for discussion)
February 2018
Line C
Line B
Line A
dcorridor