## Slide 1: WLTP-22-04e Revision 1
1
Heinz Steven
15.04.2018
Status report of the cycle and gearshift issues task force (GSTF)
Supplements and modifications compared to the previous version are highlighted in light blue, proposals from the previous version are highlighted in yellow

## Slide 2: Overview
2
GSTF web-telco at 27.03.2018
Amendment proposals for annex 2 to be adopted by the IWG:
  Paragraph 2 (editorial modifications),
  Para 3.3 (modifications for clutch operation and eng. speed),
  Paragraph 4 (a) (supplement for more reasonable results),
  Paragraph 4 (b) as discussed and adopted at 27.03.2018, improved text in addition,
  Improved examples in paragraph 4 (b) as discussed at 27.03.2018 amended with this revision,
  Paragraph 4 (c) as proposed in appendix 1 of the minutes from the GSTF web-telco at 27.03.2018.
Timeplan of a new round robin test as discussed and adopted in the GSTF web-telco at 27.03.2018

## Slide 3: GSTF web-telco at 27.03.2018
3
The remaining issue in paragraph 4 (b) was discussed on the basis of the TF leaders proposal which was distributed to the TF prior to the meeting.
The outcome of the discussion led to the amendment proposal for paragraph 4 (b) as presented in detail in the following slides.
The TF leader informed the TF about bilateral discussions with an OEM that led to further amendment proposals (see appendix 1 of the minutes).
Another agenda point was related to the side conditions and a time schedule for a new RRT for calculation tools which will also be shown in more detail in the following slides.

## Slide 4: Editorial modifications in paragraph 2
4
The term ng is specified in paragraph 2 (d). In the following sub-paragraphs ngmax is used several times instead of ng. This should be corrected.
E.g. paragraph 2 (e) should read:
(n/v)i, the ratio obtained by dividing the engine speed n by the vehicle speed v for each gear i, i to ngmax i from 1 to ng, min-1/(km/h). (n/v)i shall be calculated according to the equations in paragraph 8 of Annex 7;
Further corrections ngmax -> ng are necessary in paragraph 2 (g) and 2 (i)
Paragraph 2 (i) contains the figures A2/1a and A2/1b, illustrating the determination of ngvmax. But in the headers ngmax is used instead of ngvmax.

## Slide 5: Amendment proposal for para 3.3
5
Paragraph 3.3 deals with the selection of possible gears with respect to engine speed.
In the term
If aj ≤ 0 and ni,j ≤ nidle, ni,j shall be set to nidle and the clutch shall be disengaged.
aj ≤ 0 should be replaced by aj < 0 because at constant speed (aj = 0) some power might be required which is not possible with a disengaged clutch.

## Slide 6: Amendment proposal for para 3.3
6
The term
If aj > 0 and ni,j ≤ (1.15 × nidle), ni,j shall be set to (1.15 × nidle) and the clutch shall be disengaged.
Should be replaced by the following text
If aj ≥ 0 and ni,j < max(1.15 × nidle ; min. engine speed of the Pwot(n) curve), ni,j shall be set to the maximum of 1.15 × nidle or (n/v)i × vj and the clutch shall be set to “undefined”.
“undefined” covers any status of the clutch between disengaged and engaged, depending on the individual engine and transmission design. In this case the real engine speed may deviate from the calculated engine speed.

## Slide 7: Amendment proposal for para 3.3
7
Justification:
The modifications proposed here result from the fact, that the minimum engine speed of the power curve was changed from nidle to nmin_drive_set.
They are necessary because no power check can be performed in this engine speed range.

## Slide 8: Amendment proposal for para 4 (a)
8
The second part of paragraph 4(a) requires that gears used during accelerations at vehicle speeds ≥ 1 km/h shall be used for a period of at least 2 seconds (e.g. a gear sequence 1, 2, 3, 3, 3, 3, 3 shall be replaced by 1, 1, 2, 2, 3, 3, 3).
At the last IWG meeting the following text was added in order to avoid misinterpretation:
This requirement shall not be applied to downshifts during an acceleration phase. Such downshifts shall be corrected according to paragraph 4 (b) of this annex.

## Slide 9: Amendment proposal for para 4 (a)
9
The initial gear use for vehicle 15 of the RRT example vehicles between second 801 and 807 (acceleration phase) is
4,4,3,4,5,5,5
An OEM argued that the 3rd gear is a downshift, but the following 4th gear is used only for one second, so that the first 5th gear should be changed to 4th gear according to 4 (a) and then the 3rd gear should be changed to 4th gear according to 4 (b).
Formally this is ok, but replacing the downshift first leads to a more reasonable result, because the change of the first 5th gear to 4th gear would become superfluous.

## Slide 10: Amendment proposal for para 4 (a)
10
Therefore the following amendment of the text is proposed by the TF leader:
This requirement shall not be applied to downshifts during an acceleration phase or if the use of a gear for just one second follows immediately after such downshift. In these cases the downshifts shall be corrected first according to paragraph 4 (b) of this annex.
Example:
Gear sequence 4,4,3,4,5,5,5, where the first second determines the start of an acceleration phase shall be replaced by:
4,4,4,4,5,5,5

## Slide 11: Amendment proposal for para 4 (a)
11
In addition to that the following editorial amendment is proposed: Replace
Gears used during accelerations at vehicle speeds ≥ 1 km/h shall be used for a period of at least 2 seconds (e.g. a gear sequence 1, 2, 3, 3, 3, 3, 3 shall be replaced by 1, 1, 2, 2, 3, 3, 3). by:
Gears used during accelerations at vehicle speeds ≥ 1 km/h shall be used for a period of at least 2 seconds.
Examples:
Gear sequence 1, 2, 3, 3, 3, 3, 3 shall be replaced by:
1, 1, 2, 2, 3, 3, 3.
Gear sequence 1,2,3,4,5,5,6,6,6,6,6 shall be replaced by: 1,1,2,2,3,3,4,4,5,5,6

## Slide 12: Amendment proposal for para 4 (b)
12
At the GSTF web-telco at 27.03.2018 one TF member required that the text and the examples in paragraph 4 (b) are not clear enough and would require further explanations.
The TF leader promised to take this on board for further consideration. He had some discussions related to this issue with TF members in KW 14.
These resulted in the following proposals for improved text in paragraph 4 (b).

## Slide 13: Amendment proposal for para 4 (b)
13
It is proposed to add the text in light blue, because it is needed in further descriptions (see next slides).
If a downshift is required during an acceleration phase the gear which is required during this downshift shall be noted (iDS). The starting point of a correction procedure is defined by either the last previous second when iDS was identified or by the start point of the acceleration phase if all time samples before have gears > iDS. The highest gear of the time samples before the downshift determines the reference gear iref for the downshift. A downshift where iDS = iref – 1 is called a one step downshift, a downshift where iDS = iref – 2 is called a two step downshift. The following check shall then be applied.

## Slide 14: Amendment proposal for para 4 (b)
14
The following amendment is proposed because the old text results from a misunderstanding between the TF leader and a TF member. It does not change the results at all.
Working backwards from the end of the acceleration phase forewards from the starting point of the correction procedure to the end of the acceleration phase, the latest occurrence of a 10 second window containing iDS for either 2 or more consecutive seconds, or 2 or more individual seconds shall be identified. The last usage of iDS in this window defines the end point of the correction procedure. Between the start and end of the correction period, all requirements for gears greater than iDS shall be corrected to a requirement of iDS.

## Slide 15: Amendment proposal for para 4 (b)
15
It is proposed to add the following text because it is necessary for clarity reasons.
If one step downshifts as well as two step downshifts occur during an acceleration phase, the two step downshifts shall be corrected before the correction of the one step downshifts. In this case the starting point of the correction procedure for the one step downshifts is the second immediately following the end of the correction period for the two step downshifts. If a two step downshift occurs after a one step downshift, it overrules the one step downshift in the time period before the two step downshift.

## Slide 16: Amendment proposal for para 4 (b)
16
It is proposed to add the following text in the next sub-paragraph:
From the end of the correction period (in case of 10 second windows containing iDS for either 2 or more consecutive seconds, or 2 or more individual seconds) or from the starting point of the correction procedure (in case all 10 second windows contain iDS only for one second or some 10 second windows contain iDS not at all) to the end of the acceleration phase, if the downshift was a one step downshift, all downshifts with a duration of only one second shall be removed. If the downshift was a two step downshift, all requirements for gears greater than or equal to iDS up to the latest occurrence of iDS shall be corrected to (iDS + 1).

## Slide 17: Amendment proposal for para 4 (b)
17
With this amendment the following text can be deleted:
This final correction shall also be applied from the start point to the end of the acceleration phase, if no 10 second window containing iDS for either 2 or more consecutive seconds or 2 or more individual seconds was identified.
It is further proposed to replace the examples (i) to (iii) in paragraph 4(b) by tables A2/2 to A2/6

## Slide 18: Amendment proposal for para 4 (b)
18
(i) If the initially calculated gear use is: 2, 2, 3, [3, 4, 4, 4, 4, 3, 4, 4, 4, 4], 4, 4, 3, 4, 4, 4, the gear use shall be corrected to: 2, 2, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 4, 4, 4.
(ii) If the initially calculated gear use is: 2, 2, 3, [3, 4, 4, 3, 4, 4, 4, 4, 4, 4], 4, 4, 4, 4, 3, 4, the gear use shall be corrected to: 2, 2, 3, 3, 3, 3, 3, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4, 4.
(iii) If the initially calculated gear use is: 2, 2, 3, [3, 4, 4, 4, 4, 4, 4, 4, 4, 4], 4, 4, 4, 3, 3, 4, the gear use shall be corrected to: 2, 2, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 3, 4.
The first 10 second windows are indicated by square brackets in the examples above.
The underlined gears (e.g. 3) indicate those cases which could lead to a correction of the gear before it.

## Slide 19: Table A2/2
19

## Slide 20: Table A2/3
20

## Slide 21: Table A2/4
21

## Slide 22: Table A2/5
22

## Slide 23: Table A2/6
23

## Slide 24: Amendment proposal for para 4 (b)
24
With the amendment proposals adopted at the last IWG meeting for paragraph 4 (b) a downshift by more than one gear could occur at the transition from a deceleration or constant speed phase to an acceleration phase.
Example:
The gear sequence 6,6,6,5,5,4,4,4 where the first 5th gear determines the beginning of an acceleration phase would be changed to 6,6,6,4,4,4,4,4 according to paragraph 4 (b).
The TF leader proposed to replace the last 6th gear by gear 0 in such cases (6,6,0,4,4,4,4,4) in order to get similar results as for downshifts during deceleration phases.

## Slide 25: Amendment proposal for para 4 (b)
25
This proposal was discussed in the web-telco at 27.03.2018 and was adopted by the TF.
Therefore it is proposed to add the following text at the end of paragraph 4 (b):
After the application of 4 (b) a downshift by more than one gear could occur at the transition from a deceleration or constant speed phase to the acceleration phase.
In this case the gear for the last sample of the deceleration or constant speed phase shall be replaced by gear 0 and the clutch shall be disengaged. If the “suppress gear 0 during downshifts” option according to paragraph 4 (f) is chosen, the following lower gear shall be used instead of gear 0.

## Slide 26: Amendment proposal for para 4 (c)
26
The initial gear use for RRT example vehicle 8 between seconds 1141 and 1151 is 3,3,4,4,5,5,4,3,3,2,2.
According to 4 (c) 4,5,5,4 would be changed to 4,4,4,4 in the first modification round with the result 3,3,4,4,4,4,4,3,3,2,2.
Since the speed trace between seconds 1146 and 1150 (4,4,3,3,2) belongs to a deceleration phase the gear sequence would be changed to 4,4,0,2,2 according to 4 (f) with the final result 3,3,4,4,4,4,4,0,2,2,2.
If the 2nd gear highlighted in green would be 3rd gear, 4 (f) would not be applied and the gear sequence 3,3,4,4,4,4,4,3,3,3,2 would be changed according to 4 (c) to 3,3,3,3,3,3,3,3,3,3,2 in the second modification round.

## Slide 27: Amendment proposal for para 4 (c)
27
If 4 (c) would be applied twice in each round, the result would be: the initial gear sequence 3,3,4,4,5,5,4,3,3,2,2 would be corrected to 3,3,3,3,3,3,3,3,3,2,2, which is more reasonable than 3,3,4,4,4,4,4,0,2,2,2.
Therefore, it is proposed to add the following text at the beginning of paragraph 4 (c):
The modification check described in this sub-paragraph shall be applied to the complete cycle trace twice ahead of the application of the following sub-paragraphs.
Final remark of the TF leader: Most probably the open issues of the GSTF can be closed with these amendments and therefore it would be desirable, if they could also be included in the EU-WLTP 2nd act.

## Slide 28: New round robin test for calculation tools
28
Some TF members requested the TF leader in an earlier meeting that he should ask the IWG for a mandate to repeat the round robin test (RRT) of different gearshift calculation tools based on the latest version of GTR 15. At IWG #21 this mandate was given by the IWG.
Consequently, a tentative time schedule for the RRT was included in agenda point 3 of the TF web-telco.
And it was proposed to base the RRT on the latest version of GTR 15 including the amendments adopted at IWG #22 and to use the same example vehicles as in the first RRT.

## Slide 29: New round robin test for calculation tools
29
The proposal was accepted by the TF.
The participation of interested parties should be indicated to the TF leader by end of April 2018.
Tentative time schedule:
  Start of the RRT mid of May 2018,
  Delivery of the results (time series of the gear use for the 30 example vehicles) till end of June 2018,
  Analysis of the results and report till mid of August 2018,
  Presentation of the results at IWG # 24 September 2018.

## Slide 30: New round robin test for calculation tools
30
The TF asked the TF leader to put the input data of the example vehicles and the latest version of the ACCESS tool on the IWG website for easier access and expressed the wish to bring the ACCESS tool in a condition that it could be used as reference.
Meanwhile the WLTP IWG website at UNECE contains a subdirectory “Gearshift calculation tool” which is currently empty.
The latest tool and the example vehicle data will be uploaded, once the IWG has given the mandate.

## Slide 31: GTR #15 with the amendments proposed in this report
31
The amendments proposed in this report are included in annex 2 of the latest GTR 15 and are highlighted in yellow and light blue (revision 1). This GTR version can be accessed via the following link:

## Slide 32: End
32
Thank you for your attention!