## Slide 1: Confirmation on application to EVs unique cycle
WLTP-IWG
17-20 APR 2018
Japan
WLTP-22-05e

## Slide 2: Question from SG-EV
Question:
Should evaluation of the drive trace index be done (in the context of the Charge-Depleting-Test of an OVC-HEV) cycle by cycle or on the complete Charge-Depleting test?
Suggestion:
Calculate each cycle
Calculate each cycle
Calculate DTIs respectively
Calculate DTIs in each cycle
each DTI should meet the criteria
Cycle | IWR | RMSSE | ER/DR/EER/ASCR
1 | x.xx | x.xx | ...
2 | x.xx | x.xx | ....
... | ... | ... | ...
n+1 | x.xx | x.xx | ...
#n
#n+1
#n-1
#n-2
Cycle

## Slide 3: Unexpected situation
Example:
- Cycle #1~#4: Normal driving
- Cycle #5~#6: Smooth driving
In the case of the driver takes an intentional smooth driving partly, the DTIs derived from the whole test cycle may meet the criteria. Therefore it would be better to calculate the DTIs cycle by cycle.
Criteria (JP) 0.80 -2.0~+4.0

## Slide 4: Appendix-1) Relationship between indexes and EC of PEVs
EER
Source: WLTP-18-06e
ER
DR
EER
ASCR
RMSSE
IWR
possible criteria: < +0.8
(AVE DS1 & DS2)
(AVE DS1 & DS2)
(AVE DS1 & DS2)
(AVE DS1 & DS2)
(AVE DS1 & DS2)
(AVE DS1 & DS2)
0.8
EC: -1~+2 => IWR: -2.5 ~ +5.0

## Slide 5: Drive trace indexes for the electrified vehicles <discussion paper>
WLTP/SG-EV
29 AUG 2017
Japan
Appendix-2

## Slide 6: Discussion points
Drive trace indexes for ICEVs
Drive trace indexes for PEVs
  Consecutive cycle test
  Shortened test
Drive trace indexes for OVC-HEVs
  Charge depleting (CD) test
  Charge sustaining (CS) test
Drive trace indexes for the range extender type vehicles
Need to clarify how to calculate the drive trace indexes for the electrified vehicles

## Slide 7: 1. Drive trace indexes for the ICE vehicles
① Calculation portion
Calculate DTIs for LMH(3-phase) and LMHxH(4-phase)
② In the case that the accelerator control is fully activated
LMHxH(4-phase)
LMH(3-phase)
[Annex 7, 7.1.] The prescribed speed (value) shall be used instead of the actual vehicle speed(value) for drive trace index calculations.

## Slide 8: 2.1. Drive trace indexes for PEV consecutive cycle test
③ Calculation portion for consecutive cycle test
Calculate DTIs in each cycle
3-phase and 4-phase respectively
④ Calculation portion at the cycle reached break-off
Calculate until the break-off point. The rule of Annex 7-7.1. will be applied until this point.
Cycle | IWR | RMSSE | ER/DR/EER/ASCR
1 | x.xx | x.xx | ...
2 | x.xx | x.xx | ....
3 | x.xx | x.xx | ...
Cycle-#1
Cycle-#2
Cycle-#3
Calculation object
(Until break-off)
Continued

## Slide 9: 2.1. Drive trace indexes for PEV consecutive cycle test
⑤ Deviation of 2~3 seconds
It is possible to deviate for 2~3 seconds when a remaining battery level is low.
Do NOT accept intentional smooth driving. However if the accelerator control is fully activated, the deviation of 2~3 s may be allowed. Then this portion will be applied the rule described in the paragraph 7.1. of Annex 7.
<Necessity condition>
Follow the Annex 8, Appendix 6
-Selected appropriate driver-selectable mode
-Selected appropriate driving cycle
-Applied appropriate cycle modification
possible to deviate 2~3 sec

## Slide 10: 2.2. Drive trace indexes for PEV shortened test
Shortened test procedure
Drive trace index for DS1
Drive trace index for DS2
Reference
Use these values
2
⑥ Calculation portion for shortened test
For the shortened test, the drive trace index should be calculated during the two dynamic segments(DS1 and DS2) respectively.
It is not necessary to calculate during the constant speed segments (CSSM and CSSE) because the driving style in CSS doesn't influence the test results.
Drive trace index for DS1
Continued

## Slide 11: 2.2. Drive trace indexes for PEV shortened test
⑦ Number of deviations
Dynamic segment (LMHxHLM)
=> 2822 sec.
The duration of the dynamic segment is 2822 sec . It is longer than that of WLTC 4 phase.
Speed tolerance:
4 phase 1800 s => 10 times deviation are allowed = 1/180 s
=> 3 phase 1477 s => 8 times
=> Dynamic segment 2822 s => 16 times

## Slide 12: 3.1. Drive trace index for OVC-HEV CD tests
Calculate each cycle
Calculate each cycle
Calculate DTIs respectively
⑧ Calculation portion
Calculate DTIs in each cycle
Cycle | IWR | RMSSE | ER/DR/EER/ASCR
1 | x.xx | x.xx | ...
2 | x.xx | x.xx | ....
... | ... | ... | ...
n+1 | x.xx | x.xx | ...
⑨ Speed trace tolerances
Follow the paragraph 2.6.8.3 of Annex 6 (There shall be no more than 10 deviations within 1 sec. per each cycle.)

## Slide 13: 3.2. Drive trace index for OVC-HEV CS tests
⑩ Calculation portion
Calculate DTIs for LMH(3-phase) or LMHxH(4-phase)
LMHxH(4-phase)
LMH(3-phase)

## Slide 14: 4. Drive trace index for the range extender type vehicles
Item | Power (kW)
Electric motor | 125
Engine (Generator) | 28
Example
⑪ Range extender type vehicles
Drivability may be different between CS test and CD test ??
=> Apply the rule described in the paragraph 7.1. of Annex 7
<Necessity condition>
Follow the Annex 8, Appendix 6
-Selected appropriate driver-selectable mode
-Selected appropriate driving cycle
-Applied appropriate cycle modification
Need to discuss on the applicable test cycle (Classification / Cycle modification) for such vehicles. (?)

## Slide 15: 5. Others
⑫ the accelerator control
How to check/ensure the accelerator control is fully activated?
=> CAN data or Appropriate sensor (Potentiometer, Rotary encoder, etc)
=> Accelerator position > 95%?

## Slide 16: Discussion points on the DTIs for the electrified vehicles
# | Items | Concerns | Solutions
1 | ICEVs | Which part should be calculated the DTIs? | Calculate DTIs for LMH(3-phase) and LMHxH(4-phase) respectively
2 | ICEVs | In the case that the accelerator control is fully activated, How to deal with such portion? | (Annex 7, 7.1.) The prescribed speed (value) shall be used instead of the actual vehicle speed(value) for drive trace index calculations
3 | PEVs | When the consecutive cycle test procedure is used, which part should be calculated the DTIs? | Calculate DTIs in each cycle
4 | PEVs | When the consecutive cycle test procedure is used, how to calculate the DTIs of the cycle that the break-off criterion is reached. | Calculate until the break-off point. The rule of Annex 7-7.1. will be applied until this point.
5 | PEVs | It is possible to deviate for 2~3 seconds when a remaining battery level is low. - Break-off：4 sec or more - Speed tolerance: less than 1 sec on any one occasion | Do NOT accept intentional smooth driving. However if the accelerator control is fully activated, the deviation of 2~3 s may be allowed. Then this portion will be applied the rule described in the paragraph 7.1. of Annex 7. <Necessity condition> Follow the Annex 8, Appendix 6 -Selected appropriate driver-selectable mode -Selected appropriate driving cycle -Applied appropriate cycle modification
6 | PEVs | When the shortened test is used, which part should be calculated the DTIs? | Calculate DTI only Dynamic segments.
Continued

## Slide 17: Discussion points on the DTIs for the electrified vehicles
# | Items | Concerns | Solutions
7 | PEVs | The duration of the dynamic segment is 2822 sec . It is longer than that of WLTC 4 phase. The deviation times should be increased. | 4 phase 1800 s=> 10 times deviation are allowed => once per 180 s =>3 phase 1477 s => 8 times =>Dynamic segment 2822 s => 16 times
8 | OVC-HEVs (CD test) | Which part should be calculated the DTI? | Calculate DTIs in each cycle
9 | OVC-HEVs (CD test) | Speed trace tolerances | Follow the paragraph 2.6.8.3 of Annex 6 (There shall be no more than 10 deviations within 1 sec. per each cycle.)
10 | OVC-HEVs (CS test) | Which part should be calculated the DTI? | Calculate DTIs for LMH(3-phase) or LMHxH(4-phase) respectively
11 | Range extender type | Driveability may be different between CS tests and CD tests. | Apply the rule described in the paragraph 7.1. of Annex 7. <Necessity condition> Follow the Annex 8, Appendix 6 -Selected appropriate driver-selectable mode -Selected appropriate driving cycle -Applied appropriate cycle modification => Need to discuss on the applicable test cycle (Classification / Cycle modification) for such vehicles.
12 | Accelerator control | How to check/ensure the accelerator control is fully activated? | CAN data or Appropriate sensor (Potentiometer, Rotary encoder, etc)

## Slide 18: (Ref.) Associated sentence
Annex 6, 2.6.4.4. Accelerations
The vehicle shall be operated with the appropriate accelerator control movement necessary to accurately follow the speed trace. The vehicle shall be operated smoothly, following representative shift speeds and procedures. For manual transmissions, the accelerator controller shall be released during each shift and the shift shall be accomplished in minimum time. If the vehicle cannot follow the speed trace, it shall be operated at maximum available power until the vehicle speed reaches the respective target speed again.
Annex 6, 2.6.8.3. Speed trace tolerances
Vehicles that cannot attain the acceleration and maximum speed values required in the applicable WLTC shall be operated with the accelerator control fully activated until they once again reach the required speed trace. Speed trace violations under these circumstances shall not void a test. Deviations from the driving cycle shall be recorded.
The tolerances shall not be shown to the driver:
(a) Upper limit: 2.0 km/h higher than the highest point of the trace within ±1.0 second of the given point in time;
(b) Lower limit: 2.0 km/h lower than the lowest point of the trace within ±1.0 second of the given time.
Speed tolerances greater than those prescribed shall be accepted provided the tolerances are never exceeded for more than 1 second on any one occasion.
There shall be no more than ten such deviations per test cycle.
Annex 8, 3.1.1.2.
If the vehicle cannot follow the applicable test cycle within the speed trace tolerances according to paragraph 2.6.8.3. of Annex 6, the accelerator control shall, unless stated otherwise, be fully activated until the required speed trace is reached again.
Annex 8, 3.4.4.1.1. Speed trace and breaks(Consecutive cycle Type 1 test procedure)
The test shall be performed by driving consecutive applicable test cycles until the break-off criterion according to paragraph 3.4.4.1.3. of this annex is reached.
Breaks for the driver and/or operator are permitted only between test cycles and with a maximum total break time of 10 minutes. During the break, the powertrain shall be switched off.
Annex 8, 3.4.4.1.3. Break-off criterion(Consecutive cycle Type 1 test procedure)
The break-off criterion is reached when the vehicle exceeds the prescribed speed trace tolerance as specified in paragraph 2.6.8.3. of Annex 6 for 4 consecutive seconds or more. The accelerator control shall be deactivated. The vehicle shall be braked to standstill within 60 seconds.
Annex 8, 3.4.4.2.1. Speed trace(Shortened Type 1 test procedure)
The shortened Type 1 test procedure consists of two dynamic segments (DS_1 and DS_2) combined with two constant speed segments (CSS_M and CSS_E) as shown in Figure A8/2.
The dynamic segments DS_1 and DS_2 are used to calculate the energy consumption of the phase considered, the applicable WLTP city cycle and the applicable WLTP test cycle.
The constant speed segments CSS_M and CSS_E are intended to reduce test duration by depleting the REESS more rapidly than the consecutive cycle Type 1 test procedure.
Annex 8, 3.4.4.2.3. Break-off criterion(Shortened Type 1 test procedure)
The break-off criterion is reached when the vehicle exceeds the prescribed driving tolerance as specified in paragraph 2.6.8.3. of Annex 6 for 4 consecutive seconds or more in the second constant speed segment CSS_E. The accelerator control shall be deactivated. The vehicle shall be braked to a standstill within 60 seconds.
Annex 8, 4.4.2. Pure electric range for PEVs
The ranges determined in this paragraph shall only be calculated if the vehicle was able to follow the applicable WLTP test cycle within the speed trace tolerances according to paragraph 2.6.8.3. of Annex 6 during the entire considered period.
Annex 8 - Appendix 6 , 1.1.
The manufacturer shall select the driver-selectable mode for the Type 1 test procedure according to paragraphs 2. to 4. inclusive of this appendix which enables the vehicle to follow the considered test cycle within the speed trace tolerances according to paragraph 2.6.8.3. of Annex 6. This shall apply to all vehicle systems with driver-selectable modes including those not solely specific to the transmission.
Annex 7. 7. Drive trace indices
7.1. General requirement
The prescribed speed between time points in Tables A1/1 to A1/12 shall be determined by a linear interpolation method at a frequency of 10 Hz.
In the case that the accelerator control is fully activated, the prescribed speed shall be used instead of the actual vehicle speed for drive trace index calculations during such periods of operation.
7.2. Calculation of drive trace indices
The following indices shall be calculated according to SAE J2951(Revised JAN2014):
(a) ER : Energy Rating
(b) DR : Distance Rating
(c) EER : Energy Economy Rating
(d) ASCR : Absolute Speed Change Rating
(e) IWR : Inertial Work Rating
(f) RMSSE : Root Mean Squared Speed Error

## Slide 19: (Ref.) Applicable test procedure
The applicable test procedure is selected according to the estimated PER and the vehicle classification(max speed)

## Slide 20: (Ref.) Selection of driver-selectable modes for CD test

## Slide 21: (Ref.) Selection of driver-selectable modes for CS test

## Slide 22: (Ref.) Selection of driver-selectable modes for PEVs