## Slide 1
BMW | 12.04.2018
Proposal for a mid vehicle concept
for pure ICE vehicles

## Slide 2: Proposal for a mid vehicle concept. Introduction.
History:
Currently the limit of an Interpolation Family in terms of CO2 is 30g/km or 20% whatever is smaller. During the development of WLTP, it was checked and proven, that a range of 30g/km and even up to 40g/km is linear and allows for proper interpolation.
Due to the lack of knowledge of vehicles under a WLTP regime, no one from industry claimed for a higher range than 30g/km, and so 30g/km have been decided as a criteria.
During the first approvals, it was identified, that there is a significant amount of families in the area of 30..40 g/km CO2, which need to be separated into two families. So obviously the first educated guesses on the max range of IP families were too small.
This leads to enormous burden and intransparency in the approval process.
Using the concept for EVs as a basis, a proposal is developed also for pure ICEs, using a mid-vehicle to check linearity and extend the maximum range of the interpolation.
In the case, that the family is still linear, vehicles should be grouped into one type and family.
The proposal was already received positively at several meetings in the last year.
Due to the significant implication, more time is needed for all stakeholders to check the proposal.
The New Issues TF in Paris in March 2018 decided that this proposal should be presented and discussed in the IWG in Ispra.

## Slide 3: Proposal for a mid vehicle concept. Current Problems, including European specific issues.
Without improving the concept, apart from the additional burden, there is also a lack of clarity and transparency.
In the light of the planned transparency database with the clear demand of finding vehicles belonging to the same family, that becomes very difficult, if in fact one vehicle may belong to two different families and the OEM may chose at the point of production, to which family the vehicle should belong.
Proposal to clarify extrapolation and introduce Mid-vehicle.
Correlation
Correlation
Correlation
Correlation
WLTP perspective:
Correlation / CO2-fleet perspective:
Solution / Proposal:
One vehicle could be in two families.
One vehicle is in one family.
Even more confusion in context with correlation.
Eventually the line is split (Mid-vehicle-concept).

## Slide 4: Proposal for a mid vehicle concept. Explanation of the Proposal.
test of mid vehicle
High
Low
up to 40 g/km
Mid vehicle for ICEs
Proposal: If a mid vehicle is tested and fulfils the criteria (see hybrids), the max. range can be extended by 10 g/km CO2.
Justification / Background: Limiting the range is important, as linearity is necessary for interpolation. To avoid splitting a family (with all its complex consequences) for a few grams, it should be possible to have a bigger family, while linearity has to be demonstrated.

If Mid vehicle is tested and check is OK:
Range can be increased by 10g/km.
Effectively then 30g/km or 20% plus 10g/km, whatever is smaller.

## Slide 5: Proposal for a mid vehicle concept. Details. This proposal is new compared to what was proposed in Paris-meeting.
Basically a vehicle between H and L is selected and tested. In the case linearity is proven, vehicles are directly interpolated between H and L; otherwise, the interpolation is divided into two sub-sections.
As this concept already exists for electrified vehicles, no changes are needed for documentation or approval, as the mid-vehicle is already prepared an available in the documentation.
The rule for finding the mid-vehicle is specified more precisely compared to EVs. That includes a clear reference to the step in the postprocessing as well as basing the tolerance on the distance between M and H/L. Otherwise the mid-vehicle could be even outside of the range of H and L, which makes no sense.
High
Low
up to 40 g/km
Differences compared to the already existing mid-vehicle concept for electrified vehicles:
1.: Tolerance for mid-vehicle
2.: clear reference for comparison (step 3 after RCB correction)
example for vehicle M
average between L and H
lower segment
upper segment
none of the segments is longer than "normal" tolerance of 20% / 30g/km.

## Slide 6: Proposal for a mid vehicle concept. TExt Proposal. ~~ Any Feedback is welcomed! ~~
2.3.2.x. At the request of the manufacturer the allowed interpolation range can be increased by 10 g/km CO2 if a vehicle M is tested in that family and the conditions are met, see paragraph 2.3.2.y. of this Annex.
2.3.2.y. Vehicle M
Vehicle M is a vehicle within the interpolation family between the vehicles L and H. It is recommended to select vehicle M such, that the cycle energy demand is approximately the arithmetic average of vehicles L and H. The limits of the selection of vehicle M are such, that neither the upper nor the lower segment between the vehicles M and L/H is bigger than the allowed CO2 range according to paragraph 2.3.2.2. of this Annex. The defined road load coefficients and the defined test mass shall be recorded.
The linearity of CO2 mass emission for vehicle M shall be verified against the linear interpolated CO2 mass emission between vehicle L and H over the applicable cycle. For that verification, the CO2 values at the stage resulting from step 3 (including RCB correction), defined in Table 7/1 of Annex 7, shall be used for both, the result from the tested vehicle M and the interpolated CO2 mass emissions.
The linearity criterion for vehicle M shall be considered fulfilled, if the measured CO2 mass emission of the vehicle M over the applicable WLTC minus the CO2 mass emission derived by interpolation is less than 3 g/km or 3% of the interpolated value, whichever value is smaller. In the case where the interpolated CO2 mass emission is below 33 g/km, the 3% criterion shall be replaced by 1 g/km.
If the linearity criterion is fulfilled, individual vehicles are interpolated between vehicles L and H.
If the linearity criterion is not fulfilled, the interpolation family shall be split into two sub-families for vehicles with a cycle energy demand between vehicles L and M, and vehicles with a cycle energy demand between vehicles M and H.
Allow for additional 10 g/km
Find the "Mid-vehicle".
Check linearity.
Criteria is 3%, limited between 1 g/km and 3 g/km.
Conclusion and decision.
Define clear reference.

## Slide 7: Proposal for a mid vehicle concept. Conclusion.
Proposal already positively received at several meetings in the last year.
Using the mid-vehicle reduces the effective interpolation range to approx. 20 g/km. In other words: The interpolation line, which is based on measurements, is not extended. There is never a case, where two vehicles are more than 30 g/km apart without a test result. Therefore the initial decisions in WLTP Phase 1 are not changed.
This concept is already in place for hybrids.
Allowing bigger families will increase transparency of membership of vehicles to their families. Otherwise one vehicle may belong to two different families, on choice by the OEM.
This will reduce administrative and testing burden. This additional burden we are facing today is without any benefit for environment or precision of the results.
This proposal should be assessed on a technical basis. The initial decision on 30g/km limit was not a political one, but based on the knowledge at that time. We now have more knowledge and should make use of that experience.
test of mid vehicle
High
Low
up to 40 g/km

Request to IWG:
1) Provide feedback until Geneva-meeting such, that
2) adoption could be possible at Tokyo-meeting 2018.

## Slide 8
Thank you!

## Slide 9: Proposal for a mid vehicle concept. Old proposal on tolerance for mid-vehicle.
Basically a vehicle between H and L is selected and tested. In the case linearity is proven, vehicles are directly interpolated between H and L; otherwise, the interpolation is divided into two sub-sections.
As this concept already exists for electrified vehicles, no changes are needed for documentation or approval, as the mid-vehicle is already prepared an available in the documentation.
The rule for finding the mid-vehicle is specified more precisely compared to EVs. That includes a clear reference to the step in the postprocessing as well as basing the 10%-tolerance on the delta of the distance between H and L. Otherwise the mid-vehicle could be even outside of the range of H and L, which makes no sense.
position of mid vehicle, with 10% tolerance compared to exact average between H and L
10% referring to the delta between H and L.
Comparison based on step 3 of postprocessing (incl. RCB, but no other corrections).
High
Low
up to 40 g/km
Those are the only differences compared to the mid-vehicle concept for electrified vehicles, which is already existing the GTR.