## Slide 1
Page 1
IMMA proposal for amendments to informal document GRE 79-12-rev.1 (79th GRE, 24-27 April 2018,agenda item 4)
In order to clarify the application of Change Index and to avoid any misunderstanding,
IMMA proposes to add the sentence in blue to slide 7 of GRE-79-12-rev.1; see next slide at the bottom.
If SLR IWG agreed, IMMA recommends to add a similar text in the regulations LSD, RID & RRD
SLR-25-06

## Slide 2
GRE Informal Working Group „Simplification of Regulation“
Grouped approval marking – multiple lamp (function) type approval
Page 2
Example of a group of lamps (functions)
type approved according to the LSD and RID Regulation
E4
[LSD]R03
1b
RL
HCR
A
[RID]R05
1111
Halogen passing beam and driving beam
Headlamp
Front Position Lamp
Front Direction
Indicator Lamp
Daytime Running Lamp
Approval No
The DRL, Front Position Lamp and Front Direction Indicator Lamp are type approved according to the 03 series (for example) of amendments to the LSD Regulation
The Halogen Passing Beam and Driving Beam Headlamp is type approved according to the 05 series (for example) of amendments to the RID Regulation
The change index is NOT part of the approval marking
This page has been amended
The approval marking always shows the latest series of amendments of the Regulation applicable to the type approval of the specific lamp (function). This may not be the last series of amendment for LSD or RID, since last series of amendment may include another device that is not affecting the change index of the devices covered by the example above (i.e. last series of amendment is for a change in front fog lamp only that is not a part of or affects the above example).