## Slide 1: Description of Japan RDE methodology
Environmental Policy Division,
Road Transport Bureau,
Ministry of Land, Infrastructure, Transport and Tourism,
Japan

## Slide 2
Outline of Japan’s RDE

## Slide 3: Outline of RDE in Japan
Schedule of Introduction for RDE in Japan
New Type Approval Vehicle : October 2022
Continuous Production Vehicle : October 2024
Scope
Diesel vehicles having a gross weight of 3.5t or less
Diesel powered passenger cars having a capacity of 9 or less people
Method and Requirement
[will be described later]

## Slide 4: Concept of Japan’s RDE method
RDE method shall be able to detect whether result of chassis-dynamometer test reflects on real driving correctly or not.
The Japan’s RDE method is based on EC’s , but it is slightly modified considering different real world driving conditions and different phase of WLTC between Japan and Europe.
Therefore, we modified these factors in align with driving conditions in Japan.

## Slide 5: WLTP phases
Japan are using 3 phases in WLTP.
The average speed and max speed are greatly different between 3 phases and 4 phases.
Based on these differences, Japan modified some factors slightly.
 | 3 phases | 4 phases
Average Speed | 36.6 km/h | 46.5 km/h
Ratio of Idling Time | 15.4 % | 13.0 %
Max Speed | 97.4 km/h | 131.3 km/h
Max Acceleration | 5.7 km/h/s | 5.7 km/h/s
RPA | 0.167 | 0.152
Driving Time | 1477 s | 1800 s
Total Mileage | 15.01 km | 23.27 km
Main differences between WLTC 3 phases and 4 phases

## Slide 6: Traffic Conditions
Traffic rate of Japan and World-Wide
Low
39%
Middle
43%
High
13%
EX-High
5%
Low
14%
Middle
20%
High
32%
EX-High
34%
The traffic speed in Japan’s real driving tends to be slow compared with World-Wide.
Especially, the ratio of driving speed at 60km/h or less (“Low” + “Middle”) is very high.
Since the speed limit of Japan’s motorway is less than 100km/h in most sections, the proportion of “EX-High” is low.
The speed thresholds are 60km/h, 80km/h, 110km/h.

## Slide 7: Weather Conditions
Yellow area is about 1% (low temperature and high temperature, respectively)
Average traffic volume for every air temperature （2012-2016）
Japan is somewhat hotter than Europe.
98% of the traffic in Japan is between -2 to 34℃, calculating from traffic frequency distribution weighted by traffic volume, time and temperature, excluding upper and lower 1%.
In summer, the temperature near the vehicle increase about 4℃.
Increased temperature on the road
Air temperature
Temperature near the vehicle

## Slide 8
Detail of Japan’s RDE method

## Slide 9: Structure of J-RDE method
1. Scope
2. Definitions and Abbreviations
3. General Requirements
4. Special Requirements
5. Test Conditions
6. Running Requirement
7. Driving requirement
8. Lubricating Oil, Fuel and Reagent
9. Emission Amount of Exhaust Emission and Evaluation of Running
Appendix 1 Test Procedure for Exhaust Emission with PEMS
Appendix 2 Specification and Calibration of PEMS and Signals
Appendix 3 Validation of PEMS a Non-Traceable Exhaust Mass Flow Rate
Appendix 4 Determination of Emissions
Appendix 5 Verification of Trip Dynamic Conditions by Moving Average Window
Appendix 6 Verification of Overall Trip Dynamic State
Appendix 7 Procedure to Determine Cumulative Positive Elevation Gain of Trip
Appendix 8 Verification of Trip Conditions of OVC-HEV and Calculation of Final On-Road Emissions
Japan’s RDE is basically the same structure and method as EC’s RDE.
Japan’s RDE method

## Slide 10
 | J-RDE |  |  | E-RDE |  | 
Vehicle speed and Consist | Routes | Speed [km/h] | Consist [%] | Routes | Speed [km/h] | Consist [%]
 | Urban/Rural | V≦60 | 40-65 | Urban | V<60 | 29-44
 |  |  |  | Rural | 60<V<90 | 23-43
 | Motorway | 60<V | 35-55 | Motorway | 90<V | 23-43
Window speed characteristics | V<50:urban/rural speed 50≦V:motorway speed |  |  | V<45：urban speed 45≦V<80:rural speed 80≦V<145:motorway speed |  | 
CO2 characteristic curve reference points | P1 : Same as E-RDE P2 : Same as E-RDE P3 : ー |  |  | P1:vp1=18.882km/h (Average Speed of the Low Speed phase of the WLTP cycle) P2:vp2=56.664km/h (Average Speed of the High Speed phase of the WLTP cycle) P3:vp3=91.997km/h (Average Speed of the Extra High Speed phase of the WLTP cycle) |  | 
Based on difference of WLTP phases, Japan modified some of factors slightly as below.
Different respects between J – E WLTP phases

## Slide 11: Different respects between J – E WLTP phases
NG
 | J-RDE | E-RDE
RPA |  | 
v・apos_[95] |  | 
NG
NG
RPA
0 20 40 60 80 100 120
km/h
0.2
0.1
0
NG
RPA
0 20 40 60 80 100 120
km/h
0.2
0.1
0
Vapos_[95]
0 20 40 60 80 100 120
km/h
30
20
10
0
Vapos_[95]
0 20 40 60 80 100 120
km/h
30
20
10
0

## Slide 12
 | J-RDE | E-RDE
Order | 1.Urban/Rural 2.Motorway | 1.Urban 2.Rural 3.Motorway
Ambient conditions Altitude | 0~1000m( 700m) (Moderate altitude) | 0 ~1300m( 700m) (Moderate altitude)
temp | -2℃(0)~38℃(35) （Moderate temp） | -7 ℃(0)~ 35℃(30) (Moderate temp)
Average speed (urban driving part) | ー | 15 ~ 40 km/h
Max speed | ー | 145km/h
Motorway speed | ー | Cover range : 90 ~ at least 110 km/h Velocity : Above 100 km/h for at least 5 minutes.
Test track | Available | ー
Based on difference of real driving condition, Japan modified some of factors slightly as below.
Different respects between J – E WLTP phases

## Slide 13
 | J-RDE | E-RDE
Measurement items | NOx, CO2 Note: Japan doesn’t regulate PN under the chassis-dynamometer test and on road test. | NOx, PN, CO2
Fuel | Basically same as E-RDE(If it exceed criteria, the reference fuel defined in Annex 3 of GTR15 may be used for second RDE test. ). | The fuel, lubricant and reagent (if applicable) used for RDE testing shall be within the specifications issued by the manufacturer for vehicle operation by the customer.
If a part of the test is performed outside of ambient conditions | It is basically the test may be invalid. However, it can be made valid if the CF value conforms to limit. | The test shall be invalid.
Based on difference of regulation and concept, Japan modified some of factors slightly as below.
Different respects between J – E WLTP phases

## Slide 14
Thank you for your attention!

## Slide 15
Reference
Notes: Next content is ‘Investigation for On-Road Test’.

## Slide 16
Consideration of CO2 Characteristic Curve
WLTC Low
WLTC High