## Slide 1: Simplification stage II
RRD – Kick-off presentation for
GTB session July 2018 in Frankfurt
SLR-26-05

## Slide 2: RRD SLR from Stage II
Reg 3
Reg 27
Reg 69
Reg 70
Reg 104
RRD
Stage I
Retroreflectors
Advance Warning Triangle
Slow Moving Vehicle Plate
Rear marking Plate
for long and heavy vehicles
Conspicuity Marking
for long and heavy vehicles
IA
IB
IIIA
IIIB
IVA
Type 1
Type 2
Class 1
Class 2
Class 1
Class 2
Class 3
Class 4
Class 5
Class C
Class D
Class E
Class F
RRD
Stage II
Simplification:
system of classes
independent from
technology
performance based
harmonized test-methodes
All existing Regs to merge to one single document
Extraction
Analyse

## Slide 3: Main topics to be worked on in future
Requirements for CIL for retroreflective devices – classes
Requirements for R´ (RA) for retroreflective devices/markings – classes
Colorimetric requirements – daytime and nighttime visibility enhanced visibility
Photometric measurement conditions – to define independent from device
Water-penetration test and corrosion test independend from the device
Weathering test (colour fasness) to adapt to state of the art testing
Mechanical requirements to define testing independend from device
Chemical and environmental requirements - testing independend from device
Specific requirements and testing, which is depending from the device

## Slide 4: Retroreflective devices - RRD

## Slide 5
Source | Function | Application | Additional function | Design type | Class
R 3 | Rear-Reflector | for motor vehicles | independent |  | IA
 |  | for trailers |  |  | IIIA
 |  | for motor vehicles | with signal light |  | IB
 |  | for trailers |  |  | IIIB
 |  | for trailers |  |  | IVA
R 104 | Conspicuity Marking | contour or stripe |  |  | C
 |  | for distinctive marking graphics | for extended area |  | D
 |  |  | for background printing |  | E
 |  | for extremity marking |  |  | F
R 70 | Retroreflective Marking for Trucks and Trailers |  |  | retroreflective and fluorescent | 1
 |  |  |  |  | 2
 |  |  |  | retroreflective | 3
 |  |  |  |  | 4
 |  | For extremity marking |  |  | 5
R 69 | Slow Moving Vehicle Marking |  |  | retroreflective and fluorescent | 1
 |  |  |  | retroreflective | 2
R 27 | Advance Warning Triangle |  |  | retroreflective and fluorescent | Type 1
 |  |  |  | fluorescent retroreflective | Type 2
Structure by function and device

## Slide 6: Specific technical requirements – Structure for chapter 5
Photometric Characteristics (essential initial) | Test conditions | Requirements | Applicable for class
Retroreflection |  |  | 
Coefficient of luminous intensity (CIL) |  |  | 
Specific coefficient of retroreflection (RA) |  |  | 
Colour |  |  | 
Colour of reflected light (night-time colour) |  |  | 
Colour of retroreflective device (day-time colour) |  |  | 
Colour of fluorescent materials |  |  | 
Special specification (tests) / resistance to external agents |  |  | 

## Slide 7: Special specification – (tests) resistance to external agents - Structure of Annex
Resistance to weathering / colour fastness |  | Stability of photometric properties | 
Resistance to corrosion |  |  | 
Resistance to fuels and oils |  |  | 
Resistance to heat (and low temperature) |  | Bonding strength | 
Resistance to cleaning |  | flexing | 
Resistance to penetration of water |  | Test of clearance to ground | 
 |  | Mechanical solidity test | 
 |  | Test of stability against wind | 

## Slide 8: New structure
Specification |  | 
Shape and dimensions of retro-reflective devices | Annex 5 | 
 | Sketches and design recommendations | 
 | Defiend dimensions and tolerances | 
Photomtric measurements | Annex 4 | 
 | Photogoniometer definition | 
Test procedure for day time colours | Currently chapter 4 | 
 | to move to Annex |