## Slide 1
Action item 18/24 : Industry will reflect the harmonized High Speed test proposal in the GTR text.
- The provision for the 60 minutes test duration for Q and below will be put in square brackets, because US requested from the industry to have the rationale for the test time reduction (90 minutes to 60 minutes) (Deadline: August 2018).
- Industry will also consider China proposal when drafting the regulation.
Informal Working Group Tyre GTR
Session 20, Brussels Nov 2nd-3th
Document TYREGTR-20-09
Agenda item 4.1 AI IWG18/24

## Slide 2
Initial Assessment of LT/C HS Test Severity
Previous industry recommendations acknowledged by CPs:
  Tyres with SS ≥ S: Existing ECE Reg 54 HS test
    Final test speeds are based on the speed symbol of the tyre
    20°C to 30°C ambient temperature
Current industry recommendations for consideration by CPs:
  Tyres with SS = R: test to 170 km/h (106 mph) at 38°C ambient temperature*
  All tyres with SS ≤ Q: test to 160 km/h (99 mph) at 38°C ambient temperature*
* proposed 36.5 °C ± 1.5°C (TBC)

## Slide 3
3.16: Load/speed endurance test for LT/C tyres (from R54)
  3.16.1 Requirements
  3.16.2 Preparing the tyre
  3.16.3 Test procedures Speed Symbol ≥Q:
  3.16.4 Load/speed test programme for tyre with speed symbol Q and above All others:
  3.16.4.7 Endurance test programme
3.17 Endurance test for LT/C tyres (from FMVSS 139)
3.18 Low inflation pressure performance test for LT/C tyres (from FMVSS 139)
3.19 High speed performance test for LT/C tyres (from FMVSS 139)
To be put in relation with the Endurance test for LT/C tyres 3.17/3.18 (FMVSS 139) The two endurance programs remain
not harmonised
HIGH SPEED
ENDURANCE
Proposal: Clearly separate the ‘high speed’ tests from the ‘endurance’ ones

## Slide 4
Proposed structure:
3.16 High Speed performance for LT/C tyres with speed symbol ≥ Q (Harmonized)
3.17 High Speed performance for LT/C tyres with speed symbol <Q (from FMVSS 139, non harmonized) 3.18 Endurance test for LT/C tyres (from FMVSS 139, non harmonized)
3.19 Low inflation pressure performance test for LT/C tyres (from FMVSS 139, non harmonized)
3.20 Endurance test for LT/C tyres with Speed symbol < Q (from R54, non harmonized)

## Slide 5
3.16: Harmonized High Speed performance for LT/C tyres with speed symbol ≥ ‘Q’
  Keep 3.16.1 Requirements
  Remove 3.16.1.1.Each type of LT/C tyre shall undergo at least one load/speed endurance test carried out by the procedure described below.
  Keep 3.16.2 Preparing the tyre
  3.16.3 Test procedures Remove 3.16.3.3 In the case of tyres with a speed symbol Q and above, test procedures are as specified in paragraph 3.16.4.
  Remove 3.16.3.3.1 For all other tyre types, the endurance test programme is shown in paragraph 3.16.4.7.
  Remove 3.16.4. Load/speed test programme for tyre with speed symbol Q and above
  3.16.3.1. Mount the tyre-and-wheel assembly on the test axle and press it against the outer face of a smooth power-driven test drum 1.70 m ± 1 per cent or 2.00m ± 1 per cent in diameter having a surface at least as wide as the tyre tread.
  Keep 3.16.3.2, 3.16.3.4,
  3.16.3.5 During the test the temperature in the test-room shall be maintained at between 20 °C and 30 °C or at a higher temperature if the manufacturer so agrees. in the temperature range as specified in the following table:
  Keep 3.16.3.6
  Move to 3.16.1 “Requirements” and renumber 3.16.4.1. This programme applies to: 3.16.4.1.1. All tyres marked with load index in single 121 or less. 3.16.4.1.2. Tyres marked with load index in single 122 and above and with the additional marking "C", or "LT", referred to in paragraph 3.3.14. of this regulation.
  Keep 3.16.4.2 to 3.16.4.6
Speed Symbol | Temperature t (°C )
Q, R | 35.0 ± 3.0
S, T, H | 25.0 ± 5.0(*)
(*) or higher if the tire manufacturer agrees | 

## Slide 6
3.17: High Speed performance for LT/C tyres with speed symbol <Q Keep and renumber 3.19. 1 to 3.19.3.8 (High speed performance test for LT/C tyres)

## Slide 7
3.19: Endurance test for LT/C tyres with Speed symbol < Q
  Carbon copy and renumbering of
      3.16.1 Requirements
      3.16.2 Preparing the tyre
      3.16.3 Test procedure
      Remove 3.16.3.3. In the case of tyres with a speed symbol Q and above, test procedures are as specified in paragraph 3.16.4.
      Remove 3.16.3.3.1. For all other tyre types, the endurance test programme is shown in paragraph 3.16.4.7.
      3.16.4.7 Endurance test programme