## Slide 1
The comparison of warning effectiveness
Informal Document - ACSF-20-17
ACSF IWG 20th meeting
November 2018, Liverpool
Korea Automobile Testing & Research Institute

## Slide 2: warning comparison
The Outline for warning experiment
  Total : 35 persons / Age : 25 ~ 70 years old
Optical warning |  | Acoustic warning |  | Haptic warning | 
Location | HUD | Frequency | 880Hz + 1760Hz | Type | Driver’s seat vibration
Size | Height : 20 mm Width : 85 mm | Loudness | 70dB | Frequency | 200 ~ 250 Hz
 |  |  |  | Duration | 200 ms / 50 ms

## Slide 3: Test Case
Order | NDRTs | Warning
random *. To prevent guessing test case | Visual perceptional task (see 6th slide of ACSF-18-09) | Optical only
 |  | Acoustic only
 |  | Haptic only
 |  | Optical-Acoustic
 |  | Optical-Haptic
 |  | Acoustic-Haptic
 |  | 3 Multi
Test [n]
Test [n]
Test [n]
Test [n]
Test [n]
Test [n]
Test [n]
SET A
SET B
SET C
[n] : 1…7

## Slide 4: Test Case
Training (MD)
3min
10min
Training (MD↔AD)
4min
Training (MD)
3min
SET A,B(Training)
SET C~E(Tests)
MD
1min
17min
5min
MD
1min
5min
5min
Test
Test
Test
3min
MD→AD
AD
10”
Alarm
AD→MD
MD
1min
MD : Manual Driving
Visual NDRT Random start between
2m 10” ~ 2m 25”

## Slide 5: Result of warning comparison
The result of Single/Multi warning experiment
  Probability of reaction(taking handle or pressing brake
Reaction time | Optical | Acoustic | Haptic | Optical& Acoustic | Optical& Haptic | Acoustic& Haptic | 3 Multi
~2sec | 0% | 34% | 46% | 40% | 77% | 64% | 74%
~4sec | 0% | 97% | 94% | 97% | 100% | 94% | 100%
~8sec | 6% | 100% | 100% | 100% | 100% | 100% | 100%
8sec~ | 100% | 100% | 100% | 100% | 100% | 100% | 100%