## Slide 1: Study about Audible Warning system effects for VRU safety
JAPAN
VRU-Proxi-08-11

## Slide 2
Test condition
Audible warning timing
5 cases of timing, every participants experienced each conditions 5 trials (randomized order)
 | Positions of audible warning indication
Case 1 | 0.0m reversing (just after R-range selected)
Case 2 | 0.5m reversing
Case 3 | 1.0m reversing
Case 4 | 2.5m reversing
Case 5 | No warning
Measurements
- GPS for vehicle motion and camera for driver behavior equipped for test vehicle.
Measurements |  | Device | Accuracy
Vehicle motion | Position (reversing distance) Speed (reversing speed) Audible warning output Gear position (Reverse range) | VBOX3i SL-RTK VBOX3i SL-RTK VBOX3i SL-RTK VBOX3i SL-RTK | 0.01m (100Hz) 0.01km/h (100Hz) 0.1mV (100Hz) ON/OFF (100Hz)
Driver behavior | Pedal operation Eye sight direction | Small camera Small camera | (30Hz) (30Hz)
Test Methods
Participants: Total 24 drivers
Average 38.5±11.7 years old (20’s, 30’s, 40’s, 50’s x male/female x 3)

## Slide 3
Instructions for participants
- Reversing to parking lot about 10m behind.
- In case of aware audible warning, braking for decelerate vehicle and stop as soon as possible.
- Carefully drive imagining being at a parking lot of typical commercial facilities where people and cars come and go.
Before driving,
- Participants confirm the difference between audible warning and information sound for “reverse gear”.
- Participants confirm not to easy to see small child (about 1m height) behind the vehicle by direct or indirect vision from the driver’s seat.
- Participants exercised velocity, acceleration feel and braking feelings of test vehicle beforehand.
Image of a parking lot of typical commercial facilities
Instructions for audible waring and rear vision
Exercise of reversing of test vehicle
Test Methods

## Slide 4
Methods for driving
Environments imitating public parking space set at proving ground (JARI)
Task
1) Reversing to parking lot about 10m behind
2) In case of audible warning indication (buzzer), braking, decelerate and stop the vehicle.
Audible warning was made for any timing indication.
No obstacles located behind the vehicle.
Test Methods
Area for examiners
Pylons
Pylons
Car stop
Car stop

## Slide 5
Audible warning
・Continuous 1,220Hz
・70db at headrest
Test vehicle
SUV (Nissan X-trail) used.
Audible warning provided small speaker located upper-side of cluster.
（http://history.nissan.co.jp/X-TRAIL/T32/1312/spec_dimensions.html）
Test Methods

## Slide 6
Vw
tstart
Vmax
Vmax×0.8
Vmax×0.2
Reverse gear selected
tr
td
Lstop
αa
αd
Reversing motion started
Audible warning
Stop
Warning sound
R gear
Reversing speed
Reversing distance
Acquired data
Reversing speed [km/h]
Reversing distance [m]
Time [sec]
1) | tstart | Time to vehicle move
2) | αa | Acceleration
3) | Vmax | Maximum velocity
4) | Vw | Velocity at warning
5) | tr | Reaction time to warning
6) | td | Time to reduce speed
7) | αd | Deceleration ratio
8) | Lstop | Stop distance

## Slide 7
Time to motion from reverse gear selected
(2~5 trial at Condition 2~5, N=384)
Results
Number of cases
Time to motion [sec]
Cumulative cases [%]

## Slide 8
※Total 6 time were not stopped. It was composed by 3 of 24 drivers.
Results
Number of cases
Cumulative cases [%]
Stop distance just after reverse gear selected
(2~5 trial at Condition 1, N=384)
Stop distance [m]

## Slide 9
Speed at warning and stop distance
（2~5 trials at condition 2~4, N=384 ）
Results
Reaction time for warning and stop distance
（2~5 trials at condition 2~4, N=384 ）
Deceleration and stop distance
（2~5 trials at condition 2~4, N=384 ）
Deceleration time and stop distance
（2~5 trials at condition 2~4, N=384 ）
Stop distance [m]
Stop distance [m]
Stop distance [m]
Stop distance [m]
Speed at warning [km/h]
Reaction time for warning [sec]
Deceleration time [sec]
Deceleration [m/s2]

## Slide 10
Vw | Speed at warning
αd | Deceleration
tr | Reaction time for warning
td | Time for deceleration
Case: Estimated using minimum data from subjects
※Deceleration characteristics
Modeling of reversing behavior for warning
Estimated stop distance
Vw
tr
td
αd
Stop distance [m]
Estimated stop distance [m]
Case: Estimated using maximum data from subjects
Stop distance [m]
Estimated stop distance [m]
Case: Estimated using mean data from subjects
Stop distance [m]
Estimated stop distance [m]

## Slide 11
Calculate Stop distance to pedestrian (Dvp)
Estimate Stop distance (Dstop)
Conditions | Rw | Range of audible warning (0.0~3.5m)
 | Lp | Pedestrian distance（0.0m～3.5m）
 | Ddbsw | Stop distance in case of warning indicated before reversing motion (ID01~ID24) -> Maximum for each participants (condition 1)
 | αa | Reversing acceleration (ID01~ID24) -> Maximum for each participants (condition 5)
 | Vmax | Maximum of reversing speed (ID01~ID24) -> Maximum for each participants (condition 5)
 | Tcv | Deceleration characteristics (ID01~ID24) -> Mean for each participants (condition 2~4)
Calculated data | Dw | Reversing distance for audible waring
 | Vw | Speed at audible warning
 | Dstop | Estimated stop distance
 | Dvp | Stop distance to pedestrian
Choice of Range of audible warning (RW)
※0.1m step from 0.0～3.5m (total 36 cases)
Choice of Pedestrian distance (LP)
※0.1m step from 0.0～3.5m (total 36 cases)
Choice of driver
※ID01~ID24 (total 24 cases)
Indicate waring before reversing motion (LP≦Rw)
NO
（ Vmax ）
（ Vmax ）
Calculate Speed at audible warning (VW)
Estimate Stop distance (Dstop)
YES
Lp
Dw
vp
Initial location
Pedestrian
Audible warning
Stop
Vw
Rw
Dvp
Dstop
Calculate Stop distance (Dvp) for all combinations (total 31,104 cases) of Warning distance(Rw), Pedestrian distance (Lp) and drivers (ID01~ID24).
Methods for numerical simulation

## Slide 12
Percentage of “vehicle stop before reaching pedestrian (Dvp<0)“ were calculated as Ratio of accident reduction in each warning distance cases (total 864 cases).
Calculations of the waring effects
87% accident was reduced at 1m warning distance.
Effects of waring for damage reduction are shown in deceleration.
Vehicle speed of contact pedestrian is about 4km/h, Rap between vehicle and pedestrian is about 0.2m in the most of cases (95%tile) at 1m waring .
Ratio of accident reduction
Warning distance to pedestrian [m]
Vehicle velocity to contact pedestrian
Rap between vehicle and pedestrian
Cumulative cases [%]
Cumulative cases [%]

## Slide 13
Simulation results
Ratio of accident reduction
Warning distance to pedestrian [m]
Rap between vehicle and pedestrian
0.87 at 1m
1.0 at 1.5m
Almost 1.0 at 1m regarding fatality reduction
Cf. Small vehicle rear overhang short type : 0.43m

## Slide 14
Appendix

## Slide 15
Honda N-WAGON dimension
Honda HP （https://customer.honda.co.jp/faq2/userqa.do?user=customer&faq=faq_auto_sp&id=69628&parent=60455）

## Slide 16
Monitoring Range of Audible Warning System
OEM | Vehicle Name | Monitoring Range (cm) |  |  |  | Comment
 |  | Front Center | Front Corner | Rear Center | Rear Corner | 
MALSO(ISO17386) |  | 60 | 50 | 100 | 50 | 
TOYOTA | Crown:2018 | 100 | 60 | 150 | 60 | 
NISSAN | LEAF:2017 | 100 | 60 | 150 | 60 | 
HONDA | LEGEND:2018 | × | 60 | 110 | 60 | 
Mazda | CX-8:2017 | 100 | 55 | 150 | 55 | 
Mitsubishi | Eclipse-cross:2018 | 60 | 60 | 125 | 60 | 
Subaru | Levorg:2017 | × | × | 150 | ？ | 
Daihatsu | Thor:2017 | 100 | 60 | 150 | 60 | 
Daimler | C class:2014 | 100 | 60 | 120 | 80 | 
Daimler | A class:2018 | 30 | ？ | 100 | ？ | @default setting
BMW | 7 series:2016 | 70 | 60 | 150 | 60 | 
VW | Golf7:2013 | 120 | 60 | 160 | 60 | 
VW | Passat:2014 | 120 | 60 | 160 | 60 | 
Volvo | XC40：2018 | 80 | ？ | 150 | ？ | 
Tesla | Model S:2015 | 70※ | ？ | 90※ | ？ | Measurement value
Extracted from published material.