## Slide 1: List of potential candidate functions for GTRs ( 1/2 )
UN-ECE R48.06 | UN-ECE/FMVSS Today compatibility | Comments
6.1. MAIN-BEAM HEADLAMP | 60% | maximum luminous intensity FMVSS up to 75.000cd UN_ECE up to 215.000cd
6.2. DIPPED-BEAM HEADLAMP | 10% | Cut-off definition and installation FMVSS VOL or VOR UN_ECE Depending on the mounting height
6.3. FRONT FOG LAMP | 90% but | FMVSS not legislated (SAE J583 harmonized with UN_ECE)
6.4. REVERSING LAMP | 80% | 
6.5. DIRECTION-INDICATOR LAMP | 50% | Color and installation FMVSS rear RED or AMBER UN_ECE AMBER
6.6. HAZARD WARNING SIGNAL |  | 
6.7. STOP LAMP | 80% | 
6.8. REAR REGISTRATION PLATE |  | 
6.9. FRONT POSITION LAMP | 70% | Color FMVSS WHITE or AMBER UN_ECE WHITE
6.10. REAR POSITION LAMP | 80% | 
6.11. REAR FOG LAMP | 90% but | FMVSS not legislated (SAE J1319 OK)
6.12. PARKING LAMP |  | 
6.13. END-OUTLINE MARKER |  | 
SLR-27-02

## Slide 2: list of potential candidate functions for GTRs ( 2/2 )
UN-ECE R48 | UN-ECE/FMVSS Today compatibility | Comments
6.14. REAR RETRO-REFLECTOR, NON-TRIANGULAR |  | 
6.15. REAR RETRO-REFLECTOR, TRIANGULAR |  | 
6.16. FRONT RETRO-REFLECTOR, NON-TRIANGULAR |  | 
6.17. SIDE RETRO-REFLECTOR, NON-TRIANGULAR |  | 
6.18. SIDE-MARKER LAMPS |  | 
6.19. DAYTIME RUNNING LAMP | 70% | 
6.20. CORNERING LAMP | 90% but | FMVSS not legislated (SAE J852 ok)
6.21. CONSPICUITY MARKINGS |  | 
6.22. ADAPTIVE FRONT LIGHTING SYSTEM (AFS, including ADB) | 40% but | FMVSS not yet legislated (SAE J2838 for passing beam harmonized with UN_ECE SAE J3069 for driving beam not harmonized with UN_ECE)
6.23. EMERGENCY STOP SIGNAL |  | 
6.24. EXTERIOR COURTESY LAMP |  | 
6.25. REAR-END COLLISION ALERT SIGNAL |  | 
6.26. Manoeuvring lamps |  |