## Slide 1: Proposed Definition of the Pause Function
JASIC Noise subcommittee
Koichi Hirata

## Slide 2: Tasks for TFRW #5
Discussion status regarding Pause function at the TFRW#5
The group requested that Japan should present at the next meeting more information, evidence and facts for the need of a “Pause function” not influencing the safety aspect of a reverse warning device. The Group pointed out that an equal level of safety has to be fixed inside this UN-Regulation, if requirements about Pause Switch would be included (e.g. camera-monitor system, which also will be steered by an existing trailer with/without camera-monitor system).
What is necessary for the pause function to be usable:
- The driver is ensured of the rearward field of vision behind the vehicle, including when towing other vehicles. The rearward field-of-vision device is operable;
- The definition of the rearward field-of-vision device is clearly given;
- The acoustic reverse warning device automatically returns to normal mode (when reverse gear is re-engaged or when ignition is re-activated).

## Slide 3: Provisions of the Austrian Regulations of reverse alarm
Note 3:
The camera/monitor system shall be activated automatically when reverse gear is engaged. Further, the camera/monitor system shall comply with ECE regulation 49.02 or EU directive 2003/97/EC, otherwise it shall have the following features:
- A 6-inch screen monitor;
- A contrast ratio of 600:1 or above;
- An active brightness control;
- A TV resolution of 330 (H) x 350 (V);
- A luminous sensitivity with sufficient backup light for the driver in operation.
Note 2:
Pursuant to the 47th amendment to KDV (BGBL Part II No. 414/2001), the following phrase was added to Article 18, paragraph 8 of the Act: “the reverse warning device shall be switchable to a quiet mode of not less than 55dB (A) ± 3dB (A), while ensuring that it is automatically reactivated to normal mode every time ignition is re-activated.
Between 10:00 p.m. and 5:00 a.m., the acoustic reverse warning device may be de-activated providing it automatically activates a flashing visual warning every time reverse gear is engaged; provided, however, that a reverse warning device is not required when the vehicle is equipped with an alternative safety device, such as a camera/monitor system, that enables the driver to check the space behind the vehicle.
Changes by the 47th amendment to KDV
- Pursuant to the 47th amendment to KDV (BGBL Part II No. 414/2001 published on November 30, 2001 (see Note 2)), the manufacturer shall allow a reverse warning device to be switched temporarily to a quiet mode of not less than 55dB (A) ± 3dB (A), while ensuring automatic return to normal mode every time ignition is reactivated.
- Between 10:00 p.m. and 5:00 a.m., the acoustic reverse warning device may be de-activated subject to its triggering a flashing visual warning every time reverse gear is re-engaged. << EC expert: This means that we need to consult the appropriate GR, as we set out requirements on a visual flashing warning.
- Notwithstanding the foregoing, the acoustic reverse warning device is not required should the vehicle be equipped with an alternative safety device, such as a camera/monitor system, that allows the driver to check the space behind the vehicle (see Note 3).

## Slide 4: Draft Proposed by TFRW #5
11. Definitions (Part II)
[11.8. "Pause function" means a mechanism to halt temporarily the operation of an acoustic reverse warning device.]
[14.3. Pause function
The manufacturer may install a function for temporary deactivation of the reverse warning sound when a vehicle of category M2 (M>3500 kg), N2, M3 or N3 and O is equipped with rear camera or detection system which complies with UN Regulation No. 46. Any other deactivation function, which does not satisfy the specification below, is prohibited.
14.3.1. The function shall be located so that it is operable by the driver in a normal seating position.
14.3.2. In the case when the pause function is activated, the suspension of reverse warning sound shall be clearly indicated to the driver.
14.3.3. The acoustic reverse warning device shall be reactivated to “Normal Level” after [3] minutes or from the vehicle being re-started.
14.3.4. Operator’s manual information
If a pause function is installed, the manufacturer shall provide the operator with information (e.g. in the operator’s manual) as to the hazard(s) created by using it:
"The pause function of the reverse warning sound device shall not be used unless for an obvious lack of necessity to emit sound for alert in the surrounding area and that it is certain that there are no pedestrians at risk

## Slide 5: Proposed Changes for the Definition of the Pause Function
11. Definitions (Part II)
[11.8. "Pause function" means a mechanism to halt temporarily the operation of a reverse warning device.]
14.3. Pause function
The manufacturer may install a function to disable temporarily the acoustic reverse warning device when a vehicle of category M2 (M>3500 kg), N2, M3/N3, or O is equipped with a safety system, such as a rearward facing camera system or a detection system*, allowing the driver to check the hazard area behind the vehicle, including when towing vehicles, and it is ensured that such safety system(s) functions while reversing. Any other disabling function which does not satisfy the specifications below is prohibited:
14.3.1. The function (pause function) shall be located so that it is operable by the driver in a normal seating position.
14.3.2. In the case when the pause function is activated, the suspension of reverse warning sound will be clearly indicated to the driver.
14.3.3. The acoustic reverse warning device will be reactivated to “Normal Level” when the vehicle’s engine is re-started following each vehicle de-activation..
14.3.4. Operator’s manual information
If a pause function is installed, the manufacturer shall provide the operator with information (e.g. in the vehicle’s manual) as to the increased risks thus created:
"The pause function of the reverse warning sound device shall not be used save for an obvious lack of necessity and the driver is certain that there are no pedestrians within the hazard area."
*This type of safety system shall be activated automatically whenever reverse gear is engaged. Further, the camera/monitor system, etc. shall comply with ECE regulation xx.00 (Devices for Reversing Motion).
Considering that the safety system used to temporarily replace the reverse warning device should be compatible with relevant UN regulations adopted based on the international discussion on driver’s field of vision for safety, we propose, regarding the requirements for the video system allowing the driver to check the space behind the vehicle, that the provision refers to the new UN regulation.