## Slide 1
WLTP CoP Procedure for CO2/FC
JRC Proposal
B. Ciuffo, A. Marotta
WLTP CoP TF telco
April 8, 2019

## Slide 2
CoP is a means of evidencing the ability to produce a series of products that comply with the specifications, performance and marking requirements demonstrated and outlined in the type approval documentation.
CoP should thus be sufficiently robust to ensure the conformity of what is produced with what has been demonstrated during type-approval
Given the complexity of the “vehicle” product, CoP is not a trivial task as there are many uncertainties
  In the production process
  In the testing method
Conformity of production (CoP)

## Slide 3
Managing the existing uncertainty is a task that should not be underestimated
  It is necessary to ensure sufficient evidence to base the conformity upon
  It is important to follow sound statistical procedures in order to have sufficient confidence on the results of the assessment
In particular, what we want to achieve at the end of the CoP is sufficient confidence that there is no significant difference between the emissions and CO2/FC measured during the type-approval process (thus representative of the entire population) and what is measured from the population sample
Conformity of production (CoP)

## Slide 4
Population. During the emission type approval, CO2 results are compared with a declared value (DV). DV is accepted if the resulting CO2 is lower than DV
  When it comes to CoP, there are 3 reasons why DV should be higher than the population mean:
    Customer protection (the CO2/FC declared on the CoC should be higher than the individual vehicle CO2/FC value under WLTP, for the majority of the consumers);
    Imposing a margin between DV and population mean creates an incentive at production level to improve the quality and decrease the CO2/FC spread;
    Assuming that DV could be equal to the population mean would penalise manufacturers with higher production quality standards.
Confidence Interval. In the hypothesis that the different CoP samples are uncorrelated and that the production process does not change over time, confidence intervals can be the right tool to assess whether the population is in line with the expectation with a certain confidence
  Confidence interval around the mean with 90% or 95% confidence can be used
Conformity of production (CoP). Conditions

## Slide 5
In order to use a pragmatic approach, 16 can still be the maximum sample size
The boundaries of the confidence interval are calculated using a Student distribution with (N-1) degrees of freedom and the standard deviation of the sample
DV is assumed to be the upper bound of the acceptance region in case of 16 tests
The assumption on DV leads to the identification of the theoretical mean of the CO2 distribution. This depends on the confidence level and the standard deviation of the distribution (either the theoretical value or the sample value)
Conformity of production (CoP). Approach

## Slide 6
Conformity of production (CoP). Acceptance-Rejection Region (s=3%)
DV
DV
m
m
m=DV-(t90,(16-1)*s/√16)
m=DV-(t95,(16-1)*s/√16)

## Slide 7
The method was tested using a simulation approach. In particular
  100.000 combinations of 16 randomly generated results of CoP tests have been derived from a population having
    mean (m)
    standard deviation (s)
Simulation results derived in terms of
  Probability for a vehicle to have CO2 higher than the declared value (Pr{x<DV}): Defective rate
  Overall Pass/Fail probability
  Pass/Fail rate at the end of each CoP step
Assessment of the method

## Slide 8
Simulation results
  Pr{x<DV}=67%
  Pass/Fail Rate
Simulation 1.1: m=m, s=3%

## Slide 9
Simulation results
  Pr{x<DV}=67%
  Pass/Fail Rate
Simulation 1.2: m=m, s=2%

## Slide 10
Simulation results
  Pr{x<DV}=67%
  Pass/Fail Rate
Simulation 1.3: m=m, s=1%

## Slide 11
Simulation results
  Pr{x<DV}=67%
  Pass/Fail Rate
Simulation 1.4: m=m, s=0.5%

## Slide 12
Simulation results
  Pr{x<DV}=63%
  Pass/Fail Rate
Simulation 2.1: m=0.99, s=3%

## Slide 13
Simulation results
  Pr{x<DV}=69%
  Pass/Fail Rate
Simulation 2.2: m=0.99, s=2%

## Slide 14
Simulation results
  Pr{x<DV}=84%
  Pass/Fail Rate
Simulation 2.3: m=0.99, s=1%

## Slide 15
Simulation results
  Pr{x<DV}=98%
  Pass/Fail Rate
Simulation 2.4: m=0.99, s=0.5%

## Slide 16
Simulation results
  Pr{x<DV}=50%
  Pass/Fail Rate
Simulation 3.1: m=1, s=3%

## Slide 17
Simulation results
  Pr{x<DV}=50%
  Pass/Fail Rate
Simulation 3.2: m=1, s=2%

## Slide 18
Simulation results
  Pr{x<DV}=50%
  Pass/Fail Rate
Simulation 3.3: m=1, s=1%

## Slide 19
Simulation results
  Pr{x<DV}=50%
  Pass/Fail Rate
Simulation 3.4: m=1, s=0.5%

## Slide 20
Simulation results
  Pr{x<DV}=37%
  Pass/Fail Rate
Simulation 4.1: m=1.01, s=3%

## Slide 21
Simulation results
  Pr{x<DV}=31%
  Pass/Fail Rate
Simulation 4.2: m=1.01, s=2%

## Slide 22
Simulation results
  Pr{x<DV}=16%
  Pass/Fail Rate
Simulation 4.3: m=1.01, s=1%

## Slide 23
Simulation results
  Pr{x<DV}=3%
  Pass/Fail Rate
Simulation 4.4: m=1.01, s=0.5%

## Slide 24
In the hypothesis that the CoP sample is composed by independent tests and that the production process does not change over time, confidence intervals around the mean represent a powerful and statistically sound tool to be used for the CoP of vehicle emissions
Confidence intervals allow to identify a conform family with a high likelihood.
The risk to reject a valid family is reasonable (~10%)
The risk to accept an invalid family is reasonable as well
In order to have a family accepted an OEM has multiple options:
    declare a CO2 value sufficiently higher than the population average with a lower sample size than 16 vehicles;
    declare a lower value above the population average with a sample up to 16 vehicles;
    Improve the production quality and decrease the standard deviation.
Conclusions

## Slide 25
Thanks
Questions?
You can find me at Biagio.CIUFFO@ec.europa.eu