## Slide 1: Discussion results – 14 June 2019
Influence of EC proposal to expand the scope of crash regulations (R94/95/137)
  - Possibility to merge two objectives into one series of amendments and submit formal proposal to Dec/2019 GRSP was considered. The merged drafts will be prepared for further discussion at ad-hoc meeting (probably in early July, organized by the EC). The extension of the scope proposed does not affect the existing approvals and therefore will not affect the transitional provisions for transposition of GTR.
Need for updating R12 – Suspend the transposition and seek for guidance from WP29/GRSP
Scope of R100 – All to confirm new description of the definition of REESS
Other feedbacks on the draft V.3 – See updated draft
Overcurrent test in R100 – To confirm the US position if there is any change since adoption of GTR
R100: All to review the update made and provide feedback by end/July
Draft for submission to GRSP will be prepared by Iwasaki and forwarded to the EC and Japan by 15/Nov.

## Slide 2: Definition of REESS – outcome of 14 June 2019
2.37. "Rechargeable Electrical Energy Storage System (REESS)" means the rechargeable energy storage system that provides electric energy for electric propulsion.
A battery whose primary use is to supply power for starting the engine and/or lighting and/or other vehicle auxiliaries systems is not considered as a REESS. [Primary use in this context means that more than 50% of the energy from the battery is used for starting the engine and/or lighting and/or other vehicle auxiliaries systems over an appropriate driving cycle, e.g. WLTC for M1 and N1.]
The REESS may include subsystem(s) together with the necessary ancillary systems for physical support, thermal management, electronic control and enclosures.
Discharge current of battery integrated over the cycle will be separated for auxiliaries and for traction and if the portion of auxiliaries is greater, that battery is not considered as REESS.
Appropriate cycle will be determined through consultation between manufacturer and technical service