## Slide 1: COP statistic for UN-WLTP ACEA comments on JRC proposal presented April 8,2019
May 2019

## Slide 2
COP
ACEA comment to COP procedure presented by JRC in April 2019
  Concern about definition of a “theoretical mean” and calculation of confidence intervals around this instead of the declared value.
  Concern about the plan to revise only the statistical procedure for CO2 with the consequence to end up with totally different procedures for CO2 and pollutants.

## Slide 3
Concept proposed by JRC
… builds confidence intervals around a calculated theoretical mean m < declared value DV.
I.e. the COP assessment is based on m up to the 15th vehicle.
m is understood as an estimate for the population mean.
m is depending on the standard deviation of the population,which is normally unknown (estimate needed).
How to calculate m if vehicles with different DV are in the COP family,but the composition of vehicles in the sample is unknown at begin of the sampling process?

## Slide 4
COP testing against DV
The population mean has to be lower than the declared value.
The only reason is:protection against variation – to meet the declared value with sufficient probability.
Commitment of the manufacturer is that the CO2 emissions of the vehicles meet the declared value,and not a lower value.
Therefor the reference for COP testing has to be the declared value,from begin of the sampling process.
COP assessment based on declared value instead of m leads to faster decision.

## Slide 5
ACEA Comments (blue) to JRC rationals
  When it comes to CoP, there are 3 reasons why DV should be higher than the population mean:
    Customer protection (the CO2/FC declared on the CoC should be higher than the individual vehicle CO2/FC value under WLTP, for the majority of the consumers);
    ACEA:no,orientation for the customer and basis for his competitive analysis is only the declared value;customer cannot expect lower CO2/FC under WLTP.
    b. Imposing a margin between DV and population mean creates an incentive at production level to improve the quality and decrease the CO2/FC spread;
    ACEA:main contributer to the spread is test repeatability (driver impact) and measurement accuracy.
    c. Assuming that DV could be equal to the population mean would penalise manufacturers with higher production quality standards.
    ACEA:DV equal mean,means 50% defective.Resulting passing probability approx. 50%.No OEM would design for such a risk.

## Slide 6
Concept for c02 and pollutants
Current WLTP regulation describes the same statistical method for the COP evaluation of CO2 and pollutants.
Main concern of this method is that the uncertainty of calculated standard deviation (varianz) is not considered appropriately.
COM plans to revise only the calculation method for CO2.
This will lead to an inconsistent approach with 2 different concepts.
Fast decision for pollutants following current method,while,following JRC proposal,high number of tests would be likely needed to get decision for CO2.

## Slide 7
conclusion
ACEA asks
to re-visit the proposal to calculate confidence interval around DV (see also ACEA presentation from February 2019) and to avoid the definition of an add. theoretical mean m.
to adopt the concept of confidence intervals to pollutants (replace DV by limit)