## Slide 1
Current text requires that the cybersecurity requirements shall have already been taken into account in the development phase of the vehicle architecture including the supply chain.
Some of the Electronic Architectures of the vehicles that will still be produced in 2024, have been developed long time before the UN Regulation has been drafted (live cycle ca. 15 years).
Only for new Electronic Architectures (designed under the knowledge of the final UN Regulation) it is possible to respect all requirements.
Need to find a solution before adoption of the text.
Potential solution (as for R83 for WLTP integration): Create series 00 and series 01 with different requirement levels.
1) Application of Cybersecurity Regulation for new registrations

## Slide 2
Vehicles that can be technically retrofitted with type approved SW updates may be allowed to get those SW updates even when they are registered before the entry into force of the SW update Regulation.
This should be under the decision of each country.
May be added in the recommendation part.
2) Retrofit of SW updates on vehicles registered before entry into force of SW update Regulation

## Slide 3
To integrate an RXSWIN on the vehicle which is readable via the OBD port requires important changes in Electronic Architecture.
For this reason, the RXSWIN shall only be introduced on a voluntary basis.
The draft UN Regulation on SW update GRVA/2019/3 defines in Annex B:
"x.y. Requirements for software identification
x.y.1. For the purpose of ensuring the software of the System can be identified, an RXSWIN may be implemented by the vehicle manufacturer.
x.y.2. If the manufacturer implements an RXSWIN the following shall apply:
x.y.2.1. The vehicle manufacturer shall have a valid approval according to UN Regulation No. xxx [Software Update Process Regulation].
x.y.2.2. The vehicle manufacturer shall provide the following information in the communication form of this Regulation:
- the RXSWIN
- how to read the RXSWIN”
Can the UN TF confirm that RXSWIN is only voluntary (when the vehicle manufacturer foresees to update the system with type approval impact)?
3) Voluntary introduction of RXSWIN

## Slide 4: 4) Lifecycle of a vehicle type* vs. Lifetime of a vehicle
Development Phase
Production Phase of a Vehicle Type*
Post Production Phase
Vehicle Type Approval
(first vehicle of this vehicle type manufactured)
End of Production
(last vehicle of this vehicle type manufactured)
Article 4 of 1958 Agreement applies.
Type approval expired but vehicles can still be used (national law).
Vehicles 1 & 2 & 3 can be of different carlines
Lifetime of Vehicle 1
Use Phase
Post Use Phase
Registration
End of Registration
Scrappage
Lifetime of Vehicle 2
Use Phase
Post Use Phase
Registration
End of Registration
Scrappage
Lifetime of Vehicle 3
Use Phase
Post Use Phase
Registration
End of Registration
Scrappage
*Vehicle type regarding Cybersecurity (System Type Approval) = EE Architecture
Day of Manufacture
Lifecycle of a vehicle type*
What the UN Regulation provides:
A comprehensive management system over the entire lifecycle of the vehicle type including
  Risk management
  Inclusion of suppliers
  Field Monitoring
  Incident response