## Slide 1: SIMPLIFICATION. Status GTB WG FL on May 23rd , 2019
SLR-30-11

## Slide 2: Introduction
Definition of requirements for basic/”C” passing beam which is technologically neutral and performance oriented.
Definition of Low speed /”V” and Motorway /”E” Adverse weather passing beam requirements
Specific passing beams for 2 wheelers
Driving beam
  Specific beams for 2 wheelers
Front fog Lamp and Cornering lamp
How to manage beams / vehicles categories?
Next Step.

## Slide 3: Strategy
Currently RID In the future: RID stage 2
R112 Class A
Class B
Class AR
Class BR
R98 Class DC
Class DR
R123 Class C
Class E
Class V
Class W
Class XR
ADB
R113 Class AS
Class BS
Class CS
Class DS
Class ES
Class R-BS
Class R-CS
Class R- DS
Class R- ES
R19 Class B- F3
R119 Class K
Basic /”C” Passing beam
Low speed /”V” Passing beam
Motorway/”E” Passing beam
Adverse weather/”W” passing beam
Basic Driving beam
Low speed Driving beam
ADB
AS, BS for mopeds
CS, DS for motorbikes
Secondary driving beams (2 wheelers)
Auxiliary driving beam
Fog beam
Cornering beam
TC4-45 SAE J2829
Expertise of Optical engineers
…
Class A
Class B
Class AR
Class BR
Class DC
Class DR
Class C
Class E
Class V
Class W
Class XR
ADB
Class AS
Class BS
Class CS
Class DS
Class ES
Class R-BS
Class R-CS
Class R- DS
Class R- ES
Class F3
Class K
1 regulation
23 Beam patterns
1 regulation
16 Beam patterns
6 regulations
24 Beam patterns

## Slide 4: Performance oriented and technologically neutral
Proposal focused on performances:
Independantly from the technology used for that purpose
(e.g.: performances are independant from the light source technology) ,

## Slide 5: Next steps?
Polishing the strategy:
  How to manage the different technical requirements  Done
    Basic passing beam, low speed/ town passing beam , Motorway Passing beam , AFS, Adverse weather…
    which light distribution for which vehicles?  Waiting for CEMA input
Technical requirements:
  Validation of basic requirement for passing beam.  Done
  Validation of Passing beams for 2 wheelers : AS, BS: same as today, new CS and new DS  Done
  Management of AFS/ ADB.
    Definition of requirement for Low speed /”V” passing beam/ “E” passing beam.  Done including 125R
    ADB  Done
    Adverse Weather Passing beam :  Done
  Definition of requirements for driving beams -> Done
  Front fog beam  Done:.
  Cornering  Done.
Redaction:
  Rewrite / optimization of RID text. on going.

## Slide 6: Passing beams

## Slide 7: Measurement points and SEGMENTS
ZoneIII
B50L
BR
BRR
BLL
75R
50V
50L
Seg 50
Seg 40RR
Seg 40LL
25V
Seg 25R
Seg 25L
Seg 25
Seg 15
Seg 10
40L
40R
50R

## Slide 8: Requirements for Passing beams

## Slide 9: for comparison: Illumination projected on the road for basic /”C” passing beam and current requirement RID class C (R123 Class C).
Bird’s eye view
Significant improvement of the proposal / R123 class C
Width on the road : 20m instead of 11.6 m .
+20% at 75 m.
Proposal Basic/”C” Passing Beam
RID class C
Values in blue: Mini
Values in red: Maxi

## Slide 10: for comparison: Illumination projected on the road for Motorway /”E” passing beam and current requirement RID class E (R123 Class E).
Bird’s eye view
Significant improvement of the proposal / R123 class E
Width on the road : 20m instead of 11.6 m .
Same illumination at 75 + requirement at 125m
Proposal Motorway /”E” Passing Beam
RID class E
Values in blue: Mini
Values in red: Maxi
Chart: 
| 49.94098568871847 | 75.371511947418981 | 49.963497054583954 | 49.873994361739214 | 24.008586909175154 | 24.517237757340091 | 10.692436555027161 | 10.718966006508685
 | -1.4997 | -1.513 | 0 | 2.9893 | 6.8844 | -4.7657 | 0.84151 | -0.37431
2.7
2.7
4.0
1.9
1.9
106.4
106.4
2.7
4.0
2.7
2.7
1.7
4.3
1.7
2.7
1.9
1.9
4.0
0.5
0.5
1.7
1.7
1.0
1.0
0.75

## Slide 11: Proposal for 2 wheelers, CS, DS

## Slide 12: Proposal for 2 wheelers, CS, DS
R113-01/02
IMMA Symmetrical PB proposal

## Slide 13: Comparison Current DS/ Proposal
Chart: 
| 49.870305061004345 | 49.963497054583954 | 49.870305061004345 | 20.745372457691474 | 20.745372457691474 | 10.078672913828196 | 10.078672913828196 | 21.212770111557759 | 21.212770111557759
 | -3.0502 | 0 | 3.0502 | -5.5587 | 5.5587 | -3.6683 | 3.6683 | -3.3598 | 3.3598
0.8
5.5
2.4
2.0
2.9
0.8
5.5
2.4
2.6
2.6
2.9
Line 1
0.8
5.5
2.0
0.8
5.5
0.5
0.5
2.4
2.4
2.6
2.6
2.6
Current DS beam pattern
New DS beam pattern

## Slide 14: Driving beams

## Slide 15: Driving beams
Red dots: new points
Grey dots : point of the current requirement

## Slide 16: Driving beams
Secondary driving beam:
For motorbikes in combination with passing beam
Current R113/ RID
Proposal:
A wider pattern and increased values
Red dots: new points
Grey dots : point of the current requirement
CS
DS

## Slide 17: Front fog lamp

## Slide 18: Front Fog lamp

## Slide 19: Cornering lamp

## Slide 20: Cornering BEAM
30°

## Slide 21: Synthesis

## Slide 22: Next step:
Proposal :
To merge §5.2 and §5.3 of RID
Pending questions:
Luminous flux of light source of symmetrical passing beam,
1,000Lm thereshold for LED light sources / luminous flux in zones.
Run-up Behaviour

## Slide 23: Which beam(s) for which vehicle?
To be addressed with WG-I

## Slide 24: Installation requirements after SLR step 1 Regulation RID
R48
R86
R53
<125 cm3
>125 cm3
AS
BS, R-BS
CS, R-CS
DS, R-DS
ES, R-ES
A, AR
B, BR
CS, R-CS
DS, R-DS
ES, R-ES
Class B, BR
Class DC, DR
F3
2 x CS, 2 x R-CS
DS, R-DS
ES, R-ES
A, AR
B, BR
DC, DR
F3
Class B, BR
Class DC, DR
Class C
Class E
Class V
Class W
Class XR
ADB
Class F3
Class K
Class A, AR
Class B, BR
Class DC, DR
Class AS
Class BS, R-BS
Class CS, R-CS
Class DS, R-DS
Class ES, R-ES
Class F3
Class K
R74
Should the beam requirements be based on the category of the vehicle?
< 50 Km / h
Black: mandatory
Green : optional

## Slide 25: Proposal
Basic/”C” passing beam, Low Speed/”V” passing beam, Motorway/”E” passing beam.
Which passing beam/speed/driving conditions?
0
[50]
[110] km/h
Basic/ “C” passing beam – Basic driving beam
Low speed / “V” passing beam
Low speed driving beam
Motorway/“E” passing beam
Waiting for confirmation from Agricultural Vehicles Industry
“W”

## Slide 26: Alternative for Two Wheelers
26
0
Power (kW)
Displacement (cm3)
DS (PB & DB)
CS (PB & DB)
11kW
125cm3
AS , BS
Mopeds and electrical bikes