## Slide 1
Regulation No. 148 [LSD] – Stage II
Re-arrangement of the specific technical provisions in part 5
Existing provisions for each function in Regulation No. [148]
Proposal: New structure for Paragraph 5 including a fixed framework and empty requirements if no provision exists.
5.x. Name(s) and Symbol(s)
5.x.1. Luminous intensity (& table):
5.x.2. Standard light distribution:
5.x.3. Colour:
5.x.4. Apparent surface:
5.x.5. Measurement:
5.x.6. Other requirements:
[5.x.7. Failure provisions:]
If necessary, add additional sub-paragraphs
GTBWGSL 426 Rev1 (Rev. of GTBWGSL415)
?
Slides where guidance of IWG SLR is appreciated
Changes/clarifications to the original text/structure
text
!
Slides with changes to existing requirements
See comment on slide 2
SLR-30-12

## Slide 2
5.1 TECHNICAL REQUIREMENTS CONCERNING FRONT POSITION LAMPS (SYMBOLS A, MA) AND FRONT END-OUTLINE MARKER LAMPS (SYMBOLS AM)
5.1.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 3.
Table 3: Luminous intensities for front position and front end-outline marker lamps
5.1.2. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp must in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3, be not less than the minimum specified in paragraph 5.1.1., multiplied by the percentage specified in the said table of the direction in question.
5.1.3. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted must be not less than 0.05 cd for front position lamps and front end-outline marker lamps;
5.1.4. The colour of the light emitted shall be white, however the lamp identified by symbol ‘MA’ may be amber.
5.1. Front position lamps (A, MA) and front end-outline marker lamps (AM)
5.1.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 3.
Table 3: Luminous intensities for front position and front end-outline marker lamps
5.1.2. Standard light distribution:
5.1.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp sample must in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3, be not less than the minimum specified in paragraph 5.1.1., multiplied by the percentage specified in the said table of the direction in question.
5.1.2.2. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted must be not less than 0.05 cd for front position lamps and front end-outline marker lamps;
5.1.3. Colour:
The colour of the light emitted shall be white, however the lamp identified by symbol ‘MA’ may be amber.
5.1.4. Apparent surface:
No additional requirements.
5.1.5. Measurement:
No additional requirements.
5.1.6. Other requirements:
No additional requirements.
[5.1.7. Failure provisions:
See Par. 4.6.]
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.1.
Existing Text
New Text
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
Front position lamps, front end-outline marker lamp, A or AM | 4 | 140 | 70
Front position lamps (motorcycle), MA | 4 | 140 | N.A.
Front position lamps A incorporated in a headlamp or in a front fog lamp | 4 | 140 | N.A.
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
Front position lamps, front end-outline marker lamp, A or AM | 4 | 140 | 70
Front position lamps (motorcycle), MA | 4 | 140 | N.A.
Front position lamps A incorporated in a headlamp or in a front fog lamp | 4 | 140 | N.A.
Front position & front end-outline marker lamps
GTBWGSL 426 Rev1
For the time being add a paragraph in each function with reference to paragraph 4.6. !
Independent of a future common solution for failure provisions, it could be generally handled in one place only (paragraph 4.6.) – or to split the requirements for each function into the relevant sub-paragraph 5.x.7.?
?
Is a special paragraph “colour” necessary in the device Regulation as all the colour requirements are in the installation Regulations?

## Slide 3
5.2. Rear position lamps (R1, R2, MR) and rear end-outline marker lamps, (RM1, RM2)
5.2.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 4.
Table 4: Luminous intensities for rear position and rear end-outline marker lamps
5.2.2. Standard light distribution:
5.2.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp sample must in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2.1. of Annex 3, be not less than the minimum specified in paragraph 5.2.1., multiplied by the percentage specified in the said table for of the direction in question.
5.2.2.2. However, a luminous intensity of 60 cd shall be permitted for rear position lamps reciprocally incorporated with stop lamps below a plane forming an angle of 5° with and downward from the horizontal plane;
5.2.3. Colour:
The colour of light emitted shall be red. This requirement shall also apply within the range of variable luminous intensity produced by:
  (a) Rear position lamps of category R2;
  (b) Rear end-outline marker lamps of category RM2.
5.2.4. Apparent surface:
No additional requirements.
5.2.5. Measurement:
No additional requirements.
5.2.6. Other requirements:
No additional requirements.
[5.2.7. Failure provisions:
See Par. 4.6.]
5.2. TECHNICAL REQUIREMENTS CONCERNING REAR POSITION LAMPS (SYMBOLS R1, R2, MR) AND REAR END-OUTLINE MARKER LAMPS (SYMBOLS RM1, RM2)
5.2.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 4.
Table 4: Luminous intensities for rear position and rear end-outline marker lamps
5.2.2. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp must in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3, be not less than the minimum specified in paragraph 5.2.1., multiplied by the percentage specified in the said table for the direction in question.
5.2.3. However, a luminous intensity of 60 cd shall be permitted for rear position lamps reciprocally incorporated with stop lamps below a plane forming an angle of 5° with and downward from the horizontal plane;
5.2.4. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted must be not less than 0.05 cd for rear position lamps and end-outline marker lamps,
5.2.5. The colour of light emitted shall be red.
This requirement shall also apply within the range of variable luminous intensity produced by:
  (a) Rear position lamps of category R2;
  (b) Rear end-outline marker lamps of category RM2.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.2.
Existing Text
New Text
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
Rear position lamps, rear end-outline marker lamp |  |  | 
R1 or RM1 (steady) | 4 | 17 | 8.5
MR | 4 | 17 | N.A.
R2 or RM2 (variable) | 4 | 42 | 21
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
Rear position lamps, rear end-outline marker lamp, R1 or RM1 (steady) | 4 | 17 | 8.5
MR | 4 | 17 | N.A.
R2 or RM2 (variable) | 4 | 42 | 21
Rear position & rear end-outline marker lamps
Agreed to delete this requirement, since it is self-evident, that the colour requirement is applicable to all categories of these lamps?
It is also not mentioned for variable stop lamps and rear fog lamps!
GTBWGSL 426 Rev1
!
See comment on slide 2

## Slide 4
5.3. Parking lamps (77R)
5.3.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 5.
Table 5: Luminous intensities for parking lamps
5.3.2. Standard light distribution:
5.3.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp sample must, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2.1. of Annex 3, be not less than the minimum specified in paragraph 5.3.1., multiplied by the percentage specified in the said table of the direction in question.
5.3.2.2. However, a luminous intensity of 60 cd shall be permitted for parking lamps directed to the rear incorporated with stop lamps below a plane forming an angle of 5° with and downward from the horizontal plane;
5.3.2.3. Throughout the fields defined in the diagrams in Part A or B of Annex 2, the luminous intensity of the light emitted must be not less than 0.05 cd for front, rear and side parking lamps;
5.3.3. Colour:
The colour of light emitted shall:
  (a) For front parking lamps be white;
  (b) For rear parking lamps be red;
  (c) For side parking lamps be amber.
5.3.4. Apparent surface:
No additional requirements.
5.3.5. Measurement:
No additional requirements.
5.3.6. Other requirements:
No additional requirements.
[5.3.7. Failure provisions:
See Par. 4.6.]
5.3. TECHNICAL REQUIREMENTS CONCERNING PARKING LAMPS (SYMBOL 77R)
5.3.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 5.
Table 5: Luminous intensities for parking lamps
5.3.2. However, a luminous intensity of 60 cd shall be permitted for parking lamps directed to the rear incorporated with stop lamps below a plane forming an angle of 5° with and downward from the horizontal plane.
5.3.3. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp shall, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3, be not less than the minimum specified in paragraph 5.3.1., multiplied by the percentage specified in the said table for the direction in question.
5.3.4. Throughout the fields defined in the diagrams in Part B of Annex 2, the luminous intensity of the light emitted must be not less than 0.05 cd for front and rear parking lamps;
5.3.5. The colour of light emitted shall:
  (a) For forward facing parking lamps be white;
  (b) For rearward facing parking lamps be red;
  (c) For side facing parking lamps be amber.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.3.
Existing Text
New Text
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
forward facing parking lamps | 2 | 60
rearward facing parking lamps | 2 | 30
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
front parking lamps | 2 | 60
rear facing parking lamps | 2 | 30
Parking lamps
See additional document WGSL426 Rev.1 A
?
GTBWGSL 426 Rev1
See comment on slide 2

## Slide 5
5.4. Daytime running lamps (RL)
5.4.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 6.
Table 6: Luminous intensities for daytime running lamps
5.4.2. Standard light distribution:
5.4.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp sample must, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2.1. of Annex 3, be not less than the minimum specified in paragraph 5.4.1., multiplied by the percentage specified in the said table of the direction in question.
5.4.2.2. However, a luminous intensity of 60 cd shall be permitted for parking lamps directed to the rear incorporated with stop lamps below a plane forming an angle of 5° with and downward from the horizontal plane;
5.4.2.3. Moreover, throughout the field defined in the diagram in Part A of Annex 2, the intensity of the light emitted shall not be less than 1.0 cd.
5.4.3. Colour:
The colour of the light emitted shall be white.
5.4.4. Apparent surface:
The area of the apparent surface in the direction of the axis of reference of the daytime running lamp shall be not less than 25 cm2 and not more than 200 cm2.
5.4.5. Measurement:
No additional requirements.
5.4.6. Other requirements:
The daytime running lamp shall be subjected to the heat resistance test specified in Annex 6.
[5.4.7. Light source failure Failure provisions:
5.4.7.1. In the case of a daytime running lamp containing more than one light source, the daytime running lamp shall comply with the minimum intensity required and the maximum intensity shall not be exceeded when all light sources are activated.
In case of failure of any one light source in a single lamp containing more than one light source, one of the following provisions shall apply:
  (a) The light intensity at the points of standard light distribution defined in paragraph 2.2. of Annex 3 shall be at least 80 per cent of the minimum intensity required; or
  (b) The light intensity in the axis of reference shall be at least 50 per cent of the minimum intensity required, provided that a note in the communication form states that the lamp is only for use on a vehicle fitted with an operating tell-tale.]
5.4. TECHNICAL REQUIREMENTS CONCERNING DAYTIME RUNNING LAMPS (SYMBOLS RL)
5.4.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 6.
Table 6: Luminous intensities for daytime running lamps
5.4.2. Outside the reference axis the intensity of the light emitted by each lamp must, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3, be not less than the minimum specified in paragraph 5.4.1., multiplied by the percentage specified in the said table of the direction in question.
5.4.3. Moreover, throughout the field defined in the diagram in Part A of Annex 2, the intensity of the light emitted shall not be less than 1.0 cd.
5.4.4. Light source failure
5.4.4.1. In the case of a daytime running lamp containing more than one light source, the daytime running lamp shall comply with the minimum intensity required and the maximum intensity shall not be exceeded when all light sources are activated.
5.4.4.2. In case of failure of any one light source in a single lamp containing more than one light source, one of the following provisions shall apply:
  (a) The light intensity at the points of standard light distribution defined in paragraph 2.2. of Annex 3 shall be at least 80 per cent of the minimum intensity required; or
  (b) The light intensity in the axis of reference shall be at least 50 per cent of the minimum intensity required, provided that a note in the communication form states that the lamp is only for use on a vehicle fitted with an operating tell-tale.
5.4.5. The colour of the light emitted shall be white.
5.4.6. The area of the apparent surface in the direction of the axis of reference of the daytime running lamp shall be not less than 25 cm2 and not more than 200 cm2.
5.4.7. The daytime running lamp shall be subjected to the heat resistance test specified in Annex 6.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.4.
Existing Text
New Text
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
Daytime running lamps | 400 | 1200
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
Daytime running lamps | 400 | 1200
See comment on slide 2
Daytime Running Lamps
GTBWGSL 426 Rev1
!
?
Provision unclear. Remove completely or move to general requirement for all functions.

## Slide 6
5.5. Stop lamps (S1, S2, S3, S4, MS)
5.5.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 7.
Table 7: Luminous intensities for stop lamps
5.5.2. Standard light distribution:
5.5.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted by each lamp sample shall must, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2.1. or 2.3. of Annex 3 be not less than the minimum specified in paragraph 5.5.1., multiplied by the percentage specified in the said tables of the direction in question.
5.5.2.2. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted shall be not less than 0.3 cd for devices of categories S1, S3 and MS and for those of categories S2 and S4 by day; it shall not be less than 0.07 cd for devices of categories S2 and S4 by night.
5.5.3. Colour:
The colour of light emitted shall be red.
5.5.4. Apparent surface:
No additional requirements.
5.5.5. Measurement:
In the case of a category S3 or S4 stop lamp, which is intended to be mounted inside the vehicle, the colorimetric characteristics shall be verified with the worst case combination(s) of lamp and rear window(s) or sample plate(s).
5.5.6. Other requirements:
No additional requirements.
[5.5.7. Failure provisions:
See Par. 4.6.]
5.5 TECHNICAL REQUIREMENTS CONCERNING STOP LAMPS (SYMBOLS S1, S2, S3, S4, MS)
5.5.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 7.
Table 7: Luminous intensities for stop lamps
5.5.2. Outside the reference axis the intensity of the light emitted by each lamp shall, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2. of Annex 3 be not less than the minimum specified in paragraph 5.5.1., multiplied by the percentage specified in the said table of the direction in question.
5.5.3. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted shall be not less than 0.3 cd for devices of categories S1, S3 and MS and for those of categories S2 and S4 by day; it shall not be less than 0.07 cd for devices of categories S2 and S4 by night.
5.5.4. The colour of the light emitted shall be red.
In the case of a category S3 or S4 stop lamp, which is intended to be mounted inside the vehicle, the colorimetric characteristics shall be verified with the worst case combination(s) of lamp and rear window(s) or sample plate(s).
These requirements shall also apply within the range of variable luminous intensity produced by stop lamps of categories S2 and S4.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.5.
Existing Text
New Text
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
S1 (steady) | 60 | 260 | 130
S2 (variable) | 60 | 730 | 365
S3 (steady) | 25 | 110 | 55
S4 (variable) | 25 | 160 | 80
MS (steady) | 40 | 260 | N.A.
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
S1 (steady) | 60 | 260 | 130
S2 (variable) | 60 | 730 | 365
S3 (steady) | 25 | 110 | 55
S4 (variable) | 25 | 160 | 80
MS (steady) | 40 | 260 | N.A.
Could be also part of paragraph 5.5.3. !?
When staying in paragraph 5.5.5. we could get rid of all paragraphs 5.x.3. since colour is already stated in installation regulation?! (See slide 2 too)
Stop lamps
GTBWGSL 426 Rev1
?
See comment on slide 2

## Slide 7
5.6. Direction indicator lamps (1, 1a, 1b, 2a, 2b, 5, 6, 11, 11a, 11b, 11c, 12)
5.6.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 8 where the minimum luminous intensities shall be fulfilled:
  (a) In the case of direction indicators of categories 1, 1a, 1b, 2a, 2b, 11, 11a, 11b, 11c and 12 in the reference axis; or
  (b) in the case of direction indicators of categories 5 and 6 in direction A according to Annex 2.
Table 8: Luminous intensities for direction indicator lamps
5.6.2. Standard light distribution:
5.6.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part A or B of Annex 2, the intensity of the light emitted by each lamp sample shall must, in each direction corresponding to the points in the table of standard light distribution reproduced in:
  (a) Paragraph 2.1. of Annex 3 for categories 1, 1a, 1b, 2a, 2b, 11, 11a, 11b, 11c and 12.; or
  (b) Paragraph 2.4. of Annex 3 for category 6.
Be not less than the minimum specified in paragraph 5.6.1., multiplied by the percentage specified in the said table of the direction in question.
5.6.2.2. In divergence from paragraphs 4.8.3. and 4.8.3.1., for category 5 direction indicators, to the rear, a minimum value of 0.6 cd is required throughout the fields specified in Part B of Annex 2.
5.6.2.3. Throughout the fields defined in the diagrams in Part A of Annex 2, the luminous intensity of the light emitted shall be not less than 0.7 cd for lamps of category 1b, not less than 0.3 cd for lamps of categories 1, 1a, 2a, 6, 11, 11a, 11b, 11c, 12 and for those of category 2b by day; it shall not be less than 0.07 cd for lamps of category 2b by night.
5.6. TECHNICAL REQUIREMENTS CONCERNING DIRECTION-INDICATOR LAMPS (Symbols 1, 1a, 1b, 2a, 2b, 5, 6, 11, 11a, 11b, 11c, 12)
5.6.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 8 where the minimum luminous intensities shall be fulfilled:
  (a) In the case of direction indicators of categories 1, 1a, 1b, 2a, 2b, 11, 11a, 11b, 11c and 12 in the reference axis; or
  (b) in the case of direction indicators of categories 5 and 6 in direction A according to Annex 2.
Table 8: Luminous intensities for direction indicator lamps
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.6.
Existing Text
New Text
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
1 | 175 | 1000 | 500
1a | 250 | 1200 | 600
1b | 400 | 1200 | 600
2a (steady) | 50 | 500 | 250
2b (variable) | 50 | 1000 | 500
5 | 0.6 | 280 | 140
6 | 50 | 280 | 140
11 | 90 | 1000 | N.A.
11a | 175 | 1000 | N.A.
11b | 250 | 1200 | N.A.
11c | 400 | 1200 | N.A.
12 | 50 | 500 | N.A.
 | Minimum luminous intensity in HV (values in cd) | Maximum luminous intensity in any direction when used as (values in cd) | 
 |  | A single lamp | A lamp marked "D" (paragraph 3.3.2.5.2.)
1 | 175 | 1000 | 500
1a | 250 | 1200 | 600
1b | 400 | 1200 | 600
2a (steady) | 50 | 500 | 250
2b (variable) | 50 | 1000 | 500
5 | 0.6 | 280 | 140
6 | 50 | 280 | 140
11 | 90 | 1000 | N.A.
11a | 175 | 1000 | N.A.
11b | 250 | 1200 | N.A.
11c | 400 | 1200 | N.A.
12 | 50 | 500 | N.A.
Direction indicator lamps
GTBWGSL 426 Rev1

## Slide 8
5.6.3. Colour:
The colour of light emitted shall be amber. This requirement shall also apply within the range of variable luminous intensity produced by rear direction indicator lamps of category 2b.
5.6.4. Apparent surface:
No additional requirements.
5.6.5. Measurement:
5.6.5.1. In general, the intensities shall be measured with the light source(s) continuously alight.
However, depending on the construction of the lamp, for example, the use of light-emitting diodes (LED), or the need to take precautions to avoid overheating, it is allowed to measure the lamps in flashing mode.
  (a) This shall be achieved by switching with a frequency of f = 1.5 ± 0.5 Hz with the pulse width greater than 0.3 s, measured at 95 per cent peak light intensity. In all other cases the voltage as required in paragraph 4.7.1. shall be switched with a rise time and fall time shorter than 0.01 s; no overshoot is allowed;
  In the case of measurements taken in flashing mode the reported luminous intensity shall be represented by the maximum intensity.
5.6.5.2. In the case of lamps of category 2b the time that elapses between energizing the light source(s) and the light output measured on the reference axis to reach 90 per cent of the value measured in accordance with paragraph 5.6.2. shall be measured for the extreme levels of luminous intensity produced by the direction indicator. The time measured to obtain the lowest luminous intensity shall not exceed the time measured to obtain the highest luminous intensity.
5.6.5.3. For any direction indicator lamp except those equipped with filament light source(s), the luminous intensities measured after one minute and after 30 minutes of operation in flashing mode (f = 1.5 Hz, duty factor 50 per cent), shall comply with the minimum and maximum requirements. The luminous intensity distribution after one minute of operation can be calculated by applying at each test point the ratio of luminous intensity measured in HV after one minute and after 30 minutes of operation as above described.
5.6.2. Outside the reference axis the intensity of the light emitted by each lamp shall, in each direction corresponding to the points in the table of standard light distribution reproduced in:
  (a) Paragraph 2.1. of Annex 3 for categories 1, 1a, 1b, 2a, 2b, 11, 11a, 11b, 11c and 12.; or
  (b) Paragraph 2.4. of Annex 3 for category 6.
Be not less than the minimum specified in paragraph 5.6.1., multiplied by the percentage specified in the said table of the direction in question.
5.6.3. Failure provisions
For direction-indicator lamps of categories 1, 1a,1b, 2a, 2b, 11, 11a, 11b, 11c and 12 a signal for activation of the tell-tale prescribed in paragraph 6.5.8. of Regulation No. 48 or paragraph 6.3.8. of Regulation No. 53 shall be produced if (notwithstanding the provisions stated in paragraph 4.6.):
  (a) Any one light source has failed; or
  (b) In the case of a lamp designed for only two light sources, the intensity in the axis of reference is less than 50 per cent of the minimum intensity; or
  (c) As a consequence of a failure of one or more light sources, the intensity in one of the following directions as indicated in paragraph 2.1. of Annex 3, is less than the minimum intensity required:
    (i) H=0°, V=0°
    (ii) H=20° to the outside of the vehicle, V= +5°
    (iii) H=10° to the inside of the vehicle, V= 0°.
5.6.4. Test procedure:
In divergence from paragraphs 4.8.3. and 4.8.3.1., for category 5 direction indicators, to the rear, a minimum value of 0.6 cd is required throughout the fields specified in Part A of Annex 2;
5.6.5. Throughout the fields defined in the diagrams in Part A of Annex 2, the intensity of the light emitted shall be not less than 0.7 cd for lamps of category 1b, not less than 0.3 cd for lamps of categories 1, 1a, 2a, 11, 11a, 11b, 11c, 12 and for those of category 2b by day; it shall not be less than 0.07 cd for lamps of category 2b by night;
5.6.6. In general, the intensities shall be measured with the light source(s) continuously alight.
However, depending on the construction of the lamp, for example, the use of light-emitting diodes (LED), or the need to take precautions to avoid overheating, it is allowed to measure the lamps in flashing mode.
  (a) This shall be achieved by switching with a frequency of f = 1.5 ± 0.5 Hz with the pulse width greater than 0.3 s, measured at 95 per cent peak light intensity. In all other cases the voltage as required in paragraph 4.7.1. shall be switched with a rise time and fall time shorter than 0.01 s; no overshoot is allowed;
  (b) In the case of measurements taken in flashing mode the reported luminous intensity shall be represented by the maximum intensity.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.6. (cont‘d)
Existing Text
New Text
Agreed to delete this requirement, since it is self-evident, that the colour requirement is applicable to all categories of these lamps?
It is also not mentioned for variable stop lamps and rear fog lamps!
Agreed to delete this requirement, since it is redundant - identical to paragraph 4.8.8. !
For all other lamps, this requirement has not been duplicated in 5.6.x.
Agreed to delete this requirement, since it is redundant - This is already generally defined in paragraph 4.8.2.3.2.!
Direction indicator lamps
GTBWGSL 426 Rev1
!

## Slide 9
5.6.6. Other requirements:
5.6.6.1. For direction indicator lamps of categories 1, 1a, 1b, 2a or 2b the flash may be produced by sequential activation of their light sources if the following conditions are met:
  (a) Each light source, after its activation, shall remain lit until the end of the ON cycle;
  (b) The sequence of activation of the light sources shall produce a signal which proceeds in a uniform progressive manner from inboard towards the outboard edge of the light emitting surface;
  (c) It shall be one signal with no interruption and no vertical oscillations (e.g. not more than one change of direction along the vertical axis). The distance between two adjacent/tangential distinct parts of the light emitting surface of the sequential direction indicator shall not exceed 50mm, when measured perpendicularly to the reference axis, instead of the values defined in paragraph 5.7.2. of UN Regulation 48. These interruptions of the signal shall not create any overlap in the vertical axis between the different parts, from inboard towards the outboard of the vehicle, and shall not be used for any other lighting or light signalling functions;
  (d) The variation shall finish no more than 200ms after the beginning of the ON cycle;
  (e) The orthogonal projection of the light emitting surfaces of the direction indicator in the direction of the axis of reference shall be circumscribed by a rectangle on a plane normal to the axis of reference and having its longer sides parallel to the H-plane. The ratio of the horizontal to the vertical sides shall not be less than 1.7.
Compliance to the conditions mentioned above shall be verified in flashing mode.
5.6.6.2. The variable intensity control shall not generate signals which cause luminous intensities outside the range specified in paragraph 5.6.1. and exceeding the category 2a maximum specified in paragraph 5.6.1.:
  (a) For systems depending only on daytime and night time conditions: under night time conditions;
  (b) For other systems: under reference conditions as demonstrated by the manufacturer.
5.6.8. The variable intensity control shall not generate signals which cause luminous intensities outside the range specified in paragraph 5.6.1. and exceeding the category 2a maximum specified in paragraph 5.6.1.:
  (a) For systems depending only on daytime and night time conditions: under night time conditions;
  (b) For other systems: under reference conditions as demonstrated by the manufacturer.
5.6.9. The colour of the light emitted shall be amber. This requirement shall also apply within the range of variable luminous intensity produced by rear direction indicator lamps of category 2b.
5.6.10. For any direction indicator lamp except those equipped with filament light source(s), the luminous intensities measured after one minute and after 30 minutes of operation in flashing mode (f = 1.5 Hz, duty factor 50 per cent), shall comply with the minimum and maximum requirements. The luminous intensity distribution after one minute of operation can be calculated by applying at each test point the ratio of luminous intensity measured in HV after one minute and after 30 minutes of operation as above described.
5.6.11. For direction indicator lamps of categories 1, 1a, 1b, 2a or 2b the flash may be produced by sequential activation of their light sources if the following conditions are met:
  (a) Each light source, after its activation, shall remain lit until the end of the ON cycle;
  (b) The sequence of activation of the light sources shall produce a signal which proceeds in a uniform progressive manner from inboard towards the outboard edge of the light emitting surface;
  (c) It shall be one signal with no interruption and no vertical oscillations (e.g. not more than one change of direction along the vertical axis). The distance between two adjacent/tangential distinct parts of the light emitting surface of the sequential direction indicator shall not exceed 50mm, when measured perpendicularly to the reference axis, instead of the values defined in paragraph 5.7.2. of UN Regulation 48. These interruptions of the signal shall not create any overlap in the vertical axis between the different parts, from inboard towards the outboard of the vehicle, and shall not be used for any other lighting or light signalling functions;
  (d) The variation shall finish no more than 200ms after the beginning of the ON cycle;
  (e) The orthogonal projection of the light emitting surfaces of the direction indicator in the direction of the axis of reference shall be circumscribed by a rectangle on a plane normal to the axis of reference and having its longer sides parallel to the H-plane. The ratio of the horizontal to the vertical sides shall not be less than 1.7.
Compliance to the conditions mentioned above shall be verified in flashing mode.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.6. (cont‘d)
Existing Text
New Text
Agreed to delete this requirement, since it is redundant - This is already generally defined in paragraph 4.8.9. !
For most of the other lamps, this requirement has not been duplicated in 5.6.x.
Direction indicator lamps
GTBWGSL 426 Rev1
!

## Slide 10
[5.6.7. Failure provisions.
For direction-indicator lamps of categories 1, 1a,1b, 2a, 2b, 11, 11a, 11b, 11c and 12 a signal for activation of the tell-tale prescribed in paragraph 6.5.8. of Regulation No. 48 or paragraph 6.3.8. of Regulation No. 53 shall be produced if (notwithstanding the provisions stated in paragraph 4.6.):
  (a) Any one light source has failed; or
  (b) In the case of a lamp designed for only two light sources, the intensity in the axis of reference is less than 50 per cent of the minimum intensity; or
  (c) As a consequence of a failure of one or more light sources, the intensity in one of the following directions as indicated in paragraph 2.1. of Annex 3, is less than the minimum intensity required:
    (i) H=0°, V=0°
    (ii) H=20° to the outside of the vehicle, V= +5°
    (iii) H=10° to the inside of the vehicle, V= 0°.]
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.6. (cont‘d)
Existing Text
New Text
See comment on slide 2
Direction indicator lamps
?
GTBWGSL 426 Rev1

## Slide 11
5.7. Side marker lamps (SM1, SM2)
5.7.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 9.
Table 9: Luminous intensities for side marker lamps
5.7.2. Standard light distribution:
5.7.2.1. Outside the reference axis and within the angular fields defined in the diagrams in Part C of Annex 2, the intensity of the light emitted by each lamp sample supplied shall must:, in each direction corresponding to the points in the table of standard light distribution reproduced in paragraph 2.7. of Annex 3, be not less than the minimum specified in paragraph 5.7.1. multiplied by the percentage specified in the said table of the direction in question. In no direction within the space from which the side marker lamp is visible, exceed the maximum specified in paragraph 5.7.1..
5.7.2.2. In addition, for red side marker lamp, in the angular field from 60° to 90° in horizontal direction and ±20° in vertical direction towards the front of the vehicle, the maximum intensity is limited to 0.25 cd.
5.7.3. Colour:
The colour of the light emitted shall be amber. However, it can be red, if the rearmost side marker lamp is grouped or combined or reciprocally incorporated with the rear position lamp, the rear end-outline marker lamp, the rear fog lamp, the stop lamp, or is grouped with or has part of the light emitting surface in common with the rear retro-reflector.
5.7.4. Apparent surface:
No additional requirements.
5.7.5. Measurement:
No additional requirements.
5.7.6. Other requirements:
No additional requirements. For SM1 and SM2 categories of side marker lamps it may be sufficient to check only five points selected by the Type Approval Authority.
[5.7.7. Failure provisions:
See Par. 4.6.]
5.7. TECHNICAL REQUIREMENTS CONCERNING SIDE MARKER LAMPS (SYMBOLS SM1, SM2)
5.7.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 9.
Table 9: Luminous intensities for side marker lamps
In addition, for red side marker lamp, in the angular field from 60° to 90° in horizontal direction and ±20° in vertical direction towards the front of the vehicle, the maximum intensity is limited to 0.25 cd.
5.7.2. Outside the reference axis and within the angular fields defined in the diagrams in Part C of Annex 2, the intensity of the light emitted by each of the two side marker lamps supplied shall:
  (a) In each direction corresponding to the points in the light distribution table reproduced in paragraph 2.7. of Annex 3, be not less than the product of the minimum specified in paragraph 5.7.1. by the percentage specified in the said table for the direction in question;
  (b) In no direction within the space from which the side marker lamp is visible, exceed the maximum specified in paragraph 5.7.1..
5.7.3. For SM1 and SM2 categories of side marker lamps it may be sufficient to check only five points selected by the Type Approval Authority.
5.7.4. The colour of the light emitted shall be amber. However, it can be red, if the rearmost side marker lamp is grouped or combined or reciprocally incorporated with the rear position lamp, the rear end-outline marker lamp, the rear fog lamp, the stop lamp, or is grouped with or has part of the light emitting surface in common with the rear retro-reflector.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.7.
Existing Text
New Text
Side marker lamp of category |  | SM1 | SM2
Minimum intensity | In the axis of reference | 4.0 cd | 0.6 cd
 | Within the specified angular field, other than above | 0.6 cd | 0.6 cd
Maximum intensity | Within the specified angular field1 | 25.0 cd | 25.0 cd
Angular field | Horizontal | ±45 deg. | ±30 deg.
 | Vertical | ±10 deg. | ±10 deg.
Side marker lamp of category |  | SM1 | SM2
Minimum intensity | In the axis of reference | 4.0 cd | 0.6 cd
 | Within the specified angular field, other than above | 0.6 cd | 0.6 cd
Maximum intensity | Within the specified angular field1 | 25.0 cd | 25.0 cd
Angular field | Horizontal | ±45 deg. | ±30 deg.
 | Vertical | ±10 deg. | ±10 deg.
Agreed to delete last sentence, since it is redundant - identical to paragraph 4.8.3.2. !
Agreed to delete this requirement, since it is redundant - identical to paragraph 2.7.3., Annex 3 !
Side marker lamps
GTBWGSL 426 Rev1
!
See comment on slide 2

## Slide 12
5.8. Reversing lamps (AR)
5.8.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 10.
Table 10: Luminous intensities for reversing lamps
5.8.2. Standard light distribution:
5.8.2.1. In every other direction of measurement shown in paragraph 2.5. of Annex 3, the luminous intensity shall be not less than the minima specified in that annex.
5.8.2.2. However, in the case where the reversing lamp is intended to be installed on a vehicle exclusively in a pair of devices, the photometric intensity may be verified only up to an angle of 30° inwards where a photometric value of at least 25 cd shall be satisfied.
This condition shall be clearly explained in the application for approval and relating documents (see paragraph 3.1.).
Moreover, in the case where the type approval will be granted applying the condition above, a statement in paragraph 9.1.3. of the communication form (see Annex 1) will inform that the device shall only be installed in a pair.
5.8.3. Colour:
The colour of light emitted shall be white.
5.8.4. Apparent surface:
No additional requirements.
5.8.5. Measurement:
No additional requirements.
5.8.6. Other requirements:
No additional requirements.
[5.8.7. Failure provisions:
See Par. 4.6.]
5.8. TECHNICAL REQUIREMENTS CONCERNING REVERSING LAMPS (SYMBOLS AR)
5.8.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 10.
Table 10: Luminous intensities for reversing lamps
5.8.2. In every other direction of measurement shown in paragraph 2.5. of Annex 3, the luminous intensity shall be not less than the minima specified in that annex.
However, in the case where the reversing lamp is intended to be installed on a vehicle exclusively in a pair of devices, the photometric intensity may be verified only up to an angle of 30° inwards where a photometric value of at least 25 cd shall be satisfied.
This condition shall be clearly explained in the application for approval and relating documents (see paragraph 3.1.).
Moreover, in the case where the type approval will be granted applying the condition above, a statement in paragraph 9.1.3. of the communication form (see Annex 1) will inform that the device shall only be installed in a pair.
5.8.3 The colour of the light emitted shall be white.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.8.
Existing Text
New Text
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd) |  | 
 |  | in or above the h-plane | below the h-plane, down to 5°D | below 5°D
Reversing lamps | 80 | 300 | 600 | 8000
 | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd) |  | 
 |  | in or above the h-plane | below the h-plane, down to 5°D | below 5°D
Reversing lamps | 80 | 300 | 600 | 8000
Reversing lamps
GTBWGSL 426 Rev1
See comment on slide 2

## Slide 13
5.9. Rear fog lamps (F1, F2)
5.9.1. Luminous intensity:
The light emitted by each of the two lamps samples supplied shall meet the requirements in Table 11.
Table 11: Luminous intensities for rear fog lamps
5.9.2. Standard light distribution:
5.9.2.1. The minimum light intensity at all other points of standard light distribution is defined in paragraph 2.6. of Annex 3.
5.9.2.2. The variable intensity control shall not generate signals which cause luminous intensities outside the range specified in paragraph 5.9.1. and exceeding the category F1 maximum specified in paragraph 5.9.1.:
  (a) For systems depending only on daytime and night time conditions: under night time conditions;
  (b) For other systems: under standard conditions
5.9.3. Colour:
The colour of light emitted shall be red.
5.9.4. Apparent surface:
The apparent surface in the direction of the reference axis shall not exceed 140 cm2.
5.9.5. Measurement:
No additional requirements.
5.9.6. Other requirements:
The rear fog lamp shall be subjected to the heat resistance test specified in Annex 6.
[5.9.7. Failure provisions:
See Par. 4.6.]
5.9 TECHNICAL REQUIREMENTS CONCERNING REAR FOG LAMPS (SYMBOLS F1, F2)
5.9.1. The light emitted by each of the two lamps supplied shall meet the requirements in Table 11.
Table 11: Luminous intensities for rear fog lamps
5.9.2. The minimum light intensity at all other points of standard light distribution is defined in paragraph 2.6. of Annex 3
5.9.3. The variable intensity control shall not generate signals which cause luminous intensities outside the range specified in paragraph 5.9.1. and exceeding the category F1 maximum specified in paragraph 5.9.1.:
  (a) For systems depending only on daytime and night time conditions: under night time conditions;
  (b) For other systems: under standard conditions
5.9.4. The apparent surface in the direction of the reference axis shall not exceed 140 cm2.
5.9.5. The colour of the light emitted shall be red.
5.9.6. The rear fog lamp shall be subjected to the test specified in Annex 6.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.9.
Existing Text
New Text
Rear fog lamps of category | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
F1 (steady) | 150 | 300
F2 (variable) | 150 | 840
Rear fog lamps of category | Minimum luminous intensity in H-V (values in cd) | Maximum luminous intensity in any direction (values in cd)
F1 (steady) | 150 | 300
F2 (variable) | 150 | 840
Rear fog lamps
GTBWGSL 426 Rev1
Agreed to delete this requirement, since it is redundant - This is already generally defined in paragraph 4.8.9. !
For most of the other lamps, this requirement has not been duplicated in 5.6.x.
!
See comment on slide 2

## Slide 14
5.10. Manoeuvring lamps (ML)
5.10.1. Luminous intensity:
The intensity of light emitted shall not exceed 500 cd in all directions in which the light can be observed, when installed in any mounting position specified by the applicant.
5.10.2. Standard light distribution:
The lamp must be so designed that the light emitted directly towards the side, the front or the rear of the vehicle does not exceed 0.5 cd within the angular field as defined below.
  (a) The vertical minimum angle φmin (in degrees) is:
  φmin = arctan (1-h)/10; where h is mounting height in m
  (b) The vertical maximum angle φmax (in degrees) is: φmax = φmin + 11.3
The measurement shall be limited to a horizontal angle ranging from +90° to -90° with respect to the line which cuts the reference axis and which is perpendicular to the vertical longitudinal plane of the vehicle.
5.10.3. Colour:
The colour of light emitted shall be white.
5.10.4. Apparent surface:
No additional requirements.
5.10.5. Measurement:
The measurement distance shall be 3.0 m minimum.
5.10.6. Other requirements:
No additional requirements.
[5.10.7. Failure provisions:
No additional requirements]
5.10. TECHNICAL REQUIREMENTS CONCERNING MANOEUVRING LAMPS (SYMBOLS ML)
5.10.1. The intensity of light emitted shall not exceed 500 cd in all directions in which the light can be observed, when installed in any mounting position specified by the applicant.
5.10.2. The lamp must be so designed that the light emitted directly towards the side, the front or the rear of the vehicle does not exceed 0.5 cd within the angular field as defined below.
  (a) The vertical minimum angle φmin (in degrees) is:
  φmin = arctan (1-mounting height)/10; where h is mounting height in m
  (b) The vertical maximum angle φmax (in degrees) is: φmax = φmin + 11.3
The measurement shall be limited to a horizontal angle ranging from +90° to -90° with respect to the line which cuts the reference axis and which is perpendicular to the vertical longitudinal plane of the vehicle.
The measurement distance shall be 3.0 m minimum.
5.10.3. The colour of the light emitted shall be white.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.10.
Existing Text
New Text
Manoeuvring lamps
GTBWGSL 426 Rev1
See comment on slide 2

## Slide 15
5.11. Rear registration plate illuminating lamps (L, LM1)
5.11.1. Luminous intensity:
??? Not applicable ???
5.11.2. Photometric characteristics:
At each of the points of measurement shown in paragraph 3. of Annex 3, the luminance B shall be at least
  (a) For categories 1a, 1b, 1c, 2a and 2b equal to 2.5 cd/m2;
  (b) For categories 1 and 2 equal to 2.0 cd/m².
The gradient of the luminance between the values B1 and B2, measured at any two points 1 and 2 selected from among those mentioned above, shall not exceed 2 x Bo/cm, Bo being the minimum luminance measured at the various points, i.e.:
5.11.3. Colour:
The colour of the light emitted shall be sufficiently colourless not to cause any appreciable change in the colour of the registration plate.
5.11.4. Apparent surface:
No additional requirements.
5.11.5. Measurement:
The luminance measurements shall be made on a diffuse colourless surface with known diffuse reflection factor . The diffuse colourless surface shall have the dimensions of the registration plate or the dimension exceeding one measuring point. Its centre shall be placed in the centre of the positions of the measuring points.
This (These) diffuse colourless surface(s) shall be placed in the position normally occupied by the registration plate and 2 mm in front of its holder.
Luminance measurements shall be made perpendicularly to the surface of the diffuse colourless surface with the tolerance of 5° in each direction at the points shown in paragraph 3. of Annex 3, each point representing a circular area of 25 mm in diameter. The measured luminance shall be corrected for the diffuse reflection factor 1.0.
5.11. TECHNICAL REQUIREMENTS CONCERNING REAR-REGISTRATION PLATE ILLUMINATING LAMPS (SYMBOL L, LM1)
5.11.1. The devices for the illumination of rear-registration plates of categories 1a, 1b, 1c, 2a and 2b shall be so constructed that the whole surface of the plate will be visible within the angles given in Part D of Annex 2.
5.11.2. Measuring procedure
The luminance measurements shall be made on a diffuse colourless surface with known diffuse reflection factor . The diffuse colourless surface shall have the dimensions of the registration plate or the dimension exceeding one measuring point. Its centre shall be placed in the centre of the positions of the measuring points.
This (These) diffuse colourless surface(s) shall be placed in the position normally occupied by the registration plate and 2 mm in front of its holder.
Luminance measurements shall be made perpendicularly to the surface of the diffuse colourless surface with the tolerance of 5° in each direction at the points shown in paragraph 3. of Annex 3, each point representing a circular area of 25 mm in diameter. The measured luminance shall be corrected for the diffuse reflection factor 1.0.
5.11.3. Photometric characteristics
At each of the points of measurement shown in paragraph 3. of Annex 3, the luminance B shall be at least
  (a) For categories 1a, 1b, 1c, 2a and 2b equal to 2.5 cd/m2;
  (b) For categories 1 and 2 equal to 2.0 cd/m².
The gradient of the luminance between the values B1 and B2, measured at any two points 1 and 2 selected from among those mentioned above, shall not exceed 2 x Bo/cm, Bo being the minimum luminance measured at the various points, i.e.:
5.11.4. The colour of the light emitted shall be sufficiently colourless not to cause any appreciable change in the colour of the registration plate.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.11.
Existing Text
New Text
Rear registration plate illuminating lamps
?
What to write here?
„Not applicable“ or „No additional requirements“ ?
GTBWGSL 426 Rev1

## Slide 16
5.11.6. Other requirements:
5.11.6.1. The devices for the illumination of rear-registration plates of categories 1a, 1b, 1c, 2a and 2b shall be so constructed that the whole surface of the plate will be visible within the angles given in Part D of Annex 2.
5.11.6.2. Incidence of the light
The manufacturer of the illuminating device shall specify one or more or a field of positions in which the device is to be fitted in relation to the space for the registration plate; when the lamp is placed in the position(s) specified by the manufacturer the angle of incidence of the light on the surface of the plate does not exceed 82° at any point on the surface to be illuminated, this angle being measured from the extremity of the device's illuminating area which is furthest from the surface of the plate. If there is more than one illuminating device, the foregoing requirement shall apply only to that part of the plate intended to be illuminated by the device concerned.
When the device has one outer edge of the illuminating surface that is parallel to the surface of the registration plate, the extremity of the illuminating surface of the device which is furthest from the surface of the plate is the middle point of the edge of the illuminating surface, which is parallel to the plate and is furthest from the surface of the plate.
The device must be so designed that no light is emitted directly towards the rear, with the exception of red light if the device is combined or grouped with a rear lamp.
[5.11.7. Failure provisions:
See Par. 4.6.]
5.11.5. Incidence of the light
The manufacturer of the illuminating device shall specify one or more or a field of positions in which the device is to be fitted in relation to the space for the registration plate; when the lamp is placed in the position(s) specified by the manufacturer the angle of incidence of the light on the surface of the plate does not exceed 82° at any point on the surface to be illuminated, this angle being measured from the extremity of the device's illuminating area which is furthest from the surface of the plate. If there is more than one illuminating device, the foregoing requirement shall apply only to that part of the plate intended to be illuminated by the device concerned.
When the device has one outer edge of the illuminating surface that is parallel to the surface of the registration plate, the extremity of the illuminating surface of the device which is furthest from the surface of the plate is the middle point of the edge of the illuminating surface, which is parallel to the plate and is furthest from the surface of the plate.
The device must be so designed that no light is emitted directly towards the rear, with the exception of red light if the device is combined or grouped with a rear lamp.
Regulation No. 148 [LSD] – Stage II
Draft Proposal Part 5. – Par. 5.11. (cont‘d)
Existing Text
New Text
Rear registration plate illuminating lamps
GTBWGSL 426 Rev1
See comment on slide 2