## Slide 1: WLTP IWG 28th Session 23rd – 27th September 2019 Status Report from UNR WLTP Transposition Task Force
WLTP-28-03e

## Slide 2: Post-27th WLTP IWG Update
  Transposition Task Force WebEx meetings held on: 20th June; 7th August; and 5th September 2019:
  Review and discussions on regulatory texts
  Topics under discussion included, amongst others:
    Scope of UNR WLTP (L1a, L1b, L2)
    FAME content of diesel reference fuel
    Minimum deltas in interpolation method
    Dual-axis dyno vehicle restraint
    Requirements relating to mono-fuel gas vehicles
    Durability (see separate report)
    CoP – NB: not discussed in Transposition Task Force but in parallel CoP Task Force (see separate report)
    Potential for inclusion of OBD in UNR WLTP

## Slide 3: 28th WLTP IWG and beyond
28th WLTP IWG
  Further discussions on harmonisation, including Durability and COP + review of draft regulatory texts
  Aim is to resolve all outstanding items at the 28th IWG
Additional meetings for final drafting to be arranged for October
Submission of Working Documents by 21st October
Latest drafts of UNR texts uploaded to UNECE Wiki:
https://wiki.unece.org/display/trans/08+-+Draft+UNR+texts+for+28th+IWG+-+Bern%2C+Septmber+2019

## Slide 4: Working Documents for 80th GRPE
UNR WLTP 00 Series
  Level 1a (Europe regional option)
  Level 1b (Japan regional option)
UNR WLTP 01 Series
  Level 2 (Top level requiring mutual recognition)
UNR 83 08 Series
  Will require a demonstration of approval to UNR WLTP so that the Type 1, Type 4 and Type 5 are covered
  RDE will now be in a separate ‘UNR RDE’ and not UNR 83 08 series

## Slide 5: Summary of outstanding issues for UNR WLTP
The following slides provide a summary of the status and main open points for each of the sections that make up the new UNR WLTP
The slides were prepared to help inform discussions at the Transposition Task Force meeting on 5th September 2019 – and beyond. More detailed slides for each section will be prepared during the IWG week to help inform the discussions.
In all the elements further drafting will be required to prepare the UNR WLTP for Level 1a and Level 1b (to include distinguishing where the levels differ) and the separate document to cover Level 2.
  The preparation (and separation) of the L1a/b and L2 documents will be undertaken once all the main elements are finalised – in order to avoid having to update two separate regulatory texts as amendments come forward for inclusion
Rob Gardner, Transposition Task Force Leader, September 2019

## Slide 6: UNR WLTP - Main Body and Appendices
Section 1: Scope
L1a – same scope as EU-WLTP
L1b – same scope as GTR15
Level 2 - TBD
Section 9: Conformity of Production
Pending CoP Task Force decisions
Appendix 1: Verification of conformity of production for Type 1 test—statistical method
Pending CoP Task Force decisions
Appendix 2: Requirements for vehicles that use a reagent for the exhaust after-treatment system
Option relating to ‘performance restriction’ - TBD
Section 2: Abbreviations
Section 2 is usually ‘Definitions’ but here they are included in Section 3 to enable the GTR15 definition references to be maintained.
Section 3: Definitions
Sort out numbering for ‘generic’ definitions – to avoid overlap with GTR15 definition numbering
Confirm location for EVAP definitions – due to overlap of numbering with GTR15 definitions
Optional equipment definition – JPN vs. EU
Section 4: Application for approval
Combine UNR83 and UNR101 text
Section 5: Approval
Approval numbering and marking system to be developed
Section 6: Specifications and tests
Fuel filler cap requirement – TBD
Deter odometer reprogramming – TBD
Family definition and identifier – further clarification text required
Mono-fuel gas vehicles - 15 litre petrol exemption for Type 1(?) and Type 4(?) test – TBD
Type 5 text - pending decision from durability discussions
OBD?
Section 7: Modification of vehicle type
Copy and paste UNR83, with some minor amendments
Section 8: Extensions to type approvals
To be developed. Pending decision from durability family definition discussions.
Section 10: Penalties for non-conformity of production
Copy and paste UNR83, with some minor amendments
Section 11: Production definitively discontinued
Copy and paste UNR83
Section 12: Introductory provisions
To be developed
Section 13: Names and addresses of Technical Services …
Copy and paste UNR83





## Slide 7: UNR WLTP – Annexes Part A
Annex A1
Engine and vehicle characteristics and information concerning the conduct of tests
Under development – Appendix 3 to Annex I of EU WLTP acts as basis
Appendix 1 to Annex A1
WLTP Test Report
Under development – Appendix 8a to Annex I of EU WLTP acts as basis
Appendix 2 to Annex A1
WLTP Road Load Test Report
Under development – Appendix 8b to Annex I of EU WLTP acts as basis
Appendix 3 to Annex A1
WLTP Test Sheet
Under development – Appendix 8c to Annex I of EU WLTP acts as basis
Appendix 4 to Annex A1
Evaporative emissions Test Report
Under development – Appendix 8d to Annex I of EU WLTP acts as basis
Annex A2
Communication
Under development – Appendix 4 to Annex I of EU WLTP acts as basis
Annex A2 Addendum
Addendum to type approval communication
Under development – Addendum in Appendix 4 to Annex I of EU WLTP acts as basis
Annex A2 Addendum
Addendum to type approval communication
Under development – Addendum in Appendix 4 to Annex I of EU WLTP acts as basis
Annex A3 Arrangements of the approval mark
To be developed – based on standard UNR format
Annex A2 Appendix1 and Appendix 2
OBD communications – from UNR83 07?

## Slide 8: UNR WLTP – Annexes Part B
Annex B1: WLTC
Post-Amendment 5 modifications from Gear Shift Task Force incorporated
Annex B2: Gear selection and shift point determination for vehicles equipped with manual transmissions
Post-Amendment 5 modifications from Gear Shift Task Force incorporated
Annex B3: Reference Fuels
Diesel reference fuel FAME content - TBD
Annex B4: Road load and dynamometer setting
4.1.1.2. Atmospheric temperature range – TBD
4.2.1.1.2. Using an interpolation method – “As a guidance” – TBD
4.2.2.1. – GTR15 Classes 1-6 vs. EU WLTP Classes A-G.
Section 7 – add requirements for vehicle restraint on dual-axis dyno
Annex B5: Test equipment and calibrations
2.3. align with EU-WLTP for dual-axis dyno requirements. Add JPN proposal for new sentence in 2.3.1.2. – from WLTP-26-15 (Zagreb)
3.3.6.4.3. (c) UFM type CVS – update response time?
General note: Annex B5 includes a lot of descriptive/informative text (i.e. not regulatory text) – does this need to be Addressed?
Annex B6: Type 1 test procedures and test conditions
1.2.3.3. final sentence - not it EU WLTP, is it needed in UNR?
2.6.3.2. additional text on dual-axis dyno from EU-WLTP – TBD
2.6.8.3.2. and 2.8.6. – text from EU-WLTP – TBD
Appendix 1 para 3.1.1. – EU-WLTP amendment – TBD
App 2 Table A6.App2/1 – add LPG and NG (or x-ref to relevant ISO).
Annex B7: Calculations
Table A7/1 – EU–WLTP updates and L1b updates – TBD
3.2.1.1.1. – check Amnd 5 update was correct for definition (i.e. Ci)
3.2.1.1.4. – Les Hill corrections from WLTP-26-05e incorporated
3.2.3.2.2.3.2. – JPN to propose update to remove CFD method for L1b & L2
5. Amendment provided by GSTF incorporated
7.1. change ‘engine control unit’ to ‘electronic control unit’
Annex B8: PEV, HEV and FCHV
General clarification updates proposed in SG-EV - TBD
CoP specific updates proposed by SG-EV, including a new Appendix 8 - pending CoP Task Force decisions
Annex B9: Determination of method equivalency
JPN proposal to exclude for L1b and L2

## Slide 9: UNR WLTP – Annexes Part C
Annex C1 – Reserved
Reserved for Type 2 test
Annex C4 – Type 5 test (Durability)
Document under development – pending decisions from discussions held in the Durability Task force and in the Transposition
Annex C3 – Type 4 test (Evaporative Emissions)
Potential restructure proposed in order to allow the Evap specific definitions to be included in Annex C3 rather than the Main Body – to overcome numbering conflict between GTR15 and GTR19 definitions – TBD
GTR19 x-refs to UNR83 07 series replaced with the actual requirements.
Query as to how to incorporate the UNR83 07 x-ref provided in Appendix 1 para 6.5.5.2. (Carbon canister loading)
Should GTR19 have also provided a x-ref to para 4 of Appendix 1 to Annex 7 of UNR83 07 – which covers the Calibration of the hydrocarbon analyser?
Annex C2 – Reserved
Reserved for Type 3 test
Annex Cx – OBD?

## Slide 10
Contact information
Rob Gardner, TRL Ltd on behalf of the European Commission (Task Force Leader)
rgardner@trl.co.uk