## Slide 1: WLTP Proposals
06.08.2019
Christoph Lueginger
BMW AG
IWG #28
Bern

## Slide 2: 1) Drive Modes

## Slide 3
Drive Modes: Worst case within those last-function modes
2.6.6. Driver-selectable modes
2.6.6.1. Vehicles equipped with a predominant mode shall be tested in that mode. At the request of the manufacturer, the vehicle may alternatively be tested with the driver-selectable mode in the worst-case position for CO2 emissions.
[...]
2.6.6.3. If the vehicle has no predominant mode or the requested predominant mode is not agreed by the responsible authority as being a predominant mode, the vehicle shall be tested in the best case mode and worst case mode for criteria emissions, CO2 emissions, and fuel consumption. Best and worst case modes shall be identified by the evidence provided on the CO2 emissions and fuel consumption in all modes. CO2 emissions and fuel consumption shall be the arithmetic average of the test results in both modes. Test results for both modes shall be recorded.
At the request of the manufacturer, the vehicle may alternatively be tested with the driver-selectable mode in the worst case position for CO2 emissions.
ECO
COMFORT
SPORT
Lower CO2
Higher CO2
Predominant CO2 during Type1-test
Predominant Mode
ECO
COMFORT
SPORT
Lower CO2
Higher CO2 during
Type1-test
Basic CO2
Both, ECO or COMFORT, can be configured as vehicle start mode.
Case 1 – predominant mode available
Case 2 – no predominant mode available but not all to be configured
Not selectable as fixed mode for vehicle start.
Although the manufacturer provides a more CO2-saving mode to be a fixed mode for vehicle start, it would lead to the effect, that a mode would have to be tested (or two modes in case of best and worst case) that delivers the highest CO2 but can not be selected as fixed vehicle start mode.

## Slide 4
Drive Modes: Worst case within those last-function modes
2.6.6. Driver-selectable modes
2.6.6.1. Vehicles equipped with a predominant mode shall be tested in that mode. At the request of the manufacturer, the vehicle may alternatively be tested with the driver-selectable mode in the worst-case position for CO2 emissions.
[...]
2.6.6.3. If the vehicle has no predominant mode or the requested predominant mode is not agreed by the responsible authority as being a predominant mode, the vehicle shall be tested in the best case mode and worst case mode for criteria emissions, CO2 emissions, and fuel consumption. Best and worst case modes shall be identified by the evidence provided on the CO2 emissions and fuel consumption in all modes. CO2 emissions and fuel consumption shall be the arithmetic average of the test results in both modes. Test results for both modes shall be recorded.
At the request of the manufacturer, the vehicle may alternatively be tested with the driver-selectable mode in the worst case position for CO2 emissions.
2.6.6.x. If the vehicle has no predominant mode because the mode that is selected when the vehicle is switched on can be redefined, the worst case mode for criteria emissions, CO2 emissions, and fuel consumption within those driver-selectable modes shall be tested which are able to be set to as mode that is used when the vehicle is switched on. Other driver-selectable modes that are not able to be set as mode that is used when the vehicle is switched on, shall not be in scope.
ECO
COMFORT
SPORT
Lower CO2
Higher CO2
CO2 for Type1-test because worst case mode within those that are selectable.
Both, ECO or COMFORT, can be configured as vehicle start mode.
Not selectable as fixed mode for vehicle start.
ECO
COMFORT
SPORT
Lower CO2
Higher CO2 during
Type1-test
Basic CO2
Both, ECO or COMFORT, can be configured as vehicle start mode.
Case 2 – no predominant mode available but not all to be configured
Not selectable as fixed mode for vehicle start.

## Slide 5: 2a) Minimum Deltas – technical change.

## Slide 6
WLTP GTR Annex 4 – road load Improve definition regarding Guidance Minimum-Deltas
The purpose of the "minimum deltas" for the road load parameters is to get a sufficiently high delta between Low and High to avoid errors in the interpolation. If L and H come too close to each other, the interpolation will be inaccurate.
The important point is, to have a sufficient high difference in the physical parameters, but even more in the interpolated road load parameters f0, f2 and test mass.
As the test mass also influences the f0 value, this provision can be improved to cover a wider range of vehicle configurations. Further explanation: The added 70 kg of mass are delivering approximately the same f0-delta than a RR of 0.5 kg/t.
Current text
Last part in paragraph 4.2.1.1.2. of Annex 4:
…
As a guidance, the following minimum deltas between vehicles H and L should be fulfilled for that road load relevant characteristic:
(i) Mass of at least 30 kg;
(ii) Rolling resistance of at least 1.0 kg/tonne;
(iii) Aerodynamic drag (CD × Af) of at least 0.05 m².
New text:
Last part in paragraph 4.2.1.1.2. of Annex 4:
…
As a guidance, the following minimum deltas between vehicles H and L are recommended to be fulfilled for that road load relevant characteristic:
(i) Mass of at least 30 kg;
(ii) Rolling resistance of at least 1.0 kg/tonne; in case of RR between 0 and 1.0, the minimum of the mass delta is replaced with 100 kg instead of 30 kg;
(iii) Aerodynamic drag (CD × Af) of at least 0.05 m².

## Slide 7: 2b) Minimum Deltas – requirement?

## Slide 8
WLTP GTR Annex 4 – road load Change Guidance to requirement
ACEA wants to start the discussion, to transfer that guidance into a requirement.
Pros/cons: + Minimum deltas significantly reduce the risk of problems in case of extrapolation of parameters. + New regulations are introduced for new approvals with a reasonable lead time, so adding this as a requirement should not affect current and valid approvals. - Not checked if small families run into troubles  OICA members kindly asked to check and provide examples.
Possible options: Leave as a guidance | optional / authority request | mandatory in any case.
Current text
Last part in paragraph 4.2.1.1.2. of Annex 4:
…
As a guidance, the following minimum deltas between vehicles H and L should be fulfilled for that road load relevant characteristic:
New text:
Last part in paragraph 4.2.1.1.2. of Annex 4:
…
As a guidance, tThe following minimum deltas between vehicles H and L are recommended to shall be fulfilled for that road load relevant characteristic. At the request of the manufacturer and upon approval by the responsible authority these minimum criteria can be waived.

## Slide 9: 3) New functions in conjunction with chassis dyno testing

## Slide 10
WLTP GTR Annex 6 – chassis dyno mode Clarify situation with recent vehicle technologies
Vehicle Technology | Behaviour on road | Behaviour on chassis dyno in the lab
Emergency Brake assist (detects an obstacle in front) | Vehicle brakes in case of emergency situation. | Vehicle would brake always, due to cooling fan in the front  unwanted.  deactivate function via vehicle’s dynamometer operation mode.
Coasting (decouple engine in order to preserve the kinetic energy) | Vehicle is coasting in case of free road and no braking. | The drive trace has to be followed, so the vehicle may coast for very short periods, which is a disadvantage compared to real life and will undermine the measurement repeatability (strong dependency on driver)  unwanted.  deactivate coasting via vehicle’s dynamometer operation mode.
Using environmental data (e.g. for the purpose of deciding coasting, gear shifting, etc.) | Vehicle optimizes energy consumption depending on environmental data. | Vehicle has no environmental data available. Behaviour unknown, maybe unrepresentative, maybe better or worse in terms of CO2.  unwanted.  What is the driving situation of a WLTP: Free road or traffic or…?
Autonomous driving | Vehicle may drive (partially) autonomous, maybe limited to specific areas or roads or on demand of the driver. | Vehicle cannot drive autonomously. One could deactivate all sensors as they cannot work and save CO2. Otherwise, activating all systems may significantly increase CO2. No equal treatment ensured  unwanted.  Should that contribution be included in the Type I test?
This list are examples to demonstrate the need for a clear guidance. As a starting point, the guidance should go into the direction to come as closely as possible towards on road driving, considering also regulatory systems in Europe like "Eco-Innovations".

()
(?)
(?)

## Slide 11
Clarify situation with recent vehicle technologies Text proposal
New text (in blue), paragraph 2.4.2. of Annex 6:
2.4.2. Dynamometer operation
2.4.2.1. Auxiliary devices shall be switched off or deactivated during dynamometer operation unless their operation is required by regional legislation.
2.4.2.2. The vehicle’s dynamometer operation mode, if any, shall be activated by using the manufacturer's instruction (e.g. using vehicle steering wheel buttons in a special sequence, using the manufacturer’s workshop tester, removing a fuse).
The manufacturer shall provide the responsible authority a list of the deactivated devices and justification for the deactivation. The dynamometer operation mode shall be approved by the responsible authority and the use of a dynamometer operation mode shall be recorded.
2.4.2.3. The vehicle’s dynamometer operation mode shall not activate, modulate, delay or deactivate the operation of any part that affects the emissions and fuel consumption under the test conditions. Any device that affects the operation on a chassis dynamometer shall be set to ensure a proper operation.
2.4.2.4. If the vehicle is equipped with a coasting functionality, this functionality may be deactivated by the vehicle’s dynamometer operation mode.
Does the term "coasting" needs a definition?
Starting Note for another new paragraph 2.4.2.5.:
IWG should start dealing with functions for highly automated driving, how they are treated on the dyno and the interdependence with concepts like eco-innovations.