## Slide 1: Annex 6 (ICE Vehicles)
3.4.2. The correction shall be applied if ΔEREESS is negative (corresponding to REESS discharging) and the correction criterion, c, calculated according to paragraph 3.4.1. of this appendix is greater than the applicable threshold according to Table A6.App2/2.
3.4.3. The correction shall be omitted and uncorrected values shall be used if the correction criterion c calculated according to paragraph 3.4.1. of this appendix is less than the applicable threshold according to Table A6.App2/2.
3.4.4. The correction may be omitted and uncorrected values may be used if:
(a) ΔEREESS is positive (corresponding to REESS charging) and the correction criterion c calculated according to paragraph 3.4.1. of this appendix is greater than the applicable threshold according to Table A6.App2/2;
(b) the manufacturer can prove to the responsible authority by measurement that there is no relation between ΔEREESS and CO2 mass emission and ΔEREESS and fuel consumption respectively.

## Slide 2: Annex 8 (Electrified Vehicles)
1.1.3. The correction shall be applied if ΔEREESS,CS is negative which corresponds to REESS discharging and the correction criterion c calculated in paragraph 1.2. of this appendix is greater than the applicable threshold according to Table A8.App2/1.
1.1.4. The correction may be omitted and uncorrected values may be used if:
(a) ΔEREESS,CS is positive which corresponds to REESS charging and the correction criterion c calculated in paragraph 1.2. of this appendix is greater than the applicable threshold according to Table A8.App2/1;
(b) The correction criterion c calculated in paragraph 1.2. of this appendix is smaller than the applicable threshold according to Table A8.App2/1;
(c) The manufacturer can prove to the responsible authority by measurement that there is no relation between ΔEREESS,CS and charge-sustaining CO2 mass emission and ΔEREESS,CS and fuel consumption respectively.

## Slide 3: Update: REESS CO2 mass emission – Sub-Annex 6 Appendix 2
Voluntary CO2 correction at request by the manufacturer
  At the request of the manufacturer it should be possible that the resulting CO2 mass correction could be applied, even though the calculated RCB correction criteria ‘c’ is higher or lower then the thresholds (e.g. c = 0,5%).
Example for testing ATCT – Family-Correction-Factor (FCF):
causes unnecessary error for the FCF within the ATCT-family
the FCF is trustworthier due to RCB-corrected individual results of Type-1 and ATC-Test
Type-1-Test
REESS charging
resulting criteria
c = |0,45 %|
CO2 impact
-1,8 g/km
ATCT
REESS discharging
resulting criteria
c = |-0,39 %|
CO2 impact
1,6 g/km
normally no CO2 correction
FCF = 100 g/km / 95 g/km = 1,053
Type-1-Test
REESS charging
resulting criteria
c = |0,45 %|
CO2 impact
-1,8 g/km
ATCT
REESS discharging
resulting criteria
c = |-0,39 %|
CO2 impact
1,6 g/km
CO2 correction at request by manufacturer
FCF = 101,6 g/km / 93,2 g/km = 1,090
7
ü
1
2
!
1
2

## Slide 4: Annex 6 (ICE Vehicles) - Proposal
3.4.2. The correction shall be applied if ΔEREESS is negative (corresponding to REESS discharging) and the correction criterion, c, calculated according to paragraph 3.4.1. of this appendix is greater than the applicable threshold according to Table A6.App2/2.
3.4.3. The correction shall be omitted and uncorrected values shall be used if the correction criterion c calculated according to paragraph 3.4.1. of this appendix is less than the applicable threshold according to Table A6.App2/2.
3.4.4. At the request of the manufacturer, the correction may be omitted and uncorrected values may be used if:
(a) ΔEREESS is positive (corresponding to REESS charging) and the correction criterion c calculated according to paragraph 3.4.1. of this appendix is greater than the applicable threshold according to Table A6.App2/2;
(b) the manufacturer can prove to the responsible authority by measurement that there is no relation between ΔEREESS and CO2 mass emission and ΔEREESS and fuel consumption respectively.