## Slide 1: EVE Update
WLTP Session #28
Bern, Switzerland
EVE - IWG
WLTP-28-18e

## Slide 2: EVE Update – WLTP #28
Power Determination Status
Electrified Vehicle Durability Topics
  Background
  Objectives
  Durability Requirements
  Next steps
WLTP-28-18e

## Slide 3: Status of power determination GTR
History
  Second mandate of the EVE IWG was approved in November 2014
  WLTP had stated a clear demand for an improved procedure to determine system power of HEVs (for classification and downscaling)
  Part B of the mandate therefore included a task to develop an Annex to GTR No. 15 for system power determination
  EVE consulted with several organizations doing similar work (SAE, ISO, KATRI)
  ISO 20762 was selected as basis for power determination procedure
  Drafting group was formed to convert ISO 20762 into an Annex to GTR No. 15
  Later, contracting parties stated a preference for a standalone GTR.
WLTP-28-18e

## Slide 4: Status of power determination GTR
Drafting group drafted procedure based on ISO 20762 in 2017-2018
Validation testing was conducted in 2018
Significant differences seen between TP1 and TP2
IWG proposed additional testing, and extension of schedule
Proposed schedule:
  June 2019: Approval of authorization by GRPE to extend timeline
  October 2019: Completion of testing, review of results, and draft GTR changes
  November 2019: Approval of new timelines in formal document by AC.3
  January 2020: Preliminary draft of GTR text to be available
  June 2020: Recommendation of draft GTR by GRPE
  November 2020: Establishment of the GTR by AC.3 in Global Registry
WLTP-28-18e

## Slide 5: Status of power determination GTR
Drafting group: “Determination of Electrified Vehicle Power” (DEVP)
Recent meetings:
  DEVP #8: At EVE 30 in Stockholm (April 2019)
  DEVP #9: At EVE 31 in Geneva (May 2019)
  DEVP #10: Teleconference (planned)
Limited opportunity for drafting during Summer 2019
  Open issues were identified at EVE 30/31 (not simple drafting issues)
  Several revisions to the procedure were proposed
  Draft text developed
Revisions will be evaluated via validation program Phase 2 (in progress)
WLTP-28-18e

## Slide 6: Status of power determination GTR
Recent progress
  JRC and Environment Canada are testing additional vehicles
  Draft of technical report completed and circulated to drafting group
    Nature of power determination problem, and approaches considered
    Analysis of open issues
    Results of validation testing (forthcoming)
    Differences from ISO 20762 and their justification
Next steps
  Validation testing to be completed by October
  Technical report and test results will be discussed at EVE 32 (Brussels)
  Will seek consensus on open technical issues at EVE 32
WLTP-28-18e

## Slide 7: Electrified Vehicle Durability Background
GRPE has tentatively approved a new mandate for the EVE to develop a GTR for electrified vehicle durability
Overall support for the GTR is mixed and the exact timing is not yet determined
  European Commission wants the GTR completed as soon as possible
  Japan will provide their position at the EVE meeting in Brussels next month
EVE IWG has done considerable research and is prepared to propose several alternatives
WLTP-28-18e

## Slide 8: EVE Conclusions Regarding Durability
Every manufacturer is currently performing some type of battery durability for their electrified vehicles
All manufacturers are assessing durability differently
  … but, they are looking at the same parameters
    Calendar aging
    Discharge rates
    Charging frequency and rates
    Temperature exposure
However, the electrified vehicle market is still developing and customer usage profiles are changing with vehicle technologies and infrastructure.
  Durability GTR should not interfere with the development of xEV’s
WLTP-28-18e

## Slide 9: Durability Alternatives
Four alternatives were identified for assessing electrified vehicle durability:
  Pre-aged battery
    prescribed test cycle
  Software emulation of an aged battery
    make the battery look aged with software changes
  Aging simulation
    Simulate battery aging (as demonstrated by JRC)
  Pre-defined deterioration factors
In the US, vehicle manufacturers have reported that they use all four methods for deterioration
WLTP-28-18e

## Slide 10: GTR Goals
EVE concluded that a GTR should:
  Begin a process which provide “rock screening” – establish minimum durability requirement
  Prohibit substandard products from entering the market
  Allow room for technology development
  Allow for data collection to inform future regulations regarding durability
WLTP-28-18e

## Slide 11: Durability Requirements
If the EVE direction is to establish durability requirements, some input from WLTP would be helpful
Electrified Durability requirements could be based on a set deterioration factor
  Should the DF be additive or multiplicative?
    Is one alternative more appropriate based on criteria or architecture?
    Is there a data set which exists which could help inform the selection of a DF?
  Would alternatives be acceptable?
    Could a manufacturer adopt the defined DF or present data to establish a different DF?
    Does EVE need to prescribe a method for determining alternative DF’s?
Should the durability requirements be added to the existing GTR or should it be a stand alone GTR?
WLTP-28-18e

## Slide 12: Durability Requirements – yes or no?
Vehicle Type | Criteria Pollutants | CO2/Energy Consumption | Electric Range
HEV | Yes – already part of WLTP | Yes | No – not required
PHEV | Maybe - High load cold starts could become more frequent with battery power fade | Yes | ??
PEV | No – not required | ?? | ??
WLTP-28-18e

## Slide 13: Next Steps
Next EVE meeting will be in Brussels on October 7th and 8th (EVE 32)
Japan is expected to make a formal proposal for durability
Feedback from the WLTP will be communicated to the EVE working group
Establish recommendation and plan for electrified durability to be presented to GRPE in January 2020
WLTP-28-18e