## Slide 1: „Light sources“ in RID
Walter Schlager, Philipp Plathner
5-July 2019
SLR-31-13

## Slide 2: Under “4. General technical requirements”
4.5. Light sources
4.5.1. Restrictions on light sources
The lamps shall only be equipped with UN approved replaceable light source(s), provided that no restriction on the use is made at the time of application for type approval, and/or light source module(s), and/or non-replaceable light source(s).
[Where more than one light source is used to provide a beam, the correlated colour temperatures …]
Additional light sources may be used inside the “passing beam headlamp” to contribute to bend lighting …
Where more than one light source is used to provide the driving beam, these light sources shall be …
4.5.2. General requirements for light sources (e.g. fixation, 2000lm limit, …)
4.5.3. Specific requirements for light sources (e.g. minimum source flux, …)
4.6. Testing of the lamp with respect to light sources
Depending on the light source used, the following conditions shall apply.
Tests shall be carried out according to Annex X.
4.7. Testing of light transmitting components …
4.8. Testing of cut-off …
4.9. Tests for stability of photometric performance …
Text of 4.5.1. reduces significantly
All testing details under 4.6. will be in Annex X.

## Slide 3: Under “5. Specific Technical Requirements”
5.1. Technical requirements concerning driving-beam of the Class A, B, D (GDL), BS, CS, DS or ES (GDL)
…
5.1.3. Requirements for the luminous intensity distribution of the driving-beams:
5.1.3.1. Referring to Figure A4-II the luminous intensity distribution of the driving-beam shall meet the following requirements …
(Note: specific HID requirements removed)
…
5.2. Technical requirements concerning headlamps to provide a passing-beam of the Class A, B and D (GDL)
…
5.2.2. The passing-beam shall meet the luminous intensities at the test points referred to in Table 8 and in Figures A4-V or A4-VI.
(Note: specific HID requirements removed)
...

## Slide 4: New: Annex X „Testing [with respect to light sources]“
The luminous intensity distribution is measured and checked for compliance after photometric stability.
Depending on the lamp (function) [and on the light source technology used] the luminous intensity distribution is additionally checked for compliance* at the point in time listed in Table X:
* The luminous intensity distributions at a point in time may be calculated from the luminous intensity distribution measured after photometric stability by applying at each test point the ratio of luminous intensities measured at the reference point of the lamp (function) under consideration.
In case of doubt, the compliance with the requirements of Table X may also be checked for „known technologies“ ,
e.g. if an electronic control gear is used to negatively influence the run-up behaviour
Lamp (function) | Time after activation | Testing required for the following light source technology | Reference point
Driving beam | [1] second | Gas-discharge, unknown, [non-approved light sources] | HV
Passing beam | [4] seconds | Gas-discharge, unknown, [non-approved light sources] | 50V
… | … | … | …
Rear position | [4] seconds | Gas-discharge, unknown, [non-approved light sources] | xx
Stop | [200] milliseconds | Gas-discharge, unknown, [non-approved light sources] | xx
Direction indicator | [200] milliseconds | Gas-discharge, unknown, [non-approved light sources] | xx
LSD example inserted for illustration purpose only

## Slide 5: New: Annex X „Testing [with respect to light sources]“
In case of filament technology (or: in case of UN approved filament light sources)
A lamp (function) is deemed to comply with the corresponding minimum and maximum intensity requirements in the period between [200] milliseconds after activation and photometric stability, if the values measured after photometric stability are compliant.
In case of UN approved gas-discharge light sources (or: in case of gas-discharge technology)
A lamp (function) is deemed to comply with the corresponding minimum and maximum intensity requirements in the period between [4] seconds after activation and photometric stability, if the values measured after photometric stability are compliant.
In case of LED technology (or: in case of UN approved LED light sources)
A lamp (function) is deemed to comply with the corresponding minimum and maximum intensity requirements in the period between [200] milliseconds after activation and photometric stability, if the values measured at [1] minute after activation and after photometric stability are compliant.
In case of another light source technology (or: … and in case of non-UN-approved light sources)
The corresponding minimum and maximum intensity requirements of a lamp (function) are tested and checked for compliance at all points in time starting at the corresponding point in time listed in Table x of this Annex and ending when photometric stability is reached.