## Slide 1: Functional Requirements for Automated Vehicles
Where to start?

## Slide 2: Mandate
Develop functional requirements for AV
  In particular, combination of different functions (SAE level 2+)
  Cover requirements for Functional Safety
In line with following principles:
  System safety
  Failsafe response
  HMI/Operator information
  OEDR

## Slide 3: Background Definitions
Functional Requirements
  Define the function of a system
  System must do _____. (mandatory)
  The “what?”
Non-Functional requirements
  Define criteria that can be used to judge the system
  System shall do _____. (suggestion)
  The “how?”

## Slide 4: Where to start?
Requirements vary based on a number of factors including:
  General requirements
    Ie applicable to all functions
  Specific function(s)
    Ie ALKS, lane change system, auto-park, full automation
  SAE level
    Level of reliance on driver
  Intended use
    Ie Driver support, driver replacement, ride-sharing

## Slide 5: Things to consider
Systems are heavily software based, often relying on probabilistic methods and object models
  Nothing is 100% certain
  “All models are wrong, but some are useful“
It may be necessary to include requirements for degraded/temporary modes of operation
  Ie. Temporary loss of lane markings, sensor oversaturation/interference
  Temporary increase in risk, but may be less than overall risk of transition to driver or attempting minimal risk manoeuvre
Humans drivers are also susceptible to the above

## Slide 6: Possible method
Begin with general requirements
  Add more sophistication/complexity in layers
  Build in some adaptability in the requirements
    Re-use requirements across different functions
For each function, level and intended use choose what layer (level of sophistication) is appropriate
  Layers above could be seen as fallbacks in case of failure & have associated performance degradation/system limitations
Keep a “database” of requirements and re-use for each function

## Slide 7: Partial Example – Highway Chauffeur
System must (detect/perceive/act):
  Roadway
    Lane
      Lane markings
      Centre of lane
    Infrastructure
      Traffic control devices
        State of device
    Road type
      Road Condition
        Adverse weather
  Position of other road users (same lane, adjacent lane, opposite lane)
    Velocity of other road users
      Classify type of user
        Indications of user intent (turn signal, location in lane, acceleration)
          (Predict) user intended path
  Keep a safe distance from other users
    Accelerate/decelerate smoothly
    Reduce likelihood of crossing intended paths
Result: Can proceed at rated conditions (speed, lane change etc.)

## Slide 8: Partial Example – Highway Chauffeur – (temporary) loss of a sensor
System must (detect/perceive/act):
  Roadway
    Lane
      Lane markings
      Centre of lane
    Infrastructure
      Traffic control devices
        State of device
    Road type
      Road Condition
        Adverse weather
  Position of other road users (same lane, adjacent lane, opposite lane)
    Velocity of other road users
      Classify type of user
        Indications of user intent (turn signal, location in lane, acceleration)
          (Predict) user intended path
  Keep a safe distance from other users
    Accelerate/decelerate smoothly
    Reduce likelihood of crossing intended paths
Result: Degraded mode (may need to reduce speed, cannot lane change, increase distances to other users)

## Slide 9: Starting point
Use some of the concepts in published guidance documents as starting point
Build upon & categorise
Begin with general statements, add complexity/layers when required for a technology
  Less complex system requirements can become the degraded modes of more sophisticated systems
Work towards specific requirements which can be testable

## Slide 10: A few possible – “System must” from Canada’s Safety Assessment
1. ADS Level of Automation and intended use
  Have a defined level of automation
  Have a clear intended use
  Be able to identify the software & hardware version
2.Operational Design Domain
  Have a clearly defined ODD
    Prevent system from activating if outside ODD
    Ability to detect if OD outside ODD
    Minimize risk if ODD exceeded
  Maintain the safe flow of traffic
  Comply with the traffic rules

## Slide 11: A few possible – “System must” from Canada’s Safety Assessment
3. Object and Event Detection and Response
  Detect & perceive other road users
  Respond appropriately to (road infrastructure, other users, traffic control, unlawful users, animals, unclassified objects)
6. Safety Systems
  Have redundancies
    Monitor performance
    Detect faults
    Conduct hazard analyses
  Signal malfunctions
    Execute corrective action
  Transition to safe fall-back

## Slide 12: A few possible – “System must” from Canada’s Safety Assessment
7. Human-Machine Interface and Accessibility of Controls
  Have intuitive controls
  Communicate critical messages (to occupants and others)
  Clearly communicate a take-over request
  Allow sufficient time for a fall-back driver to respond
  Show when the system is available, not available and operational
  Signal intention to other road users

## Slide 13: A few possible – “System must” from Canada’s Safety Assessment
8. Public Education and Awareness
  Be clear to the driver when and how it performs DDT or partial DDT
    Indicate maintenance requirements
  Make it’s intent clear to other road users
9. User Protections during Collisions or System Failures
  Achieve a safe state after a collision/failure
    Communicate with passengers, first responders, emergency services
  Conduct system tests prior to returning to circulation

## Slide 14: A few possible – “System must” from Canada’s Safety Assessment
11. System Updates and After-Market Repairs/Modifications
  Conduct system checks after update/modification/repairs
  Be disabled if the function is no longer supported