## Slide 1
Describe in a few sentences what should be the outcome of the ‘audit/virtual testing/in-use data reporting
Audit/assessment
Audit: Confirmation that the manufacturers have appropriate processes in place to develop AV’s for the road through the management processes, development phase and lifecycle of the vehicle. This shall include the process of updating vehicles on the road.
Assessment of vehicle safety: Assessment of manufacturer performance data demonstrating that the vehicle design, verification and validation done by the manufacturer has mitigated risk and meet the minimum performance requirements.
Well adapted to assess performances that are not easy to test on track or on road.
What are the questions to be answered?
What are the minimum documentation requirements to achieve this?
Documentation necessary to conclude on the process/safety validation (Reference can be found in ISO PAS 21448 SOTIF/ISO 26262/Annex 6-R79,etc)?
How early in the development phase should this audit/assessment process start?
2 steps: when safety concept is clear and after verification/validation. (V model)
Audit: Not linked to the product. Shall start before development. The cyber regulation could be used as reference.
How prescriptive (how deep) do the requirements need to be and what level should aim for? Data provided by manufacturer to be confirmed by independent test?
Audit :Check that the process is robust enough, documented and is implemented
Assessment: Check that the risk assessment is complete, that safety concept is addressing the risk assessment. Check that the safety concept is implemented consistently in the design of the different functions of the AD system. Check the verification validation process is robust enough (simulation, track test, in use data)
Who should conduct the audit/assessment?
Audit and assessment to be conducted by a qualified independent 3rd party.
What are pass/fail criteria/ an acceptable level of risk (link with WP29/GRVA/FRAV-VMAD/1a) & what is the appropriate method to demonstrate a certain level of risk?
Failed audit: process not documented, no demonstration that there is an appropriate level of management
Failed assessment: The residual level of risk is not acceptable (accident preventable and .. See FD).
Difference between harmonized track tests (link with VMAD/2b) and verification tests (to verify safety concept)?
Information on existing practices:
Use R79 Annex 6 as a basis (Annex CEL). However, more is required. ISO26262 (mainly regarding failures) and SOTIF (some focus on driver assistance systems) taking the basic principles and applying them to an audit approach.
FMEA’s, Fault Tree Analysis will be included – how to manage the negative outcomes. Other risk analysis methods as well.
UL 4600 draft standard
VMAD-04-05
SG 2a “Audit/ In-use reporting

## Slide 2
Virtual Testing
-Allow the manufacturer to validate safe driving without having to drive the vehicle millions of km in various traffic scenarios.
-This data can be used to demonstrate validation/safety performance to authorities.
-Virtual testing is well adapted to critical/dangerous/complex scenarios, validate variants
What are the questions to be answered?
Do we need one standardised tool or can multiple solutions be permitted?
No one-fits-all solution exists today. Several simulation tools for different purposes (HIL, SIL, etc.). Need to ensure interfaces . In the long run harmonized tool could be beneficial.
Need to clarify the different concepts of simulation/models/virtual testing. What is used today?
How to ensure that the results of virtual Testing make sense?
Requirements on the correlation of the expected results with track tests/on road tests, scope, traceability, etc.
Who validates virtual testing? Manufacturers? Authorities?
Mostly by manufacturers. However some parameters to be checked by authorities.
Information on existing practices:
R140 is a good example for validation of simulation tools. 1958 Agreement/Rev3
On-going standardization work at ISO on digital interfaces
Remarks:
Link with subgroups 2b for track testing/on road testing
Only a subset of functional requirements can be validated by virtual testing

## Slide 3
In use reporting (after placing on the market)
To cover residual risks
Verify compliance on the ground
To improve traffic models/scenarios
What questions need to be answered?
How to cover residual risks once the vehicle is on the market?
A process shall be put in place by the manufacturer to minimize risks over the lifetime of the vehicles and shall include new unknown scenarios in the vehicle capability. There is however an asymptote in risk management.
How do we ensure continuous compliance (e.g. traffic rules) on the ground in particular (but not only) after an OTA (Link with OTA/CS group)? Check by authorities?
What kind of data shall be collected by manufacturers? What kind of data shall be reported to authorities (e.g. Reporting on accidents to authorities)? How often? There are limits to the data that can collected/shared. How do we ensure suitable oversight of the reporting? How this data should be collected (e.g. use EDR/DSSAD for in use reporting)? What shall authorities do with this data? How do ensure operational feedback from the field on traffic scenarios in the common database? There is a common interest in sharing new unknown scenarios
Remark:
In use reporting can also be used by manufacturers to validate their ADS

## Slide 4
c) Indicate which persons/organisations need to be involved in this group?
CP’s, TAA’s, Tech services, OEM’s, Suppliers, Software companies should be involved
Companies that are deep into validating simulation tool chains
Keep as one group Audit/virtual testing/in-service