## Slide 1: Proposal for a 00 / 01 Series for the CS Regulation
to address Implementation issues for existing vehicle architectures
Submitted by the Expert from OICA
TFCS-16-18 Rev1

## Slide 2
Cyber Security Management System
E/E Architecture with regard to CS
Cyber Security Management System
E/E Architecture with regard to CS
00 Series
01 Series
CSMS requirements
Original content of 7.2.
NEW
E/E type requirements
New content for 7.3.
Transitional Provisions
NEW
CSMS requirements
Original content of 7.2.
E/E type requirements
Original content of 7.3.
Annex 1
Amendment necessary?
Annex 1
UN Regulation No. 15X on Cyber Security
Possible structure for the 00/01 Series approach
New chapter 12.
Original content

## Slide 3
7.3. Requirements for vehicle types
7.3.1. Before the assessment of a vehicle type for the purpose of type approval is carried out the vehicle manufacturer shall demonstrate to the Approval Authority or Technical Service that their Cyber Security Management System has a valid Certificate of Compliance for CSMS relevant to the vehicle type being approved.
7.3.2. The Approval Authority or Technical Service shall verify that the manufacturer has taken the necessary measures relevant for the vehicle type to:
(a) Collect and verify information required under this Regulation, through the supply chain;
(b) Document risk assessment, test results and mitigations applied to the vehicle type, including design information supporting the risk assessment;
(c) Implement appropriate security measures in the design of the vehicle and its systems;
7.3.2. 7.3.3. The vehicle manufacturer shall demonstrate the risk assessment for the vehicle type and, that it considers its subsystems and their interactions and the approach taken for managing risks. and how the risks have been treated/managed.
7.3.3. 7.3.4. The vehicle manufacturer shall identify demonstrate that critical elements of the vehicle type are protected against risks identified in the vehicle manufacturer’s risk assessment. Proportionate mitigations shall be implemented to protect such elements.
7.3.4. The vehicle manufacturer shall demonstrate that risks identified during the risk assessment for the vehicle type are being monitored and managed by an incident response process.
7.3.5. The vehicle manufacturer shall demonstrate that appropriate and proportionate measures have been put in place to secure dedicated environments on the vehicle type (if provided) for the storage and execution of aftermarket software, services, applications or data.
7.3.6. The vehicle manufacturer shall describe what testing has been performed to verify the effectiveness of the security measures implemented and the outcome of those tests.
7.3. Requirements for vehicle types
7.3.1.Before the assessment of a vehicle type for the purpose of type approval is carried out the vehicle manufacturer shall demonstrate to the Approval Authority or Technical Service that their Cyber Security Management System has a valid Certificate of Compliance for CSMS relevant to the vehicle type being approved.
7.3.2.The Approval Authority or Technical Service shall verify that the manufacturer has taken the necessary measures relevant for the vehicle type to:
(a) Collect and verify information required under this Regulation, through the supply chain;
(b) Document risk assessment, test results and mitigations applied to the vehicle type, including design information supporting the risk assessment;
(c) Implement appropriate security measures in the design of the vehicle and its systems;
7.3.3.The vehicle manufacturer shall demonstrate the risk assessment for the vehicle type and that it considers its subsystems and their interactions.
7.3.4.The vehicle manufacturer shall demonstrate that critical elements of the vehicle type are protected against risks identified in the vehicle manufacturer’s risk assessment. Proportionate mitigations shall be implemented to protect such elements.
7.3.5. The vehicle manufacturer shall demonstrate that appropriate and proportionate measures have been put in place to secure dedicated environments on the vehicle type (if provided) for the storage and execution of aftermarket software, services, applications or data.
7.3.6.The vehicle manufacturer shall describe what testing has been performed to verify the effectiveness of the security measures implemented and the outcome of those tests.
„Vehicle type requirements“ of „existing vehicles“
Original content
Proposed amendments

## Slide 4: Transitional Provisions
Proposed wording (based on UN guideline):
12. Transitional Provisions
12.1. As from the official date of entry into force of the 01 series of amendments, no Contracting Party applying this Regulation shall refuse to grant or refuse to accept type approvals under this Regulation as amended by the 01 series of amendments.
12.2. As from 1 September [2022], Contracting Parties applying this Regulation shall not be obliged to accept type approvals to the 00 series of amendments, first issued after 1 September [2022].
12.3. Contracting Parties applying this Regulation shall continue to accept type approvals issued according to the 00 series of amendments to this Regulation first issued before 1 September [2022].
12.4. Contracting Parties applying this Regulation shall not refuse to grant type approvals according to any preceding series of amendments to this Regulation or extensions thereof.
12.5 Notwithstanding paragraph 12.3, as from 1 September [2028], Contracting Parties applying this Regulation shall not be obliged to accept type approvals to the 00 series of amendments for vehicle types incorporating capabilities for receiving over the air software updates, which may impact type approved systems.

## Slide 5: How “high risk vehicles” are addressed
High risk vehicles:
- vehicles with high level of connectivity (e.g. OTA capability for type approval relevant systems)
Automated vehicles of Level 3+
The draft proposal for the 00 Series requires risk management, incl. risk assessment, identification of critical elements, etc. which will be different for a conventional vehicle compared to a vehicle with a high level of connectivity and/or automated driving functions
Transitional Provisions ensure limited acceptance of 00 Series approvals for vehicle types incorporating capabilities for receiving over the air software updates, which may impact type approved systems
=> Automated vehicles are expected to have OTA capabilities