## Slide 1
Proposed Type Differentiation Criteria for the Cyber Security Interpretation Document
TFCS-16-36

## Slide 2: Example of changes in the E/E Architecture
Development of an E/E Architecture requires a new type.
Change of outcome of risk assessment by introducing new technologies
No change of outcome of risk assessment
Requires a new type, since security in existing subsystem is being influenced.
Replacing an existing subsystem, and this does not change the cybersecurity of the resulting E/E architecture, and thus does not require a type extension. This is the usual situation.
Development of a new E/E Architecture
Possible changes in the E/E Architecture
Replacing an existing subsystem or adding a new subsystem, and this introduces some minor changes to the cybersecurity of the resulting E/E architecture, and thus requires an type extension.
New type
Extension of existing type
No impact
New Type or Type Extension
Changes of outcome of risk assessment by adding or replacing subsystems
Development of an E/E Architecture requires a new type.
Adding new external interfaces (NFC Near Field Communication) for new services such as personalization
Change of network topology by adding a gateway with new com. protocol
Replacing an ECU:
new state of the art processor, more memory, no new functionality,
different supplier
Examples
Replacing a UMTS communication unit by a 5G communication unit -> additional communication possible
Replacing an ECU by a new one with a HSM (hardware security module)
Example criteria

## Slide 3: Suggested addition to the interpretation document Cyber Security
New Types
Type Extension
Development of a new E/E architecture or fundamental change(s), that influences cyber security of the existing E/E architecture.
Changes that have minor impact to the cyber security of the existing E/E architecture and can occur with the introduction of an additional subsystem or the replacement of an existing subsystem.