## Slide 1: Event Data Recorder (EDR) & Data Storage System for Automated Driving (DSSAD)

## Slide 2: The foundations of this “2-step” strategy
Time is short until March 2020 and November 2020 for deciding of which data for DSSAD and which new data for EDR (format, sampling rate, …) or trigger is pertinent.
Time is short until May 2022 for Industry to deeply change the technical definitions of already existing EDRs of current vehicles with existing E/E architectures.
(Memory capacities are limited, and DSSAD must be incorporated too)
What opportunity with adressing the « new trigger » in step 2 ?
“Intervention of AEBS” could be an additional candidate for triggering the EDR.
but : EU will mandate AEBS for Pedestrians & Cyclists in 2024 for NT / 2026 for AR.
(AEBS introduced in 2022/2024 only address Car-to-Car collisions)
EU will mandate EDR on Heavy Duty Vehicles (M2, N2, M3, N3) in 2025 for NT / 2028 for AR
It would be beneficial to evaluate the pertinence and feasibility of any other « new trigger »
on both Light (M1, N1) and Heavy Duty Vehicles (M2, N2, M3, & N3) before mandating.

## Slide 3
A dual “2-step” strategy for EDR & DSSAD
 | EDR (step 1 = M1/N1) | DSSAD (All vehicles with ALKS)
Purpose | Accident analysis | Legal responsability, liability (research, monitoring)
When (text finalized) | 2020, November (step 1) | 2020, March
When (application date) | 2022 NT / 2024 AR in EU Already exists in USA & South Korea Draft in China (2021/2023 to be confirmed) | Same time as ALKS (end of 2020 ?) and for ALKS
Reference | FMVSS 49 CFR Part 563 | Concept as proposed by OICA & JAPAN
Must incorporate in step 1 | Requirements of texts already enforced (prioritize harmonization on existing) Same requirements for “conventional” & “AD (ALKS)” | Answers both questions : Was Driver or System requested to drive ? Was Driver or System actually driving ? Uses definitions given by ALKS
Can incorporate in step 1 | Inputs from recent ADAS (if covered by UN ECE) Revisiting format of some existing elements if justified by field experience | Only parameters that establish the answer to the dual question above
Will incorporate in step 2 (EDR) (2025 NT / 2028 AR) | New “trigger(s)” (for Heavy Duty Vehicles) New trigger(s) (for Vulnerable Road Users) New data (after field feedback of step 1 & application of Chinese regulation) | (no schedule yet for step 2 today) New parameters if needed for systems “after ALKS” New parameters after field experience feedback