## Slide 1: MVC meeting #6 2016, March 2-3, Brussels
Industry input
ISO11992 Electric Control Line
Point-to-point connection
Version 2
Pierre Teyssier
Volvo Group

## Slide 2: Aim of the document
Provide technical background about the electric control line
Review the main requirements related to the electric control line in the UN R13 regulation
Clarify if routers and repeaters are covered / permitted by UN R13
Conclude on whether there is a need to mandate a router in UN R13

## Slide 3: Electric control line in UN R13 Main requirements
The electric control line pin 6 and 7 of ISO 7638 connector shall conform to ISO 11992 standard
The CAN-connection between towing and towed vehicle shall be a point-to-point connection
The CAN bus length shall not be more than 40m (15m for truck, 18m for trailer, 7m for electric coil)
CAN interface (towing vehicle)
CAN interface (towed vehicle)
ISO 7638
Pin 6 – CAN H
Pin 7 – CAN L
ISO 11992
ISO 11992
< 40m
Point-to-point means:
YES
NO
coil

## Slide 4: Electric control line CAN - Router
2
EBS
Router
EBS
EBS
EBS
EBS
EBS
Solution 1: router function integrated to EBS
Solution 2: stand-alone router
Conclusions:
There is a no need to mandate a router in UN R13.
The need for a “router function” is induced by the “point-to-point connection” requirement.
The standalone router is only one possible technical solution.
Current layout

## Slide 5: Electric control line CAN - Repeater
2
EBS
Router
EBS
EBS
EBS
EBS
Solution 1: The router intrinsically includes a repeater function
Solution 2: The router is a standalone device
Summary:
A router is needed when the required CAN length is longer than 40m (actually when trailer CAN > 18m)
The router could be a standalone device or integrated in EBS (or elsewhere)
It should be checked whether a repeater is explicitly permitted by UN R13 (if not, then it should be)
> 40m
Repeater