## Slide 1
Status report to GRBP #71
Task Force on Reverse Warning Sound issues
Transmitted by the Chair of TF RWS
(TFRWS-10-03)
Informal document GRBP-71-27-Rev.1
(71st GRBP, January 28-31, 2020,
agenda item 6)

## Slide 2
Meeting
9th meeting participants
10th meeting participants
Contracting parties : Japan, Germany, Netherland, EC
NGOs, etc : OICA, GREWUS (Guest), ESG (Guest)
9th Meeting : October 22-24, 2019 – Brussels
Small group drafting meeting
10th Meeting : January 28, 2020 – Geneva
Task force meeting
Contracting parties : Japan
NGOs, etc : OICA, GREWUS(Guest)

## Slide 3
Schedule of document submission to GRBP
TFRWS aimed to submit working document to GRBP in January, 2020 (GRBP #71).
Then, we decided to postpone submitting because validation of test method has not been conducted yet, and the information of limit value table to be discussed has not been provided enough by contracting parties.
Self-adjusting device is not expected at starting time of this group, however it is on a draft now. Making test method for self-adjusting device is taking more time than expected.
Status of discussion

## Slide 4
Questionnaire research
Scope
M3, M2(3.5t >), N3, N2
Pause switch
Pause switch should be allowed when the other safety device (e.g. camera monitor system or detection system) is effective.
Requirement of warning sound
Sound emitting count per minutes, frequency range of tonal sound
Completed items in a draft of new regulation

## Slide 5
Part I : Component test
Step-wise self adjusting device : Validation test
Self adjusting device : Proposal of test method and validation test
Limit value : Calculated based on limit value of Part II
Effect of R28 : Modification of unsuitable sentences for RWS
Part II : Vehicle test
Step-wise self adjusting device: Validation test
Self adjusting device : Proposal of test method and validation test
Limit value : Mode of sound level, necessity of limit value difference depending on sound type
Uncompleted items in a draft of new regulation

## Slide 6
Requirement of warning sound
CLEPA proposed tonal sound should be limited from 700 Hz to 2800 Hz.
On the other hand, from 500 Hz to 4000 Hz of tonal sound which is defined in South Korean domestic law, and Japanese current situation is same frequency range. Based on the information above, TF group agreed tonal sound should be in the frequency range from 500 Hz to 4000 Hz.
TF group agreed sound emitting count per minute are 24-120.
Previously, table of limit value consists of 3 sound types (tonal sound, Broad band sound, 1/3 Octave band sound). After discussion in the group, TF group decided BBS and 1/3 octave band sound are same limit value.
Status of discussion

## Slide 7
Test method for self-adjusting device
The test method is being made, now. After completion, verification test will be conducted.
In part I test (component test), 4 different volume pink noise is proposed to be used.
In part II test (vehicle test), it is difficult to control BGN level, a realistic and an appropriate test method will be discussed.
Status of discussion

## Slide 8
7 m
2 m
4.5 m
7 m
2 m
4.5 m
45⁰
Measurement distance
(Outdoors):
2 m
4,5 m
7 m
10 m
14 m
Test Condition 1
10 m
14 m
10 m
14 m
Collecting measurement data protocol
The aim of collecting data is to understand sound field behind the vehicle.

## Slide 9
1 m
0.5 m
1.5 m
Microphone Height
Reflecting Ground
Test Condition 2
Microphone position above ground
(Outdoors):
8 points on a circle
Collecting measurement data protocol
Measurement position

## Slide 10
1 m
0.5 m
1.5 m
Microphone Height
Test Condition 3
Sweep to find maximum sound presure level
Microphone position above ground
(Outdoors):
Sweep on the line between
0⁰ and 180⁰
Collecting measurement data protocol
Reflecting Ground

## Slide 11
Test Condition 4
11 measurement points between
0.5 m and 1.5 m, Δ = 0.10 m
Microphone position above ground
(Outdoors):
11 points on the line between
0⁰ and 180⁰
Collecting measurement data protocol
Reflecting Ground
1 m
0.5 m
1.5 m
Microphone Height

## Slide 12
Test Condition 5
1 measurement point at 1.2 m
Microphone position above ground
(Outdoors):
1 point at 1.2 m on the line between
0⁰ and 180⁰
Collecting measurement data protocol
Reflecting Ground
1 m
0.5 m
1.5 m
Microphone Height

## Slide 13
7 m
2 m
4.5 m
7 m
2 m
4.5 m
45⁰
At
Measurement
distance
(Outdoors):
2 m
4,5 m
7 m
10 m
14 m
Test Conditions
10 m
14 m
10 m
14 m
Microphone
position above ground
(Outdoors):
Condition 3, 5
Condition 3,5
Condition 2, 3, 4
Condition 3, 5
Condition 3, 5
The sound pressure level shall be measured at the fixed height(s) for a duration of at least 30 seconds
Collecting measurement data protocol

## Slide 14
Coordination with GRSG and VRU-Proxi IWG
Switzerland reported last our status report (GRBP-70-24) to GRSG (October, 2020).
Following sentences were made by Switzerland and secretariat of GRSG
GRSG understand the need for a pause switch. However, it should not be active in every situation e.g. when a redundant safety system e.g. camera monitor system or detection system is not providing the sufficient safety.
GRSG considered as an example the case of a vehicle with a coupled trailer. If the vehicle with trailer is in reversing gear, the pause switch should be ineffective as the camera would not deliver necessary information to the driver.
GRSG recommends that the conditions shall be listed in the future regulation when the pause switch is effective or, if not possible, criteria shall be envisaged.

## Slide 15
Coordination with GRSG and VRU-Proxi IWG (con't)
Depending on suggestion by GRSG, the conditions when the pause switch is allowable or not, are summarized as follows.
Regarding trailer, it should be discussed that it is possible to make a system enable to judge whether the other safety device installed in the trailer is effective or not.

## Slide 16
11th meeting :
May 26-27, 2020 – Brussels (TBC)
The main issue of 11th session is to verify measurement method and discuss about limit value.
The discussion will be proceed based on collected data.
Please submit data until May 22, 2020.
Any small information is welcomed!
To : manfred.klopotek@scania.com
Cc: houzu@ntsel.go.jp
Schedule