## Slide 1: Flexibilities for Euro 6 Step 2

## Slide 2
The Euro 6 Step 2 OBD thresholds pose very technology driving requirements. Considering the large volume of vehicles and the large number of vehicles types some flexibilities are needed for the introduction of new technologies.
Deficiencies are already established in 692/2008 and Regulation 83.
The scope of deficiencies is very limited
  3.4. The approval authority will not accept any deficiency request that does not respect the OBD threshold limits in Section 2.3.
Deficiencies
Flexibilities for Euro 6 Step 2

## Slide 3
This limitation is not present in the US (CARB) legislation or in the European Heavy Duty legislation.
Proposal - align with Euro VI deficiency basis.
Other option:
  4.2.2. The authority will not accept any deficiency request that does not respect would result in the OBD threshold limits in paragraph 3.3.2 being exceeded by a factor of two.
Deficiencies
Flexibilities for Euro 6 Step 2

## Slide 4
USA
To grant a deficiency the following points shall be considered:
the extent to which the requirements of section 1968.2 are satisfied overall based on a review of the vehicle applications in question,
the relative performance of the resultant OBD II system compared to systems fully compliant with the requirements of title 13, CCR section 1968.2,
and a demonstrated good-faith effort on the part of the manufacturer to:
(1) meet the requirements in full by evaluating and considering the best available monitoring technology;
and (2) come into compliance as expeditiously as possible.
Europe
To grant a deficiency the following points shall be considered:
technical feasibility
lead time
production cycles including phase-in or phase-out of engines
vehicle designs
programmed upgrades of computers
the extent to which the resultant OBD system will be effective in complying with the requirements of the Regulation
that the manufacturer has demonstrated an acceptable level of effort toward compliance with the requirements of this Regulation
Comparison regarding granting an OBD deficiency

## Slide 5
USA
Executive Officer, upon receipt of an application from the manufacturer, may certify vehicles even though said vehicles may not comply with one or more of the requirements.
No deficiency for vehicles which would be subject to ordered recall for:
IUPR ratios not fulfilled with one monitors average ratio below 33% of the required ratio or 66 % of the vehicles have one Monitor ratio below the minimum required ratios
Lack of monitoring of a major component prior to 3.5 up to 4.5 times the applicable emission standard
Misfire above 20% than the disclosed misfire rates for catalyst damage for gasoline and misfire above 10% than the disclosed misfire rates for Diesel
EVAP monitor not able to detect leaks 1.5 bigger than 0.020 inch diameter
malfunction of a component that effectively disables a major monitor
For 2013 and subsequent model year medium-duty diesel vehicles the PM filter monitor is unable to detect and illuminate the MIL for a missing substrate fault or malfunction of the PM filter that causes PM emissions to be equal to or greater than the emission level of the engine or vehicle with the PM filter substrate completely removed.
The motor vehicle class cannot be tested so as to obtain valid test for communication requirements
Europe
Restrictions for which no deficiency will be granted:
Lack of monitoring for
reduction in the efficiency of the catalytic converter with respect to emissions of THC and NOx
Misfire
Oxygen sensor deterioration
Other emission control system components or systems, or emission related powertrain components or systems which are connected to a computer, the failure of which may result in tailpipe emissions exceeding the limits
Any other emission-related power-train component (including EVAP) connected to a computer, including any relevant sensors to enable monitoring functions to be carried out, shall be monitored for circuit continuity;
Violation of OBD thresholds
Violation of Communication Standards
Comparison regarding granting an OBD deficiency

## Slide 6
3. ADMINISTRATIVE PROVISIONS FOR DEFICIENCIES OF OBD SYSTEMS
3.1. In considering the request for granting type-approval to a vehicle with a deficiency or deficiencies as set out in Article 6(2), the approval authority shall determine whether compliance with the requirements of this Annex is infeasible or unreasonable.
3.2. The approval authority shall take into consideration data from the manufacturer that details such factors as, but not limited to, technical feasibility, lead time and production cycles including phase-in or phase-out of engines or vehicle designs and programmed upgrades of computers, the extent to which the resultant OBD system will be effective in complying with the requirements of this Regulation and that the manufacturer has demonstrated an acceptable level of effort toward compliance with the requirements of this Regulation.
3.3. The approval authority shall not accept any deficiency request that includes the complete lack of a required diagnostic monitor or of mandated recording and reporting of data related to a monitor.
3.4. The approval authority will not accept any deficiency request that does not respect the OBD threshold limits in Section 2.3.
3.5. In determining the identified order of deficiencies, deficiencies relating to sections 3.3.3.1, 3.3.3.2 and 3.3.3.3 of Annex 11 of UN/ECE Regulation 83 for positive ignition engines and sections 3.3.4.1, 3.3.4.2 and 3.3.4.3 of Annex 11 of UN/ECE Regulation 83 for compression-ignition engines shall be identified first.
3.6. Prior to or at the time of type-approval, no deficiency shall be granted in respect of the requirements of section 6.5, except section 6.5.3.4 of Appendix 1 to Annex 11 of UN/ECE Regulation 83.
LD: EC 692/2008 last amended by EC 136/2014 Annex XI Appendix 1
Deficiency Regulation Europe

## Slide 7
6.4. Approval of an OBD system containing deficiencies
6.4.1. Approval authorities may approve upon request of a manufacturer an OBD system even though the system contains one or more deficiencies.
In considering the request, the Type Approval Authority shall determine whether compliance with the requirements of this annex is feasible or unreasonable.
The Type Approval Authority shall take into consideration data from the manufacturer that details such factors as, but not limited to, technical feasibility, lead time and production cycles including phase-in or phase-out of engines designs and programmed upgrades of computers, the extent to which the resultant OBD system will be effective in complying with the requirements of this annex and that the manufacturer has demonstrated an acceptable level of effort toward meeting the requirements of the annex.
The Type Approval Authority will not accept any deficiency request that includes the complete lack of a required diagnostic monitor (i.e. a complete lack of the monitors required in Appendix 3 to this annex).
6.4.2. Deficiency period
A deficiency is granted for a period of one year after the date of approval of the engine system.
If the manufacturer can adequately demonstrate to the Type Approval Authority that substantial engine modifications and additional lead time would be necessary to correct the deficiency, then this deficiency can be granted again for an additional one year, provided that the total deficiency period does not exceed three years (i.e. three times one year deficiency allowance is permitted).
HD: Regulation No 49, Annex 9B
Deficiency Regulation Europe