Agricultural vehicles: Mechanical connections on towed vehicles

-) Sviwel hitch rings

Figure 1— Round eye configuration

Table 1 — Shapes, dimensions and allowable loads

| Vertical load S (daN) | D value (kN) | Class | Coupling ring [mm] |
| --- | --- | --- | --- |
|  |  |  | Round eye configuration |
|  |  |  | d | b | c | t | i | h |
|  |  |  | ±0,5 | min | min | min | max | ±1 |
| ≤1000 | ≤35 | (?) | 22 | 40 | 80 | 30 | 30 | 20 |
| ≤3000 | ≤120 | (?) | 50 | 55 | 140 | 60 | 55 | 35 |

## Trailer shank travel angles

When the trailer shank fitted with the specified hitch ring is fixed to the self-propelled machine attachment, the shank shall be free to turn so that the angles formed with the horizontal situated in the self-propelled machine's plane of symmetry and passing through the coupling point have the following minimum values.

Angle of yaw: rotation around a vertical axis passing through the coupling point, minimum value of 60° on both sides (see Figure 3).

Angle of pitch: rotation around a horizontal axis passing through the coupling point and perpendicular to the machine's longitudinal plane of symmetry, minimum value 20° top and bottom (see Figure 4).

Allowance should be made for the towing vehicle being up to ± 3° from horizontal, due to front/rear tyre sizes.

Angle of roll: rotation around a horizontal axis passing through the coupling point and located in the machine's plane of symmetry, minimum value 20° top and bottom (see Figure 5).

Figure 2 — Angle of yaw

Figure 3 — Angle of pitch

Figure 4 — Angle of roll

# Constructional requirements

Hitch rings in accordance with this part of ISO 5692 shall be substantially toroidal and shall be manufactured by forging. The removable hitch ring shall be jointed to a sleeve which is fixed on the trailer drawbar.

# Permissible mechanical connections between rings and couplings

See Table 2.

Table 2 — Permissible mechanical connections between rings and couplings

| Ring | Coupling |
| --- | --- |
| ISO 5692-3 Class D | ISO 6489-5 Class d |
| ISO 5692-3 Class F | ISO 6489-5 Class f |

-) Non sviwel couplings

Figure 5 — non sviwel coupling

Table 3 — Shapes and dimensions of trailer clevis couplings

| Vertical load [S] (daN) | D value (kN) | Class | Dimensions [mm] |
| --- | --- | --- | --- |
|  |  |  | D | a | b |
|  |  |  | ±0,5 | min | min |
| ≤1000 | ≤35 | (?) | 18 | 50 | 40 |
| ≤3000 | ≤120 | (?) | 43 | 100 | 80 |