## Slide 1
(N)OVC-HEV: KCO2 correction factor family Proposal ACEA EV for SG EV
Text proposal:
For (N)OVC-HEV, it is allowed to merge two or more interpolation families into the same KCO2 correction factor family at which KCO2 shall be determined with vehicle H of one of the included interpolation families.
At the request of the responsible authority, the manufacturer shall provide evidence on the justification and technical criteria for merging these interpolation families for example in the following cases:
Two or more interpolation families are merged
which were split because the maximum interpolation range of 20 g/km CO2 is exceeded (in case vehicle M measured: 30g/km);
which were split due to different engine power ratings of the same physical combustion engine (different power only related to software)
which were split because the n/v ratios are just outside the tolerance of 8%;
which were split, but still fulfil all the family criteria of a single IP family.
which were split because there is different number of powered axles
Different electric energy converters between recharge-plug-in and traction REESS shall not be considered as an criterion in the context of the correction factor family as no impact on KCO2 determination procedure.

## Slide 2: Back Up

## Slide 3
OVC-HEV: KCO2 correction factor family CoP family for Type 1 test as basis
8.1.3.1. CoP family for Type 1 test
For the purposes of the manufacturer's conformity of production check on the Type 1 test, including, where applicable and if required, the determination of the OBFCM device accuracy, the family means the conformity of production (CoP) family as specified in paragraphs 8.1.3.1.1 and 8.1.3.1.2.
8.1.3.1.1. For interpolation families as described in paragraph 6.3.2. of this Regulation with a planned vehicle production volume of more than 1,000 vehicles per 12 months, the CoP family for the Type 1 test shall be identical to the interpolation family.
8.1.3.1.2. For interpolation families as described in paragraph 6.3.2. of this Regulation with a planned production volume of 1,000 vehicles or less per 12 months, it is allowed to include other interpolation families into the same CoP family, up to a combined maximum production volume of 5,000 vehicles per 12 months. At the request of the responsible authority the manufacturer shall provide evidence on the justification and technical criteria for merging these interpolation families, ensuring that there is a large similarity between those families, for example in the following cases:
two or more interpolation families are merged which were split because the maximum interpolation range of 30 g/km CO2 is exceeded;
interpolation families that were split because there are different engine power ratings of the same combustion engine;
interpolation families that were split because the n/v ratios are just outside the tolerance of 8%;
interpolation families that were split, but still fulfil all the family criteria of a single IP family.