## Slide 1: Status Report of TF TA to 83rd GRBP session
Progress Report (September 2025 – February 2026)
Finalisation of draft UN Regulation on tyre abrasion for C1 tyres and Launch of C2 Work
[DRAFT – TFTA discussion document]
Note to the UNECE Secretariat:
The author and the speaker of this presentation confirm that they have authorization to use all content including photos and visual elements.
The material is either copyright-free or the author/speaker hold the necessary copyright or permission.
The UNECE will remove any material from its events and supporting websites if there is unlawful use of copyrighted material.
The author/speaker takes responsibility for any infringement on copyright and holds the UNECE harmless to this effect.
Transmitted by the co-chairs of TF for Tyre Abrasion

## Slide 2: Task Force on Tyre Abrasion
Targets | Develop a robust procedure for measuring the abrasion of tyres: Test conditions and methods; Define the acceptable uncertainty for the tyre abrasion test method(s) and assess the uncertainty of the tyre abrasion test method(s); Based on the abrasion test method(s), define a characterisation of relative mileage potential index; Evaluate the abrasion performance and tread depth reduction of a wide range of tyres available in the market; Define abrasion limits for tyres in order to limit the emission of microplastics to the environment; Develop a proposal of new UN Regulation for the type approval of tyres in respect to their abrasion.
Roles | Co-chairs: UK (Eleanor.Deansmith@dft.gov.uk [interim]) and European Commission (Vicente.Franco@ec.europa.eu) Secretariat: ETRTO (European Tyre and Rim Technical Organisation)
Reporting | To both working parties: GRPE and GRBP Adoption: GRBP
Web page | Task Force on Tyre Abrasion (TF TA) - Transport - Vehicle Regulations - UNECE Wiki ToRs: TF TA Terms of Reference
[DRAFT – TFTA discussion document]

## Slide 3: Task Force on Tyre Abrasion: facts and figures
  38th online meeting: 30th October 2025
  39th hybrid meeting (Brussels): 4th and 5th December
  40th online meeting: 18th December 2025
  41st online meeting: 13th January 2026
  42nd online meeting: 26th January 2026
  43rd online meeting: 2nd February 2026
  44th online meeting: 5th February 2026
  CPs: European Commission, France, China, Germany, India, Japan, Norway, Netherlands, South Korea, Spain, Switzerland, UK, USA, Canada, +Türkiye
  Other organisations: ADAC, AVL, ETRMA, ETRTO, HORIBA, IDIADA, ITMA, JAMA, JATMA, LINK, OICA, SMMT, TRAC, TÜV Nord, UBA, UniBW., USTMA, UTAC, VTI, TWMS, +fka + DEKRA
Meetings
Attendees ~80
[DRAFT – TFTA discussion document]

## Slide 4: Task Force on Tyre Abrasion: work completed
Adoption of methodologies | Test conditions and methods for C1 tyres: adopted  GRBP/2024/10 as amended by GRBP-79-12rev2 new supplement to UNR117.04  Adopted at WP.29 during its 193rd session in June 2024 ECE/TRANS/WP.29/2024/65 
C1 Testing | For C1: conduct an extensive market assessment test campaign to inform abrasion limit development – completed March 2025  For C1: conduct a correlation/validation study of the two test methods – completed March 2025 
C1 limits | Develop proposal for C1 tyre abrasion limits – Working document at GRBP in Sept 2025  - further refined by Informal document for the consideration of GRBP in February 2026 Develop an informal document addressing remaining issues (including the issue of method correlation) in working document and targeting adoption at GRBP in February 2026 
[DRAFT – TFTA discussion document]

## Slide 5: Documents for consideration by GRBP
  Two working documents submitted for the consideration of GRBP in September 2025:
  Draft UN Regulation on tyre abrasion (GRBP/2025/27): proposal for a new UN Regulation on the uniform provisions concerning the approval of tyres with regard to abrasion performance, following mandate given to TF TA at 81st GRBP session.
  Amendments to UNR 117 (GRBP/2025/28): proposal for a new supplement to UNR 117.04. The main aim of this proposal will be to remove the provisions related to tyre abrasion from UNR 117.
GRBP endorsement at the 82nd session was, however, not achieved. The lack of correlation [agreement] between the two candidate methods found for some of the tyres included in the market assessment raised technical questions about the soundness of using the same set of limits for both methods.
The TFTA terms of reference were updated at the 82nd session, with a mandate to work on a technical proposal to secure the inclusion of both candidate methods, for adoption by the 83rd session (see GRBP-82-34-Rev.1e)
[DRAFT – TFTA discussion document]

## Slide 6: Draft UN Regulation on tyre abrasion
Testing methods
[DRAFT – TFTA discussion document]

## Slide 7: Draft UN Regulation on tyre abrasion
Source: TA-37-6 (JASIC)
Testing methods – correlation study
[DRAFT – TFTA discussion document]

## Slide 8: Draft UN Regulation on tyre abrasion
Testing methods – market assessment data
Source: TA-32-10rev1 (RDW)
[DRAFT – TFTA discussion document]

## Slide 9: Focus of TF TA activities since GRBP 82
  Three workstreams contributing to the objective of the inclusion of both candidate methods (addressing the ‘inversion risk’):
  Data analysis (on the basis of historic TFTA measurements) to identify outliers and find plausible explanations for them. Output: targeted adjustments to both candidate methods aimed at reducing their uncertainty (and therefore the risk of ‘inversion’) [ETRTO/JASIC + EC (JRC)]
  Editorial improvements aiming at increasing clarity, overall quality of the draft UN Regulation
  Development of a new, dedicated Annex 4 (and accompanying guidance document) with legally binding criteria to establish the ‘equivalence’ of tyre abrasion measurement facilities (circuits or indoor drums) on the basis of a so-called inter-facilities equivalence exercise [EC with contributions by FR, DE, NL and UK experts]
      + Two alternative proposals from ETRTO and JASIC based on the concept of (temporary, conservative) ‘transfer functions’ applied to indoor drum facility results.
[DRAFT – TFTA discussion document]

## Slide 10: Documents for consideration by GRBP
  One informal document submitted by TF TA for the consideration of GRBP in February 2026 (workstreams 1 and 2):
  Amendments to Draft UN Regulation on tyre abrasion (GRBP/2025/27):
  [List of key modifications?]
[DRAFT – TFTA discussion document]

## Slide 11: Further changes introduced by [GRBP-83-xx]
Introduction of new definition of Road Legal Race tyres
Removal of square brackets to:
  confirm 3PMSF and non-3PMSF tyres cannot fall within the same tyre type
  confirm the abrasion margin applied at CoP should be the same as at the original type approval
Introduce small improvements to the drum and on-road methods to reduce areas of measurement uncertainty
Introduce provisions for the testing of mixed fitment vehicles tyres (i.e. where the candidate tyre cannot be fitted on all 4 positions on the candidate vehicle)
Drafting improvements to address errors and bring clarity, based on feedback
[DRAFT – TFTA discussion document]

## Slide 12: Documents for consideration by GRBP
  Informal documents submitted by TF TA stakeholders for the consideration of GRBP in February 2026 (workstream 3):
  To be considered as alternatives to address the issue of methods equivalence.
  Complete package for endorsement:
    Working document GRBP/2025/27
    Informal document submitted by TFTA (targeted method improvements, editorial improvements, compromise proposal on limits for C1 tyres)
    One of the alternatives to address the issue of methods equivalence
[DRAFT – TFTA discussion document]

## Slide 13: Draft UN Regulation on tyre abrasion
Introductory provisions
The proposed introductory provisions mirror the Euro 7 calendar for C1 tyres and support a two-stage approach.
Stage 1:
New approvals required no sooner than [30 June 2028].
All approvals required no sooner than [30 June 2030].
Stage 2:
New approvals required no sooner than [31 December 2032].
All approvals required no sooner than [31 December 2034].
Fitting of non-compliant C1 tyres on a vehicle in use:
Until [30 June 2032] for tyres manufactured prior to [30 June 2030].
Extended acceptance (transition from Stage 1 to Stage 2):
Approvals granted before the relevant cutoff can be extended until [31 December 2034].
Square brackets removed by informal document
Provision re-drafted in line with UNR 117 text and new paragraph 12.7. added to cover stage 2. Square brackets added around both paragraphs.
[DRAFT – TFTA discussion document]

## Slide 14: New UNR - what is still to be agreed?
  Inclusion (or not) of special use tyres from the scope
Special use tyres are currently included within the scope in the draft regulation, but with limits marked as “not defined” in square brackets:
There are two main points of view on how to handle special use tyres within the regulation:
  Exclude them from the scope of the regulation entirely
  Include them within the scope, but without a limit defined, to allow monitoring of their abrasion performance and potential inclusion of limits in future
[DRAFT – TFTA discussion document]

## Slide 15: New UNR - what is still to be agreed?
  Limit adjustments and margins
It was not possible to come to a consensus within TF TA on limit adjustments for stage 2, abrasion margins and CoP margins.
As some of these numbers relate not just to technical feasibility, but also to the desired environmental outcome of CPs, we have brought this to GRBP for discussion and agreement.
Figures within square brackets represent the co-chairs’ attempt to try to come to a proposal based on the various positions expressed within the task force. However, there remain a range of positions with regards to stringency of the limits.
Based on analysis presented by the co-chairs within TF TA, the proposed limits and margins would be expected to give rise to reductions in the mean abrasion rate of normal tyres of ~10% in the first stage and would result in ~30% rejection of tyre types based on those tested in the market assessment. Different figures have been presented by other participants of the task force, depending on the analysis method taken.
[DRAFT – TFTA discussion document]

## Slide 16: New UNR - what is still to be agreed?
  Stage 2 dates
  Whilst dates for stage 1 have been agreed within TF TA, there remain different views on the date of application of a stage 2
  As discussion of an appropriate date relates also to the accompanying stringency of the limits for stage 2, we have brought this to TF TA for discussion and agreement
[DRAFT – TFTA discussion document]

## Slide 17: Amendments to UNR 117 (GRBP/2025/28)
  Overview
Justification: establishes the separation of abrasion requirements into a new dedicated UN Regulation, making UNR 117 more focused and streamlined.
Scope change: removes tyre abrasion provisions from UNR 117, focusing it exclusively on rolling resistance, rolling noise, and wet grip.
Deletions: all definitions, requirements, and annexes related to abrasion rate, abrasion level, and abrasion index for C1 tyres are deleted from UNR 117.
Updated scope wording: clarifies that UNR 117 applies to abrasion only until the new dedicated UNR applies.
[DRAFT – TFTA discussion document]
No changes since GRBP 82

## Slide 18: Technical Progress: C2 Tyres
With finalisation of C1 close, the TF focus shifts to C2.
Activity (Sept 26- Feb 26):
  Launch of the C2 Market Assessment.
  Selection of ~50 representative C2 tyre models.
Method Adaptation (by June 2026): Testing is underway to verify if the C1 test methods (Vehicle convoy loads / Drum parameters) need adjustment for the heavier duty cycle of C2 vans.
Target: Test protocol and preliminary C2 data expected by September 2026.
[DRAFT – TFTA discussion document]

## Slide 19: Task Force on Tyre Abrasion: next steps
C1 tyres | Develop proposal for C1 tyre abrasion limits – Working document at GRBP in Sept 2025  Develop an informal document addressing remaining issues in working document and targeting adoption at GRBP February 2026  Assess the feasibility of rating and definition of the mileage of tyres -“relative mileage potential calculated performance”- ongoing - February Sept 2026  NEW – conduct further work on C1 methods improvement – working document at GRBP in Sept 2026 
C2 tyres | Assessment of C1 method suitability for C2 tyres – ongoing  Propose abrasion method(s) – working document at GRBP in Feb 2026 Develop proposal for C2 tyre abrasion limits – working document at GRBP in Sept 2027
C3 tyres | Propose abrasion method(s) – working document at GRBP in Feb 2027 Develop proposal for C3 tyre abrasion limits – working document at GRBP in Sept 2029
[DRAFT – TFTA discussion document]

## Slide 20: Thank you